## Slide 1: The DMM
Dr. Len Trombetta
ECE 2100

## Slide 2: Meter Resistance
All meters add a resistance to the circuit they are connected to. The resistance varies from one meter to the next. For the Agilent 34405A in the lab…
dc voltage measurement: Rm,V = 10[MW] on all scales
dc current measurement: Rm,A = 20[W] at 10[mA]
= 2[W] at 100[mA]
= 0.5[W] at 1[A]

## Slide 3: Meter Ranging
Manual ranging: choose your own full-scale range.
The 34405A is auto-ranging: it will automatically choose the full-scale best suited to the measurement you are making. But…
This button (along with the “shift” key) will return the DMM to the auto-ranging mode.
The secondary display shows the full-scale range.

## Slide 4: RMS Measurements
Another way to characterize the amplitude of a periodic waveform is the rms (root-mean-square) amplitude:
When set for ac voltage or current measurement, the Fluke automatically provides rms.
If v(t) is a sine or cosine (sinusoid), then