## Slide 1: Lab VI: Measuring Phase Shift
Dr. Len Trombetta
ECE 2100

## Slide 2: Time Constant Experiment
When you get to the lab, set up this circuit. Use a square-wave input to show the RC charge/discharge curves.
R = 47 [kW]
C = 0.022 [mF]

## Slide 3: Phase Shift Measurement
input
output
Now change the input signal to a sinusoid.
R = 47 [kW]
C = 0.022 [mF]

## Slide 4: The Idea…
This lab:
- Apply a sinusoid to find frequency domain properties.
- Measure phase difference between input and output.
Previous lab:
- Time domain measurement of an RC time constant.
- Apply a square wave to simulate the on/off action of a switch.

## Slide 5: Phasor Analysis
+
-
+
-
Vin
Vout
What happens to the output at very high and very low frequencies? Is there a phase change? Observe this on the scope.

## Slide 6: Phase Difference
Input and output are not in phase. We want to measure the phase difference .
We cannot measure the absolute phase of either waveform - we can only measure the phase difference.

## Slide 7: The Measurement
Because one full period (T) of the input (and output) sinusoids corresponds to 360 [deg], we have:
Dt
T
You can use the vertical cursors to help with this.

## Slide 8: What about the sign?
In this case, the output is shifted to the right: this is a negative phase shift (<0). We say that the output is lagging the input, because it is coming later in time.

## Slide 9: The Scope Probe
Problem: The oscilloscope input impedance distorts the measurement of vc(t), just as a voltmeter distorts the measurement of a dc voltage. The distortion is a function of frequency.
Cscope ~ 20 [pF]
Rscope ~ 1 [MW]
Thevenin Equivalent of the oscilloscope input

## Slide 10: The Solution…
We can compensate for this effect by using a “scope probe” between the circuit output and the scope.
+
-
vin
Circuit
Scope Probe
Scope
+
-
vmeas
Connect your circuit to the oscilloscope using the scope probe. What happens to the signal?

## Slide 11: Analysis
+
-
Vout
+
-
Vmeas
Rp, Cp: scope probe resistance and capacitance
Rs, Cs: oscilloscope input resistance and capacitance
Vout: circuit output; this is what we want to measure
Vmeas: input to scope; this is what shows up on the display

## Slide 12: Analysis
+
-
Vmeas
Note that R in parallel with 1/jwC is:
Now, let’s design a scope probe that will be useful…
+
-
Vout
circuit

## Slide 13
If we design the probe so that CpRp = CsRs, then…
If we also make Rp = 9 Rs and Cp = 1/9 Cs, then CsRs = CpRp and
From the last slide:
What have we accomplished?
+
-
Vmeas
+
-
Vout
circuit

## Slide 14
Making a probe like this is useful because…
(i) The error in vmeas(t) does not depend on frequency, whereas it did without the scope probe.
(ii) The input impedance of the scope (looking from the circuit output) is…
=10
…which is 10 X higher than it was without the scope probe.
+
-
Vmeas
+
-
Vout
circuit

## Slide 15: Bottom Line
+
-
Vout
+
-
Vmeas
We have increased the input impedance of the scope by 10X. This means less distortion in the measurement. It’s like having a voltmeter with 10X more resistance.
We have removed frequency dependence in the error, i.e., we no longer have a frequency-dependent distortion in the amplitude and phase measurements.
We have paid a price for this: our signal has been reduced by a factor of 10X. In other words, our measurement is 10X less sensitive.

## Slide 16: Scope Probe Calibration
Calibration: Connect the probe to the calibration port, and adjust the screw on the side of the probe until the square wave is “clean”. Do this with the plastic screwdriver in your lab kit.
Probe gets connected here
Scope input capacitance can vary from scope to scope.

## Slide 17: The “Probe” Setting
Probe button cycles among allowable probe ratios. Choose 10:1.
This changes the vertical scale indicator, so that you don’t have to do the 10X multiplication to get the right amplitude.
vertical scale indicator changes according to probe ratio.
500 mV/
Choose the input you want to adjust.

## Slide 18: Summary
If the scope probe is properly adjusted, it compensates for the input impedance of the oscilloscope. It removes the frequency dependence in the measurement error, and reduces the error by increasing the input impedance of the scope by 10X. But it also reduces the sensitivity of the measurement by 10X. Usually, this is a good tradeoff.

## Slide 19: RMS Measurements
Another way to characterize the amplitude of a periodic waveform is the rms (root-mean-square) amplitude:
When set to measure ac voltage or current, the Agilent automatically displays rms.
If v(t) is a sine or cosine (sinusoid), then