Practice Examination Questions With Solutions

Module 3 – Problem 2

Filename:  PEQWS_Mod03_Prob02.doc

Note:  Units in problem are enclosed in square brackets.

Time Allowed:  25 Minutes

Problem Statement:

Use the mesh-current method to write a complete set of independent equations that could be used to solve this circuit.  Do not attempt to solve the equations.  Do not attempt to simplify the circuit.

Problem Solution:

The problem statement was:

Use the mesh-current method to write a complete set of independent equations that could be used to solve this circuit.  Do not attempt to solve the equations.  Do not attempt to simplify the circuit.

The first step in the solution is to identify the meshes, and define the mesh currents.  This is done in the circuit schematic that follows.  The mesh currents are marked in red.

Now we need to write the Mesh-Current Method Equations.  There will be six equations plus two more for the dependent source variables iX and vY.  We will take them alphabetically.  For mesh A, we have a current source as a part of only that one mesh.  We can use the current source to write

For mesh B, we can write

Mesh C is similar; there is a voltage source that will be one of the terms in the equation.  We have

Now, for mesh D, there is a current source, that is a part of two meshes.  We need to write a supermesh equation and a constraint equation using the current source.  The supermesh is drawn on the circuit with a dashed line.

The supermesh equation is

and the constraint equation is

Finally, we need an equation for the F mesh.  We can write

Now, we have to write equations for the dependent sources.  The current iX is the current between two meshes, and we can write

Finally, we need to write an equation for vY.  This is the voltage across a current source, and therefore depends on the things that the current source is connected to.  We can pick a closed path and write a KVL equation.  Probably the most simple and easy closed path to use is mesh D.  Note that we have not yet written KVL for mesh D because of the supermesh.  We can write

This is 8 equations in 8 unknowns, and completes the solution that was requested.

Note 1:  For clarity in showing this solution, and how it unfolds, we have redrawn the circuit a couple of times.  In solving this problem on an examination, we would not redraw each time, but rather make marks on the original circuit.  In addition, we would not include all of the text that is present here.  With this, it should be possible to complete the problem in the allotted time.

Note 2:  Some students have difficulty trying to determine whether their solution was a valid one, particularly if they have taken a slightly different approach such as picking different directions for the mesh currents.  While it is not requested in this problem, a numerical solution for iX and vY is given here.  If you are in doubt about the validity of your solution, solve for these quantities, and compare with this solution.  If your solution is significantly different, then something must be wrong.

Our equations were:

Now, we are going to substitute in the values that were given in the circuit.  We get the following system of equations:

Now, we will substitute these equations into MathCAD.  The solution is given in a MathCAD file called PEQWS_Mod03_Prob02_Soln.mcd.  The results are given here:

iA = 0.3[A]

iB = 0.01034[A]

iC = 0.37895[A]

iD = 247.491[A]

iE = -0.07549[A]

iF = 0.05365[A]

iX = -0.3787[A]

vY = -8.1672[mV]

While the mesh current values depend on how you define these variables, iX  and vY should be the same with any approach.  You can use these answers to check your work.

Problem adapted from ECE 2300, Exam 1, Problem 5, Fall 1998, Department of Electrical and Computer Engineering, Cullen College of Engineering, University of Houston.