## Slide 1: ECE 2201 Circuit Analysis
Lecture Set #3
Equivalent Circuits
Series, Parallel, Delta-to-Wye,
Voltage Divider and
Current Divider Rules
Version 28
Dr. Dave Shattuck
Associate Professor, ECE Dept.

## Slide 2: Series, Parallel, and other Resistance Equivalent Circuits

## Slide 3: Overview Series, Parallel, and other Resistance Equivalent Circuits
In this lecture set, we will cover the following topics:
Equivalent circuits
Definitions of series and parallel
Series and parallel resistors
Delta-to-wye transformations
Notes: You can click on the links to jump to the subject that you want to learn about now.

## Slide 4: Equivalent Circuits – The Concept
Equivalent circuits are ways of looking at or solving circuits. The idea is that if we can make a circuit simpler, we can make it easier to solve, and easier to understand.
The key is to use equivalent circuits properly. After defining equivalent circuits, we will start with the simplest equivalent circuits, series and parallel combinations of resistors.

## Slide 5: Equivalent Circuits: A Definition
Imagine that we have a circuit, and a portion of the circuit can be identified, made up of one or more parts. That portion can be replaced with another set of components, if we do it properly. We call these portions equivalent circuits.
Two circuits are considered to be equivalent if they behave the same with respect to the things to which they are connected. One can replace one circuit with another circuit, and everything else cannot tell the difference.
We will use an analogy for equivalent circuits here. This analogy is that of jigsaw puzzle pieces. The idea is that two different jigsaw puzzle pieces with the same shape can be thought of as equivalent, even though they are different. The rest of the puzzle does not “notice” a difference. This is analogous to the case with equivalent circuits.

## Slide 6: Equivalent Circuits: A Definition Considered
Two circuits are considered to be equivalent if they behave the same with respect to the things to which they are connected. One can replace one circuit with another circuit, and everything else cannot tell the difference.
In this jigsaw puzzle, the rest of the puzzle cannot tell whether the yellow or the green piece is inserted. This is analogous to what happens with equivalent circuits.

## Slide 7: Equivalent Circuits: Defined in Terms of Terminal Properties
Two circuits are considered to be equivalent if they behave the same with respect to the things to which they are connected. One can replace one circuit with another circuit, and everything else cannot tell the difference.
We often talk about equivalent circuits as being equivalent in terms of terminal properties. The properties (voltage, current, power) within the circuit may be different.

## Slide 8: Equivalent Circuits: A Caution
Two circuits are considered to be equivalent if they behave the same with respect to the things to which they are connected. The properties (voltage, current, power) within the circuit may be different.
It is important to keep this concept in mind. A common error for beginners is to assume that voltages or currents within a pair of equivalent circuits are equal. They may not be. These voltages and currents are only required to be equal if they can be identified outside the equivalent circuit. This will become clearer as we see the examples that follow in the other parts of this lecture set.
Go back to Overview slide.

## Slide 9: Series Combination: A Structural Definition
A Definition:
Two parts of a circuit are in series if the same current flows through both of them.
Note: It must be more than just the same value of current in the two parts. The same exact charge carriers need to go through one, and then the other, part of the circuit.

## Slide 10: Series Combination: Hydraulic Version of the Definition
A Definition:
Two parts of a circuit are in series if the same current flows through both of them.
A hydraulic analogy: Two water pipes are in series if every drop of water that goes through one pipe, then goes through the other pipe.

## Slide 11: Series Combination: A Hydraulic Example
A Definition:
Two parts of a circuit are in series if the same current flows through both of them.
A hydraulic analogy: Two water pipes are in series if every drop of water that goes through one pipe, then goes through the other pipe.
In this picture, the green part and the blue part of the pipes are in series, but the blue part and the orange part are not in series.

## Slide 12: Parallel Combination: A Structural Definition
A Definition:
Two parts of a circuit are in parallel if the same voltage is across both of them.
Note: It must be more than just the same value of the voltage in the two parts. The same exact voltage must be across each part of the circuit. In other words, the two end points must be connected together.

## Slide 13: Parallel Combination: Hydraulic Version of the Definition
A Definition:
Two parts of a circuit are in parallel if the same voltage is across both of them.
A hydraulic analogy: Two water pipes are in parallel the two pipes have their ends connected together. The analogy here is between voltage and height. The difference between the height of two ends of a pipe, must be the same as that between the two ends of another pipe, if the two pipes are connected together.

## Slide 14: Parallel Combination: A Hydraulic Example
A Definition:
Two parts of a circuit are in parallel if the same voltage is across both of them.
A hydraulic analogy: Two water pipes are in parallel if the two pipes have their ends connected together. The Pipe Section 1 (in red) and Pipe Section 2 (in green) in this set of water pipes are in parallel. Their ends are connected together.
Go back to Overview slide.

## Slide 15: Series Resistors Equivalent Circuits
Two series resistors, R1 and R2, can be replaced with an equivalent circuit with a single resistor REQ, as long as

## Slide 16: More than 2 Series Resistors
This rule can be extended to more than two series resistors. In this case, for N series resistors, we have

## Slide 17: Series Resistors Equivalent Circuits: A Reminder
Two series resistors, R1 and R2, can be replaced with an equivalent circuit with a single resistor REQ, as long as
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.)

## Slide 18: Series Resistors Equivalent Circuits: Another Reminder
Resistors R1 and R2 can be replaced with a single resistor REQ, as long as
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.) The voltage vR2 does not exist in the right hand equivalent.

## Slide 19: The Resistors Must be in Series
Resistors R1 and R2 can be replaced with a single resistor REQ, as long as
Remember also that these two equivalent circuits are equivalent only when R1 and R2 are in series. If there is something connected to the node between them, and it carries current, (iX ¹ 0) then this does not work.
R1 and R2 are not in series here.

## Slide 20: Parallel Resistors Equivalent Circuits
Two parallel resistors, R1 and R2, can be replaced with an equivalent circuit with a single resistor REQ, as long as

## Slide 21: More than 2 Parallel Resistors
This rule can be extended to more than two parallel resistors. In this case, for N parallel resistors, we have

## Slide 22: Parallel Resistors Notation
We have a special notation for this operation. When two things, Thing1 and Thing2, are in parallel, we write Thing1||Thing2 to indicate this. So, we can say that

## Slide 23: Parallel Resistor Rule for 2 Resistors
When there are only two resistors, then you can perform the algebra, and find that
This is called the product-over-sum rule for parallel resistors. Remember that the product-over-sum rule only works for two resistors, not for three or more.

## Slide 24: Parallel Resistors Equivalent Circuits: A Reminder
Two parallel resistors, R1 and R2, can be replaced with a single resistor REQ, as long as
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.)

## Slide 25: Parallel Resistors Equivalent Circuits: Another Reminder
Two parallel resistors, R1 and R2, can be replaced with REQ, as long as
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.) The current iR2 does not exist in the right hand equivalent.

## Slide 26: The Resistors Must be in Parallel
Two parallel resistors, R1 and R2, can be replaced with REQ, as long as
Remember also that these two equivalent circuits are equivalent only when R1 and R2 are in parallel. If the two terminals of the resistors are not connected together, then this does not work.
R1 and R2 are not in parallel here.
Go back to Overview slide.

## Slide 27: Why are we doing this? Isn’t all this obvious?
This is a good question.
Indeed, most students come to the study of engineering circuit analysis with a little background in circuits. Among the things that they believe that they do know is the concept of series and parallel.
However, once complicated circuits are encountered, the simple rules that some students have used to identify series and parallel combinations can fail. We need rules that will always work.
Go back to Overview slide.

## Slide 28: Why It Isn’t Obvious
The problem for students in many cases is that they identify series and parallel by the orientation and position of the resistors, and not by the way they are connected.
In the case of parallel resistors, the resistors do not have to be drawn “parallel”, that is, along lines with the same slope. The angle does not matter. Only the nature of the connection matters.
In the case of series resistors, they do not have to be drawn along a single line. The alignment does not matter. Only the nature of the connection matters.
Go back to Overview slide.

## Slide 29: Examples (Parallel)
Some examples are given here.

## Slide 30: Examples (Series)
Some more examples are given here.
Go back to Overview slide.

## Slide 31: How do we use equivalent circuits?
This is yet another good question.
We will often use these equivalents to simplify circuits, making them easier to solve. Sometimes, equivalent circuits are used in other ways. In some cases, one equivalent circuit is not simpler than another; rather one of them fits the needs of the particular circuit better. The delta-to-wye transformations that we cover next fit in this category. In yet other cases, we will have equivalent circuits for things that we would not otherwise be able to solve. For example, we will have equivalent circuits for devices such as diodes and transistors, that allow us to solve circuits that include these devices.
The key point is this: Equivalent circuits are used throughout circuits and electronics. We need to use them correctly. Equivalent circuits are equivalent only with respect to the circuit outside them.
Go back to Overview slide.

## Slide 32: Delta-to-Wye Transformations
The transformations, or equivalent circuits, that we cover next are called delta-to-wye, or wye-to-delta transformations. They are also sometimes called pi-to-tee or tee-to-pi transformations. For these lecture sets, we will call them the delta-to-wye transformations.
These are equivalent circuit pairs. They apply for parts of circuits that have three terminals. Each version of the equivalent circuit has three resistors.
Many courses do not cover these particular equivalent circuits at this point, delaying coverage until they are specifically needed during the discussion of three phase circuits. However, they are an excellent example of equivalent circuits, and can be used in some cases to solve circuits more easily.

## Slide 33: Delta-to-Wye Transformations
Three resistors in a part of a circuit with three terminals can be replaced with another version, also with three resistors. The two versions are shown here. Note that none of these resistors is in series with any other resistor, nor in parallel with any other resistor. The three terminals in this example are labeled A, B, and C.

## Slide 34: Delta-to-Wye Transformations (Notes on Names)
The version on the left hand side is called the delta connection, for the Greek letter D. The version on the right hand side is called the wye connection, for the letter Y. The delta connection is also called the pi (p) connection, and the wye interconnection is also called the tee (T) connection. All these names come from the shapes of the drawings.

## Slide 35: Delta-to-Wye Transformations (More Notes)
When we go from the delta connection (on the left) to the wye connection (on the right), we call this the delta-to-wye transformation. Going in the other direction is called the wye-to-delta transformation. One can go in either direction, as needed. These are equivalent circuits.

## Slide 36: Delta-to-Wye Transformation Equations
When we perform the delta-to-wye transformation (going from left to right) we use the equations given below.

## Slide 37: Wye-to-Delta Transformation Equations
When we perform the wye-to-delta transformation (going from right to left) we use the equations given below.

## Slide 38: Deriving the Equations
While these equivalent circuits are useful, perhaps the most important insight is gained from asking where these useful equations come from. How were these equations derived?
The answer is that they were derived using the fundamental rule for equivalent circuits. These two equivalent circuits have to behave the same way no matter what circuit is connected to them. So, we can choose specific circuits to connect to the equivalents. We make the derivation by solving for equivalent resistances, using our series and parallel rules, under different, specific conditions.

## Slide 39: Equation 1
We can calculate the equivalent resistance between terminals A and B, when C is not connected anywhere. The two cases are shown below. This is the same as connecting an ohmmeter, which measures resistance, between terminals A and B, while terminal C is left disconnected.

## Slide 40: Equations 2 and 3
So, the equation that results from the first situation is
We can make this measurement two other ways, and get two more equations. Specifically, we can measure the resistance between A and C, with B left open, and we can measure the resistance between B and C, with A left open.

## Slide 41: All Three Equations
The three equations we can obtain are
This is all that we need. These three equations can be manipulated algebraically to obtain either the set of equations for the delta-to-wye transformation (by solving for R1, R2 , and R3), or the set of equations for the wye-to-delta transformation (by solving for RA, RB , and RC).

## Slide 42: Why Are Delta-to-Wye Transformations Needed?
This is a good question. In fact, it should be pointed out that these transformations are not necessary. Rather, they are like many other aspects of circuit analysis in that they allow us to solve circuits more quickly and more easily. They are used in cases where the resistors are neither in series nor parallel, so to simplify the circuit requires something more.
One key in applying these equivalents is to get the proper resistors in the proper place in the equivalents and equations. We recommend that you name the terminals each time, on the circuit diagrams, to help you get these things in the right places.
Go back to Overview slide.

## Slide 43: Example Problem #1

## Slide 44: Example Problem #2

## Slide 45: Example Problem #3

## Slide 46: Example Problem #4

## Slide 47: Example Problem #5
Find the equivalent resistance as seen from terminals A and B.

## Slide 48: Voltage Divider and Current Divider Rules

## Slide 49: Overview Series, Parallel, and other Resistance Equivalent Circuits
In this part, we will cover the following topics:
Voltage Divider Rule
Current Divider Rule
Signs in the Voltage Divider Rule
Signs in the Current Divider Rule
Notes: You can click on the links to jump to the subject that you want to learn about now.

## Slide 50: Voltage Divider Rule – Our First Circuit Analysis Tool
The Voltage Divider Rule (VDR) is the first of a long list of tools that we are going to develop to make circuit analysis quicker and easier. The idea is this: if the same situation occurs often, we can derive the solution once, and use it whenever it applies. As with any tools, the keys are:
Recognizing when the tool works and when it doesn’t work.
Using the tool properly.

## Slide 51: Voltage Divider Rule – Setting up the Derivation
The Voltage Divider Rule involves the voltages across series resistors. Let’s take the case where we have two resistors in series. Assume for the moment that the voltage across these two resistors, vTOTAL, is known. Assume that we want the voltage across one of the resistors, shown here as vR1. Let’s find it.

## Slide 52: Voltage Divider Rule – Derivation Step 1
The current through both of these resistors is the same, since the resistors are in series. The current, iX, is

## Slide 53: Voltage Divider Rule – Derivation Step 2
The current through resistor R1 is the same current. The current, iX, is

## Slide 54: Voltage Divider Rule – Derivation Step 3
These are two expressions for the same current, so they must be equal to each other. Therefore, we can write

## Slide 55: The Voltage Divider Rule
This is the expression we wanted. We call this the Voltage Divider Rule (VDR).

## Slide 56: Voltage Divider Rule – For Each Resistor
This is easy enough to remember that most people just memorize it. Remember that it only works for resistors that are in series. Of course, there is a similar rule for the other resistor. For the voltage across one resistor, we put that resistor value in the numerator.
Go back to Overview slide.

## Slide 57: Current Divider Rule – Our Second Circuit Analysis Tool
The Current Divider Rule (CDR) is the second of a long list of tools that we are going to develop to make circuit analysis quicker and easier. Again, if the same situation occurs often, we can derive the solution once, and use it whenever it applies. As with any tools, the keys are:
Recognizing when the tool works and when it doesn’t work.
Using the tool properly.

## Slide 58: Current Divider Rule – Setting up the Derivation
The Current Divider Rule involves the currents through parallel resistors. Let’s take the case where we have two resistors in parallel. Assume for the moment that the current feeding these two resistors, iTOTAL, is known. Assume that we want the current through one of the resistors, shown here as iR1. Let’s find it.

## Slide 59: Current Divider Rule – Derivation Step 1
The voltage across both of these resistors is the same, since the resistors are in parallel. The voltage, vX, is the current multiplied by the equivalent parallel resistance,

## Slide 60: Current Divider Rule – Derivation Step 2
The voltage across resistor R1 is the same voltage, vX. The voltage, vX, is

## Slide 61: Current Divider Rule – Derivation Step 3
These are two expressions for the same voltage, so they must be equal to each other. Therefore, we can write

## Slide 62: The Current Divider Rule
This is the expression we wanted. We call this the Current Divider Rule (CDR).

## Slide 63: Current Divider Rule – For Each Resistor
Most people just memorize this. Remember that it only works for resistors that are in parallel. Of course, there is a similar rule for the other resistor. For the current through one resistor, we put the opposite resistor value in the numerator.
Go back to Overview slide.

## Slide 64: Signs in the Voltage Divider Rule
As in most every equation we write, we need to be careful about the sign in the Voltage Divider Rule (VDR). Notice that when we wrote this expression, there is a positive sign. This is because the voltage vTOTAL is in the same relative polarity as vR1.

## Slide 65: Negative Signs in the Voltage Divider Rule
If, instead, we had solved for vQ, we would need to change the sign in the equation. This is because the voltage vTOTAL is in the opposite relative polarity from vQ.

## Slide 66: Check for Signs in the Voltage Divider Rule
The rule for proper use of this tool, then, is to check the relative polarity of the voltage across the series resistors, and the voltage across one of the resistors.
Go back to Overview slide.

## Slide 67: Signs in the Current Divider Rule
As in most every equation we write, we need to be careful about the sign in the Current Divider Rule (CDR). Notice that when we wrote this expression, there is a positive sign. This is because the current iTOTAL is in the same relative polarity as iR1.

## Slide 68: Negative Signs in the Current Divider Rule
If, instead, we had solved for iQ, we would need to change the sign in the equation. This is because the current iTOTAL is in the opposite relative polarity from iQ.

## Slide 69: Check for Signs in the Current Divider Rule
The rule for proper use of this tool, then, is to check the relative polarity of the current through the parallel resistors, and the current through one of the resistors.
Go back to Overview slide.

## Slide 70: Do We Always Need to Worry About Signs?
Unfortunately, the answer to this question is: YES! There is almost always a question of what the sign should be in a given circuits equation. The key is to learn how to get the sign right every time. As mentioned earlier, this is the key purpose in introducing reference polarities.
Go back to Overview slide.

## Slide 71: Example Problem #6