Name:  _____________________________ (please print)

Signature: __________________________

ECE 2300  Circuit Analysis

Quiz #1A

February 15, 1999

DO NOT OPEN THIS QUIZ BOOKLET UNTIL YOU ARE TOLD TO BEGIN

1.  This quiz is open book and open notes.  Any calculator may be used.

2.  You will have 30 minutes to complete this quiz.

3.  Show all work on these pages.  Show all work necessary to complete the problem.  A solution without the work shown will receive no credit.

4.  Use appropriate notation.

5.  Show units in all answers and in all major intermediate results.  Units in the exam questions will be enclosed in square brackets.

6.  Do not use red ink.  Do not use red pencil.

______________/20

Room for extra work

A device can be modeled by an ideal voltage source in series with a resistor.  When this device is connected one at a time to current sources of different values, the voltage vD, that result are given in the table.  The connection of the current source to the device is shown in Fig. (a) below.  Then, the device is connected to a 10[] resistor as shown in Fig. (b).  Find vD for this resistor value.

| it [A] | vD [V] |
| --- | --- |
| 0.5 | 9.5 |
| 1 | 7 |
| 1.5 | 4.5 |
| 2 | 2 |

Solution:  Quiz 1A, ECE 2300, February 15, 1999

A device can be modeled by an ideal voltage source in series with a resistor.  When this device is connected one at a time to current sources of different values, the voltage vD, that result are given in the table.  The connection of the current source to the device is shown in Fig. (a) below.  Then, the device is connected to a 10[] resistor as shown in Fig. (b).  Find vD for this resistor value.

| it [A] | vD [V] |
| --- | --- |
| 0.5 | 9.5 |
| 1 | 7 |
| 1.5 | 4.5 |
| 2 | 2 |

Solution:

Draw the circuit twice, using 2 different values from the table.  Using this, we can solve for the values of the voltage source and resistor for the model of the device.  Then, we connect the resistor to this model to solve the problem.