## Slide 1
ECE 3317
Applied Electromagnetic Waves
Prof. David R. Jackson
Fall 2023
Notes 14 Transmission Lines (Discontinuity Effects)

## Slide 2
Discontinuity Effects
Two effects not predicted by transmission line theory:
Reflections from discontinuities
Radiation from discontinuities
Any practical system will have discontinuities.

## Slide 3
The discussion here will mainly focus on two common types of transmission lines, coaxial cable and twin lead, but the discussion is general and applies to other similar types of lines.
Coaxial cable
Twin lead
Discontinuity Effects (cont.)

## Slide 4
Coaxial Cable
The coaxial cable is a perfectly shielded system – there is never any radiation.
The fields are confined to the region between the two conductors.
Assumption: The conductor thickness is large compared to a skin depth.
The coax does not interfere with anything, nor pick up interference from anything.

## Slide 5
Coaxial Cable (cont.)
Reflections can still occur at bends.
It is good to keep the radius of curvature of the bend large compared with the diameter of the coax.
Bend
Incident wave
Reflected
Transmitted wave
Coax

## Slide 6
Twin Lead
The twin lead is an open type of transmission line – the fields extend out to infinity.
The fields may cause interference with nearby objects (or cause the twin lead to pick up interference).
+
-

## Slide 7
An infinite straight twin lead transmission line will not radiate, even though the fields extend to infinity.
A transmission line wave represents an exact solution to Maxwell’s equations on an infinite straight line.
(This wave has no attenuation on a lossless line, and hence no radiation.)
Twin Lead (cont.)
Incident
Twin Lead

## Slide 8
Twin Lead (cont.)
Incident wave
Bend
Reflected wave
Radiation
Twin Lead
A discontinuity on the twin lead will cause radiation and reflections.
Note:
Radiation effects increase as the frequency increases.
Example: Bend

## Slide 9
A discontinuity on the twin lead will cause radiation and reflections.
Example: Obstacle (e.g., a pipe)
Twin Lead (cont.)
Incident wave
Pipe
Reflected wave
Radiation
Twin Lead
Note:
Radiation effects increase as the frequency increases.

## Slide 10
Transmission line theory predicts no reflections (same Z0) – but there will be reflections at high frequency, along with radiation.
Twin Lead (cont.)
A discontinuity on the twin lead will cause radiation and reflections.
Example: Change in dimensions
Radiation
Twin Lead
Incident wave
Reflected wave

## Slide 11
To reduce reflection and radiation effects at discontinuities:
Reduce the separation distance h (keep h << ).
Twist the lines (twisted pair).
CAT 5 cable
(twisted pair)
Twin Lead (cont.)
Insulating jacket

## Slide 12
Microstrip
At discontinuities, the following effects occur at high frequency:
Reflections
Radiation
Excitation of a surface wave
Microstrip line
Quarter-wave transformer
Microstrip line “extension”
Device
Incident wave
Reflected wave
Surface wave
Radiation
None of these effects are predicted by transmission-line theory.