## Slide 1
Notes 19
Waveguiding Structures
ECE 3317
Applied Electromagnetic Waves
Prof. David R. Jackson
Fall 2023

## Slide 2
Waveguiding Structures
A waveguiding structure is one that carries a signal (or power) from one point to another without having energy escape.
There are three common types:
Transmission lines
Fiber-optic guides
Waveguides (hollow pipes)
An alternative to a waveguiding system is a wireless system using antennas.

## Slide 3
Waveguiding Structures (cont.)
Transmission lines
Fiber-optic guides
Waveguides (hollow pipes)
Three common types of waveguiding structures:

## Slide 4
Transmission lines
Lossless:
Has two conductors running parallel
Can propagate a signal at any frequency (in theory)
Becomes lossy at high frequency
Can handle low or moderate amounts of power
Has signal distortion due to loss
May or may not be immune to interference
Does not have Ez or Hz components of the fields (TEMz)
Properties
(nonmagnetic filling)

## Slide 5
Fiber-Optic Guide
Properties
Has a single dielectric rod
Can propagate a signal at any frequency (in theory)
Can be made very low loss (no metal + low-loss glass)
Has minimal signal distortion
Very immune to interference
Not suitable for high power
Has both Ez and Hz components of the fields (“hybrid mode”)

## Slide 6
Fiber-Optic Guide (cont.)
Two types of fiber-optic guides:
1) Single-mode fiber
2) Multi-mode fiber
Carries a single mode. Requires the fiber diameter to be small relative to a wavelength. This is the lowest loss type of fiber.
Has a fiber diameter that is large relative to a wavelength. It operates on the principle of total internal reflection (critical angle effect).

## Slide 7
Multi-Mode Fiber
http://en.wikipedia.org/wiki/Optical_fiber

## Slide 8
Multi-Mode Fiber (cont.)
At left end of rod (input), Snell’s law gives us:
There is a maximum angle max at which the beam can be incident from outside the rod.
Assume cladding is air
At the critical angle

## Slide 9
Waveguide
Has a single hollow metal pipe
Can propagate a signal only at high frequency: f > fc
The width a must be at least one-half of a wavelength d
Has signal distortion, even in the lossless case
Immune to interference
Can handle large amounts of power
Has low loss (compared with a transmission line)
Has either Ez or Hz component of the fields (TMz or TEz)
Properties
https://en.wikipedia.org/wiki/Waveguide_(radio_frequency)
Inside microwave oven
Rectangular waveguide
Note: The pipe may be filled with a material having r.

## Slide 10
Waveguide (cont.)
Coax
Waveguide
The coax has higher loss and is more susceptible to dielectric breakdown (can handle less power).
Waveguide vs. Coax
The electric field and surface current of the coax are concentrated near the narrow inner conductor (very strong electric field and current density there). This gives more loss and also more susceptibility to dielectric breakdown.
The waveguide is usually hollow, and thus has no dielectric loss.

## Slide 11
Waveguide (cont.)
Wavenumber inside a waveguide (derived later):
(wavenumber of material inside waveguide)
(propagation)
(evanescent decay)
Cutoff frequency fc for a lossless waveguide (k is real):
where

## Slide 12
Field Expressions for a Guided Wave
All six field components of a guided wave can be expressed in terms of the two fundamental field components Ez and Hz.
Assumption:
(This is the definition of a guided wave.)
A proof of this “statement” is given in Appendix A.
Statement:
"Guided-wave theorem"
See the table on the next slide for the results.

## Slide 13
Summary of Fields
Field Expressions of a Guided Wave (cont.)

## Slide 14
TEMz Wave
To avoid having a completely zero field (see table on previous slide):
Assume a TEMz wave:
TEMz
Hence,

## Slide 15
TEMz Wave (cont.)
Examples of TEMz waves:
In each case the fields do not have a z component !
A wave on a transmission line*
A plane wave








Coax
Plane wave
* Exactly true if there is no conductor loss.

## Slide 16
Relation Between E and H for any TEMz Mode:
TEMz Wave (cont.)
The electric and magnetic fields of a TEMz wave are perpendicular to each other, and the amplitudes of them are related by .
A proof is given in Appendix B.
(intrinsic impedance of filling material)

## Slide 17
Waveguide Modes
In a waveguide, the fields cannot be TEMz.

## Slide 18
Waveguide Modes (cont.)
In a waveguide (hollow pipe of metal), there are two types of modes:
TMz: Hz = 0, Ez  0
TEz: Ez = 0, Hz  0
Each type of mode can exist independently.

## Slide 19
Appendix A
(illustrated for Ey)
or
Now solve for Hx :
Proof of Guided Wave Theorem

## Slide 20
Substituting this into the equation for Ey yields the result
Next, multiply by
Appendix A (cont.)

## Slide 21
Solving for Ey, we have:
This gives us
The other three components Ex, Hx, Hy may be found similarly.
Combining terms,
Appendix A (cont.)

## Slide 22
Faraday's Law:
Take the x component of both sides:
Assume that the field varies as
Hence,
Therefore, we have
Appendix B
Relation Between E and H for any TEMz Mode

## Slide 23
Now take the y component of both sides:
Hence,
Therefore, we have
Hence,
Appendix B (cont.)

## Slide 24
These two equations may be written as a single vector equation:
The electric and magnetic fields of a TEMz wave are perpendicular to each other, and the amplitudes of them are related by .
Summary:
Appendix B (cont.)