## Slide 1
Notes 21
Introduction to Antennas
ECE 3317
Applied Electromagnetic Waves
Prof. David R. Jackson
Fall 2023

## Slide 2
Introduction to Antennas
An antenna is a device that is used to transmit and/or receive an electromagnetic wave.
Examples:
Cell-phone antenna (transmit and receive)
TV antenna in your home (receive only)
Wireless LAN antenna (transmit and receive)
FM radio antenna (receive only)
Satellite dish antenna (receive only)
AM radio broadcast tower (transmit only)
GPS position location unit (receive only)
The antenna itself can always transmit or receive, but it may be used for only one of these functions in a particular application.

## Slide 3
For communication over long distances, to have lower loss (see next slide)
Where waveguiding systems (e.g., transmission lines such as coaxial cable or fiber optic cable) are impractical or inconvenient
When it is desired to communicate with many users at once
Antennas are often used for a variety of reasons:
Antenna
Advantages of Antennas
Fiber optic cable
Twisted pair (CAT 5 cable)
Coax

## Slide 4
Wireless systems using antennas will always be better (lower loss) than wired (waveguiding) systems for large distances.
Power loss from waveguiding system:
Power loss from antenna broadcast:
(always better for large r)
( = attenuation constant)
Antennas vs. Waveguiding Systems
A
B
Antenna
Waveguiding system

## Slide 5
Antennas vs. Waveguiding Systems (cont.)
r [meters]
Comparison of Two Functions

## Slide 6
Comparison of Waveguiding Systems with Wireless Systems
Distance | Coax | Fiber | Wireless | Wireless
1 m | 0.4 | 0.0003 | 28.2 | -
10 m | 4 | 0.003 | 48.2 | -
100 m | 40 | 0.03 | 68.2 | -
1 km | 400 | 0.3 | 88.2 | 39.3
10 km | 4000 | 3 | 108.2 | 59.3
100 km | - | 30 | 128.2 | 79.3
1000 km | - | 300 | 148.2 | 99.3
10,000 km | - | 3000 | 168.2 | 119.3
100,000 km | - | - | 188.2 | 139.3
1,000,000 km | - | - | 208.2 | 159.3
10,000,000 km | - | - | 228.2 | 179.3
100,000,000 km | - | - | 248.2 | 199.3
RG59
1 GHz
Single Mode
Two Dipoles
34m Dish+Dipole
Attenuation in dB

## Slide 7
Main properties of antennas:
Radiation pattern
Beamwidth and directivity (how directional the beam is)
Sidelobe level
Efficiency (power radiated relative to total input power)
Polarization (linear, CP)
Input Impedance
Bandwidth (the useable frequency range)
Main Properties of Antennas

## Slide 8
Reflector (dish) antenna
Very high bandwidth
High directivity (directivity is determined by the size / wavelength)
Linear or CP polarization (depending on how it is fed)
Works by focusing the incoming wave to a collection (feed) point
Ideally, the dish is parabolic in shape.
Types of Antennas

## Slide 9
Dipole Wire Antenna
Very simple
Moderate bandwidth
Low directivity
Omnidirectional in azimuth
Most commonly fed by a “twin-lead” transmission line
Linear polarization (E , assuming wire is along z axis)
The antenna is resonant when the length is about one-half free-space wavelength
Current
(resonant)
Types of Antennas (cont.)

## Slide 10
Dipole Wire Antenna (cont.)
Types of Antennas (cont.)
“Bow-tie” variation (for higher bandwidth)
“Rabbit ears”

## Slide 11
Folded Dipole Antenna
The folded dipole is a variation of the dipole antenna. It has an input impedance that is 4 times higher than that of the regular dipole antenna.
Compatible with TV twin lead
Types of Antennas (cont.)
Matched system:

## Slide 12
Monopole Wire Antenna
This is a variation of the dipole, using a ground plane instead of a second wire.
h
Feeding coax
Similar properties as the dipole
Mainly used when the antenna is mounted on a conducing object or platform
Usually fed with a coaxial cable feed
Types of Antennas (cont.)

## Slide 13
Monopole Wire Antenna (cont.)
Types of Antennas (cont.)

## Slide 14
Yagi Antenna
This is a variation of the dipole, using multiples wires (with one “reflector” and one or more “directors” (acting as a lens).
Low bandwidth
Moderate directivity
Commonly used as a UHF TV antenna
Prof. Yagi
Types of Antennas (cont.)
Excited element

## Slide 15
Yagi Antenna (cont.)
UHF Yagi
VHF Log-periodic
UHF Yagi
UHF Yagi
Types of Antennas (cont.)

## Slide 16
Yagi of CP Elements
Used for circular polarization
Two perpendicular dipoles fed 90o out of phase.
Types of Antennas (cont.)

## Slide 17
Log-Periodic Antenna
This consists of multiple dipole antennas of varying lengths, connected together.
High bandwidth
Moderate directivity
Commonly used as a VHF TV antenna
Beam
Types of Antennas (cont.)
The input impedance repeats periodically when plotted vs. the log of the frequency.

## Slide 18
Log Periodic Antenna (cont.)
Types of Antennas (cont.)

## Slide 19
Typical Outdoor TV Antenna
Types of Antennas (cont.)
VHF Log Periodic
UHF Yagi
Corner Reflector

## Slide 20
CP Helical Antenna
Helical antennas are often used for circular polarization.
GPS satellite
Types of Antennas (cont.)

## Slide 21
Horn Antenna
It acts like a “loudspeaker” for electromagnetic waves.
High bandwidth
Moderate to high directivity (directivity is determined by the size / wavelength)
Commonly used at microwave frequencies and above
Often used as a feed for a reflector antenna
Types of Antennas (cont.)

## Slide 22
Horn Antenna (cont.)
Arno A. Penzias and Robert W. Wilson used a large horn antenna to detect microwave signals from the “big bang” (Nobel Prize, 1978).
Types of Antennas (cont.)

## Slide 23
Horn Antenna (cont.)
This is a variation called the “hoghorn” antenna (a combination of horn+reflector).
Types of Antennas (cont.)

## Slide 24
Microstrip (Patch) Antenna
It consists of a printed “patch” of metal on top of a grounded dielectric substrate.
Acts as a radiating resonant cavity
Easily fed by microstrip line or coaxial cable
Low to moderate bandwidth (usually a few percent)
Low directivity (unless used in an array)
Low-profile (h can be made very small, at the expense of bandwidth)
Can be easily made by etching or machining
Can be made conformable (flexible and mounted on a curved surface)
Commonly used at microwave frequencies and above
Current
Types of Antennas (cont.)

## Slide 25
Microstrip (Patch) Antenna (cont.)
Types of Antennas (cont.)

## Slide 26
Dielectric Resonator Antenna (DRA)
It consists of a dielectric material (such as ceramic) on top of a grounded dielectric substrate.
Acts as a resonating dielectric object
Moderate to large bandwidth
Low directivity (unless used in an array)
Commonly used at microwave frequencies and above
Usually more difficult to fabricate than a patch antenna
The dielectric resonator antenna was invented by our very own Prof. Long in the Dept. of ECE!
Cylindrical DRA
Types of Antennas (cont.)

## Slide 27
Dielectric Resonator Antenna (cont.)
Types of Antennas (cont.)

## Slide 28
We consider here the radiation from an antenna.
The far-field radiation acts like a plane wave going in the radial direction.
The shape of the pattern in the far field is only a function of (, ).
"far field"
S = Poynting vector
Antenna Radiation
+
-
r
(phasor electric field)

## Slide 29
How far do we have to go to be in the far field?
Sphere of minimum diameter D that encloses the antenna.
+
-
Antenna Radiation (cont.)

## Slide 30
The far-field has the following form:
Depending on the type of antenna, either or both polarizations may be radiated
(e.g., a vertical wire antenna radiates only E polarization).
Antenna Radiation (cont.)
Example: vertical dipole
Example: horizontal loop antenna
TMz
TEz

## Slide 31
The power density in the far field is:
or
Antenna Radiation (cont.)

## Slide 32
The far field always has the following form:
In decibels (dB):
Antenna Radiation (cont.)

## Slide 33
A normalized far-field pattern is usually shown vs. the angle  (for a fixed angle  =0) in polar coordinates.
The subscript “m” denotes the beam maximum.
An “elevation cut”
Antenna Radiation (cont.)
-9
-3
-6
0o dB
30°
30°
60°
120°
150°
150°
120°
60°
0

## Slide 34
Antenna Radiation (cont.)
E-plane and H-plane
E-plane
H-plane
Current flow
Feed
E-plane:
the plane containing the E vector.
H-plane:
the plane containing the H vector.
Example: Microstrip antenna

## Slide 35
The Poynting vector in the far field is
The total power radiated (in Watts) is then given by
Hence, we have
Radiated Power

## Slide 36
In dB,
The directivity (in a particular direction) is the ratio of the actual power density radiated in that direction to the power density that would be radiated in that direction if the antenna were an isotropic radiator (radiates equally in all directions).
The directivity of the antenna in the directions (, ) is defined as
Note: The directivity is sometimes referred to as the “directivity with respect to an isotropic radiator.”
Directivity

## Slide 37
The directivity is then directly expressed in terms of the far field pattern:
Directivity (cont.)
Usually, the directions are chosen to corresponds to the main beam direction:

## Slide 38
Directivity (cont.)
Antenna with moderate directivity
(e.g., dipole)
Antenna with high directivity
(e.g., horn or dish)
-9
-3
-6
0 dB
30°
30°
60°
120°
150°
150°
120°
60°
-9
-3
-6
0 dB
30°
30°
60°
120°
150°
150°
120°
60°

## Slide 39
Two Common Cases: Dipole Antennas
Short dipole wire antenna (l << 0): D = 1.5
Resonant half-wavelength dipole wire antenna (l = 0 / 2): D = 1.643
-9
-3
-6
0 dB
30°
30°
60°
120°
150°
150°
120°
60°
Short dipole
Wire dipole antenna
Directivity (cont.)
Feed

## Slide 40
The beamwidth measures how narrow the beam is
(the narrower the beamwidth, the higher the directivity).
HPBW = half-power beamwidth
The power density is down by a factor of 1/2.
The field is down by a factor of 1/2 = 0.707.
In dB, we are down by 3 dB.
At the “half-power” points:
Beamwidth

## Slide 41
The sidelobe level measures how large the sidelobes are.
In this example the sidelobe level is about -13 dB.
Sidelobe Level
Sidelobes
Sidelobe level
Main beam

## Slide 42
The radiation efficiency of an antenna is defined as
Prad = power radiated by the antenna
Pin = power input to the antenna
The gain of an antenna in the directions (, ) is defined as
In dB, we have
Gain and Efficiency

## Slide 43
The gain tells us how strong the radiated power density is in a certain direction, for a given amount of input power.
Therefore, in the far field:
Recall that
Gain and Efficiency (cont.)

## Slide 44
The antenna acts like a load impedance during transmit.
At resonance, the input reactance Xin is zero (the desired situation).
Input Impedance
Note: We usually want a match between the input impedance and the characteristic impedance Z0 of the feeding transmission line, to avoid reflection.

## Slide 45
At resonance:
Input Impedance (cont.)
Monopole:
Dipole:

## Slide 46
The Thévenin equivalent circuit of an antenna being used as a receive antenna is shown below.
Receive Antenna
+
-
+
-
The Thevenin impedance is the same as the input impedance of the antenna.

## Slide 47
The power received by an optimum conjugate-matched load:
For a resonant dipole wire antenna:
Receive Antenna (cont.)
+
-
Load
Prec = PL = power absorbed by load
ANT

## Slide 48
We can find the power received using an effective area.
Receive circuit: Assume an optimum conjugate-matched load:
Receive Antenna (cont.)
+
-
Prec = PL = power absorbed by load
ANT

## Slide 49
We have the following general formula*:
*A derivation is given in the following book:
C. A. Balanis, Antenna Engineering, 3rd Ed., 2016, Wiley.
G = G(,) = gain of antenna in direction (,)
Receive Antenna (cont.)
(Usually, we assume that (,) is in the main beam direction.)

## Slide 50
Effective area of a lossless resonant half-wave dipole antenna:
Hence:
Assuming normal incidence ( = 90o):
Receive Antenna (cont.)
Assume lossless antenna:
er = 100%
(G = D)
Note: The dipole will receive more power at a lower frequency (larger l), assuming the same incident power.

## Slide 51
Example
Find the received power Prec in the example below, assuming that the receiver is connected to an optimum conjugate-matched load.
f = 1 [GHz] (0 = 0.29979 [m])
Pin = 10 [W]
r = 1 [km]
Example with Wire Antennas
Assume lossless antennas:
er = 100%
(G = D)
z
Receive antenna (RX)
x
r
Transmit antenna (TX)
Resonant dipoles

## Slide 52
Hence:
The result is:
Gain of TX
Example with Wire Antennas (cont.)
Gain of RX

## Slide 53
Effective area of dish (reflector) antenna
Aphy = physical area of dish
eap = “aperture efficiency”
In the maximum gain (main beam) direction:
The aperture efficiency is usually less than 1 (less than 100%).
Receive Antenna (cont.)
Now it is the effective area that we know, and from this we can calculate the gain.

## Slide 54
Dish antenna:
Obtaining a higher gain means having a larger dish.
Gain of Dish Antenna

## Slide 55
Example
A microstrip antenna on a CubeSat with a gain of 8 (9.03 dB) transmits with an input power of 1 [W] at 10.0 GHz from a distance of 50,000,000 [km] (near Mars).
How much power will be received by the NASA Deep Space Network dish at Goldstone, CA, which has a diameter of 70 [m]? Assume an aperture efficiency of 0.75 (75%).
Express answer in Watts and in dBm (dB relative to a milliwatt).
Example with Dish Antenna

## Slide 56
Example (cont.)
Parameters:
Example with Dish Antenna (cont.)