## Slide 1
Adapted from notes by Prof. Stuart A. Long
Notes 4 Maxwell’s Equations
ECE 3317
Applied Electromagnetic Waves
Prof. David R. Jackson
Fall 2023

## Slide 2: Overview
Here we present an overview of Maxwell’s equations. A much more thorough discussion of Maxwell’s equations may be found in the text and class notes for ECE 3318:
http://courses.egr.uh.edu/ECE/ECE3318
Notes 10: Electric Gauss’s law
Notes 18: Faraday’s law
Notes 28: Ampere’s law
Notes 28: Magnetic Gauss law
Extra reference: D. Fleisch, A Student’s Guide to Maxwell’s Equations, Cambridge University Press, 2008. (This is on reserve in the Library.)

## Slide 3: Electromagnetic Fields
Four vector quantities
E electric field [Volt/meter]
D electric flux density [Coulomb/meter2]
H magnetic field [Amp/meter]
B magnetic flux density [Weber/meter2] or [Tesla]
Each are functions of space and time
e.g. E(x,y,z,t)
J electric current density [Amp/meter2]
ρv electric charge density [Coulomb/meter3]
Reminder:
The Handscript SF font is used to denote time-varying vectors.

## Slide 4: MKS units
Length – meter [m]
Mass – kilogram [kg]
Time – second [s]
Some common prefixes and the power of ten each represent are listed below
femto - f - 10-15
pico - p - 10-12
nano - n - 10-9
micro - μ - 10-6
milli - m - 10-3
mega - M - 106
giga - G - 109
tera - T - 1012
peta - P - 1015
centi - c - 10-2
deci - d - 10-1
deka - da - 101
hecto - h - 102
kilo - k - 103

## Slide 5: Maxwell’s Equations
(Time-varying, differential form)

## Slide 6: Maxwell
James Clerk Maxwell (1831–1879)
James Clerk Maxwell was a Scottish mathematician and theoretical physicist. His most significant achievement was the development of the classical electromagnetic theory, synthesizing all previous unrelated observations, experiments and equations of electricity, magnetism and even optics into a consistent theory. His set of equations—Maxwell's equations—demonstrated that electricity, magnetism and even light are all manifestations of the same phenomenon: the electromagnetic field. From that moment on, all other classical laws or equations of these disciplines became simplified cases of Maxwell's equations. Maxwell's work in electromagnetism has been called the "second great unification in physics", after the first one carried out by Isaac Newton.
Maxwell demonstrated that electric and magnetic fields travel through space in the form of waves, and at the constant speed of light. Finally, in 1864 Maxwell wrote A Dynamical Theory of the Electromagnetic Field where he first proposed that light was in fact undulations in the same medium that is the cause of electric and magnetic phenomena. His work in producing a unified model of electromagnetism is considered to be one of the greatest advances in physics.
(Wikipedia)

## Slide 7: Maxwell’s Equations (cont.)
Faraday’s law
Ampere’s law
Magnetic Gauss law
Electric Gauss law
Questions: When does a magnetic field produce an electric field? When does an electric field produce a magnetic field? When does a current flow produce a magnetic field? When does a charge density produce an electric field?

## Slide 8: Charge Density
Example: Protons are closer together as we move to the right.
Non-uniform cloud of charge density
+ + + +
+ + + +
+ + + +

## Slide 9: Current Density Vector
Medium
Current flow is defined to be in the direction that positive charges move in.
Note: If negative charges are moving, we can pretend that positive charges are moving in the opposite direction.

## Slide 10: Current Density Vector (cont.)
Material |  [S/m]
Silver | 6.3107
Copper | 6.0107
Copper (annealed) | 5.8107
Gold | 4.1107
Aluminum | 3.5107
Zinc | 1.7107
Brass | 1.6107
Nickel | 1.4107
Iron | 1.0107
Tin | 9.2106
Steel (carbon) | 7.0106
Steel (stainless) | 1.5106
http://en.wikipedia.org/wiki/Electrical_resistivity_and_conductivity
Ohm’s law

## Slide 11: Current Density Vector (cont.)
Current through a tilted surface:
Medium

## Slide 12: Current Density Vector (cont.)
Note:
The direction of the unit normal vector determines whether the current is measured going up or down through the surface.

## Slide 13
Law of Conservation of Electric Charge (Continuity Equation)
Flow of electric current out of volume (per unit volume)
Rate of decrease of electric charge (per unit volume)
This is the continuity equation in point or differential form.
(“zero identity”)

## Slide 14
Continuity Equation (cont.)
Apply the divergence theorem:
Integrate both sides over an arbitrary volume V:
V
S
Hence:
(outward normal)
(current flowing out of V)

## Slide 15
Continuity Equation (cont.)
Physical interpretation:
V
S
(This assumes that the surface is stationary.)
or
Hence
Right-hand side:

## Slide 16
Continuity Equation (cont.)
This implies that charge is never created or destroyed.
It only moves from one place to another!

## Slide 17: Maxwell’s Equations (cont.)
Note: Regular (not script) font is used for statics, just as it is for phasors.

## Slide 18: Maxwell’s Equations (cont.)
Time-harmonic (phasor) domain

## Slide 19
Constitutive Relations
The characteristics of the media relate D to E and H to B
(exact value that is defined)
Free Space
*Prior to 2019
(since 1983)

## Slide 20
Definition of I =1 Amp:
I
I
d
Fx2
x
# 1
# 2
Two infinite wires carrying DC currents
Definition of the Amp*:
From ECE 3318:
Constitutive Relations (cont.)
*Prior to 2019

## Slide 21
Constitutive Relations (cont.)
Free space, in the phasor domain:
This follows from the fact that
(where a is a real number)

## Slide 22
Example
Given the following electric field E in free space:
Find the magnetic field H.
In the phasor domain:
Hence
(no  variation)

## Slide 23
Example (cont.)

## Slide 24
Example (cont.)
Alternative approach (in the time domain directly):
(no  variation)

## Slide 25
Example (cont.)
So
All fields must be pure sinusoidal waves in the time-harmonic steady state.

## Slide 26
Example (cont.)
This describes the far-field radiation from a small vertical dipole antenna.

## Slide 27
In a material medium:
r = relative permittivity
r = relative permeability
Material Properties
Note: The fields E and B are the physical fields, meaning they exert a force on a charged particle that can be measured. The other two fields are defined.

## Slide 28
Material Properties (cont.)
Where does permittivity come from?
Water
Molecule:

## Slide 29
Linear material:
Define:
Then
Note: e > 0 for most materials
The term e is called the “electric susceptibility.”
so
Material Properties (cont.)

## Slide 30
Teflon
Water
Styrofoam
Quartz
(a very polar molecule, fairly free to rotate)
Note: r > 1 for most materials:
Material Properties (cont.)

## Slide 31
Where does permeability come from?
Because of electron spin, atoms tend to acts as little current loops, and hence as electromagnetics, or bar magnets. When a magnetic field is applied, the little atomic magnets tend to line up.
N
S
N
S
N
S
N
S
Material Properties (cont.)
Electron:
Iron

## Slide 32
so
Define:
Then
The term m is called the “magnetic susceptibility.”
Linear material:
Note: m > 0 for most materials
Material Properties (cont.)

## Slide 33
Note: Values can often vary depending on purity and processing.
http://en.wikipedia.org/wiki/Permeability_(electromagnetism)
Material | Relative Permeability r
Vacuum | 1
Air | 1.0000004
Water | 0.999992
Copper | 0.999994
Aluminum | 1.00002
Silver | 0.99998
Nickel | 600
Iron | 5000
Carbon Steel | 100
Transformer Steel | 2000
Mumetal | 50,000
Supermalloy | 1,000,000
Material Properties (cont.)

## Slide 34
Lorenz Force Law
The fields E and B are the two physical fields, since they exert a force on a particle (the Lorenz force law). The D and H fields are the defined fields.
Lorenz force law:
This experimental law gives us the force on a particle with charge q moving with a velocity vector v.

## Slide 35
Variation Independent of Dependent on
Space Homogenous Inhomogeneous
Frequency Non-dispersive Dispersive
Time Stationary Time-varying
Field strength Linear Non-linear
Direction of Isotropic Anisotropic
E or H
Terminology
Properties of  or 

## Slide 36
Isotropic Materials
Isotropic: This means that ε and μ are scalar quantities,
which means that D || E (and B || H )
x
y
x
y

## Slide 37
Here ε (or μ) is a tensor (can be written as a matrix)
This results in E and D NOT being in the same direction.
Anisotropic Materials
Example:
or
“biaxial medium”

## Slide 38
Anisotropic Materials (cont.)
Practical example: uniaxial substrate material
Teflon substrate
Fibers (horizontal)
There are two different permittivity values, a horizontal one and a vertical one.

## Slide 39
Anisotropic Materials (cont.)
This column indicates that v is being measured.
RT/duroid® 5870/5880/5880LZ High Frequency Laminates
https://www.rogerscorp.com/advanced-electronics-solutions/rt-duroid-laminates/rt-duroid-5870-laminates