## Slide 1
Adapted from notes by Prof. Stuart A. Long
Notes 5 Poynting’s Theorem
ECE 3317
Applied Electromagnetic Waves
Prof. David R. Jackson
Fall 2023

## Slide 2
Poynting Theorem
The Poynting theorem is one of the most important in EM theory. It tells us the power flowing in an electromagnetic field.
John Henry Poynting (1852-1914)
John Henry Poynting was an English physicist. He was a professor of physics at Mason Science College (now the University of Birmingham) from 1880 until his death.
He was the developer and eponym of the Poynting vector, which describes the direction and magnitude of electromagnetic energy flow and is used in the Poynting theorem, a statement about energy conservation for electric and magnetic fields. This work was first published in 1884. He performed a measurement of Newton's gravitational constant by innovative means during 1893. In 1903 he was the first to realize that the Sun's radiation can draw in small particles towards it. This was later coined the Poynting-Robertson effect.
In the year 1884 he analyzed the futures exchange prices of commodities using statistical mathematics.
(Wikipedia)

## Slide 3
Poynting Theorem (cont.)
From these we obtain:

## Slide 4
Subtract, and use the following vector identity:
We then have:
Poynting Theorem (cont.)

## Slide 5
Next, assume that Ohm's law applies for the electric current:
or
Poynting Theorem (cont.)

## Slide 6
From calculus (chain rule), we have that
Hence, we have
Poynting Theorem (cont.)

## Slide 7
This may be written as
Poynting Theorem (cont.)

## Slide 8
Final differential (point) form of Poynting’s theorem:
Poynting Theorem (cont.)

## Slide 9
Volume (integral) form
Integrate both sides over a volume and then apply the divergence theorem:
Poynting Theorem (cont.)
Divergence theorem

## Slide 10
Final volume form of Poynting theorem in the most general case:
For a stationary surface:
Poynting Theorem (cont.)
stationary surface

## Slide 11
Poynting’s theorem:
Power dissipation as heat (Joule's law)
Rate of change of stored magnetic energy
Rate of change of stored electric energy
Left-hand side = power flowing into the region V.
(We assume here that S is stationary.)
Poynting Theorem (cont.)
Conservation of energy:

## Slide 12
Or, we can say that
Define the Poynting vector:
Hence
Poynting Theorem (cont.)

## Slide 13
Analogy:
J = current density vector
S = power flow vector
Poynting Theorem (cont.)

## Slide 14
Direction of power flow in W/m2
Poynting Theorem (cont.)
Poynting vector
Note:
At high frequencies (e.g., light or x rays), it is often convenient to think of photons moving in space, carrying the power flow.
The two points of view are consistent.

## Slide 15
Power Flow
The power P flowing through the surface S (from left to right) is:
Surface S

## Slide 16
Time-Average Poynting Vector
Assume sinusoidal (time-harmonic) fields:
From our previous discussion (Notes 2) about time averages, we know that

## Slide 17
Complex Poynting Vector
Define the complex Poynting vector:
We then have that
Note:
The imaginary part of the complex Poynting vector corresponds to the Vars/m2 flowing in space.
The units of S are [VA/m2].

## Slide 18
The complex power P flowing through the surface S (from left to right in the above figure) is:
Surface S
Complex Poynting Vector (cont.)
Note:
The direction of the unit normal determines whether the power flow is form left to right or from right to left.

## Slide 19
Complex Poynting Vector (cont.)
What does Vars flowing in space mean?
Equation for Vars flowing into a region (derivation omitted):
The Vars flowing into the region V is equal to the difference in the time-average magnetic and electric stored energies inside the region (times a factor of 2).
VARS
Question:
does an inductor absorb positive or negative Vars?

## Slide 20
Complex Poynting Vector (cont.)
VARS “consumed”
Power (watts)
consumed
Watts
V
S
Vars
(heat dissipation inside the region)

## Slide 21
Photons
At high frequencies (e.g., light, x-rays), physicists like to think in terms of photons.
Np photons per m3
A
v
Photons moving:
(energy of photon)
(Planck’s constant)

## Slide 22
Photons (cont.)
Example
A cell phone base station antenna transmits at 2.1 [GHz] with 100 [W] of power. At 1 [km] away the power density is 10-4 [W/m2]. What is the photon density?

## Slide 23
Photons (cont.)
(momentum of photon)
Photons also carry momentum, and can therefore exert a force on objects.
Solar Sail

## Slide 24
Example
At z = 0:
Find the Watts and Vars crossing the plane z = 0 (downward) through a 1 m2 area S.

## Slide 25
Example (Cont.)
At z = 0:
(phasor domain)
Hence

## Slide 26
Note on Circuit Theory
Although the Poynting vector can always be used to calculate power flow on a transmission line, circuit theory can also be used, and this is usually easier.
The second form is much easier to calculate!
Example (low frequency circuit):
Voltage phasor
Current phasor
(This is exact for a transmission line.)

## Slide 27
Example: Parallel-Plate Transmission Line
At z = 0:
The voltage and current have the form of waves that travel along the line in the z direction.
+
-

## Slide 28
At z = 0:
Example (cont.)
(from ECE 3318)
+
-

## Slide 29
Example (cont.)
We then have
+
-
so