## Slide 1
Prof. David R. Jackson
Dept. of ECE
Spring 2023
Notes 2
Charge
ECE 3318
Applied Electricity and Magnetism
Notes prepared by the EM Group University of Houston

## Slide 2
Definition: No time variation. In terms of frequency, f = 0 [Hz]
The electromagnetic field splits into two independent parts:
Electrostatics: (q, E) charge produces electric field
Magnetostatics: (I, B) current produces magnetic field
The static approximation is usually accurate for d <<0
(d is the dimension of the circuit or device).
Statics
Example:
The electric field from a 60 [Hz] power line mainly comes from the charge on it.
The magnetic field from a 60 [Hz] power line mainly comes from the current on it.

## Slide 3
Example: f = 60 [Hz]
Clearly, most circuits fall into the static-approximation category at 60 [Hz]!
This gives:
Statics (cont.)
Note: This is an exact (defined) value since 1983.

## Slide 4
The following are special cases of electromagnetics at low frequency:
Circuit theory (e.g., ECE 2201, ECE 2202)
Electronics
Power engineering
Magnetics (design of motors, generators, transformers, etc.)
Examples of high-frequency systems that are not modeled by statics:
Antennas
Transmission lines
Microwaves
Optics
ECE 3317
Statics (cont.)

## Slide 5
Statics (cont.)
A transformer in a substation
Overhead high-voltage power lines
Power buses in a substation
Examples of low-frequency systems
Generators at Hoover dam

## Slide 6
Charge
Atom
e
p
Ben Franklin
Ben Franklin chose the convention of using positive and negative charges.

## Slide 7
1) Volume charge density v [C/m3]
Charge Density
a) Uniform (homogeneous) volume charge density
Uniform cloud of charge density
Example: protons floating in space.
+ + + +
+ + + +
+ + + +

## Slide 8
b) Non-uniform (inhomogeneous) volume charge density
Charge Density (cont.)
Example: Protons are closer together as we move to the right.
Non-uniform cloud of charge density
+ + + +
+ + + +
+ + + +

## Slide 9
so
Hence
Charge Density (cont.)

## Slide 10
2) Surface charge density s [C/m2]
Non-uniform
Uniform
Charge Density (cont.)
Non-uniform sheet of surface charge density
Example: Protons are sprayed onto a sheet of paper.
+ + + +
+ + + +
+ + + +

## Slide 11
Charge Density (cont.)
Hence
so

## Slide 12
3) Line charge density l [C/m]
Non-uniform
Uniform
Charge Density (cont.)
Non-uniform line charge density
Example: Protons are sprayed onto a thread.
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 13
Charge Density (cont.)
so
Hence
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 14
Charge Summary

## Slide 15
Find: Q
Example
v = v0 =10 [C/m3]
Note: This is a uniform charge density.

## Slide 16
Find: Q
Example
v = 2r [C/m3], r < a
Separable integrand
This is a separable integrand with fixed limits of integration, so we can split it up into a product of 1-D integrals.
Note: This is a non-uniform (inhomogeneous) charge density.
(Please see the next slide for a reminder about spherical coordinates.)

## Slide 17
Reminder of Spherical Coordinates
Note: 0    
.

## Slide 18
Example:
Find the Equivalent Surface Charge Density for a Slab of Volume Charge Density
Note:
Equivalent charge density is a helpful concept for finding the fields from charges, as we will see later in Gauss’s law.

## Slide 19
Example (cont.)
Equivalent surface charge density:

## Slide 20
Compare:
Example (cont.)
In our case (uniform volume charge density) we have:
so

## Slide 21
Analogy with mass density:
Example (cont.)
(mass per unit area of the plate)
Metal plate