## Slide 1
Prof. David R. Jackson
Dept. of ECE
Spring 2023
Notes 3
Current
ECE 3318
Applied Electricity and Magnetism
Notes prepared by the EM Group University of Houston

## Slide 2
Current is the flow of charge: the unit is the ampere (amp).
Current
1 amp  1 [C/s]
Convention (Ben Franklin): Current flows in the direction that positive charges move in.
+
+
+
+
Current flows from left to right.
Velocity
Ampere

## Slide 3
Ampere
History of the Ampere
Current (cont.)
Before May 20, 2019:
The amp was defined first, from the force between two parallel wires.
The coulomb was then defined from the amount of charge flowing in one second.
After May 20, 2019:
The coulomb was defined first.
The amp was then defined from the flow rate of one coulomb per second.
1 amp  1 [C/s]

## Slide 4
Current (cont.)
Definition of I =1 Amp:
Previous definition of Amp (before May 20, 2019):
From later in the semester:
Note: 0 = permeability of free space.
I
I
d
Fx2
x
# 1
# 2
Two infinite wires carrying DC currents
Exact value!

## Slide 5
Current (cont.)
Present definition of Amp (after May 20, 2019):
1 amp  1 [C/s]
Present definition of coulomb:
(no longer an exact value)
Exact defined value
Note:
Although the values of both 0 and 0 changed in 2019, the speed of light did not. It is still defined the way it was in 1983:
c  2.99792458108 [m/s]
Definition
(derivation omitted)

## Slide 6
Postulate: Positive charges moving one way is equivalent to negative charges moving the other way (in terms of most measurable physical electromagnetic effects).
Current (cont.)
1 [A]
-
-
-
-
Flow rate is 1 [C] per second
Velocity
This is equivalent to:
+
+
+
+
Flow rate is 1 [C] per second
Velocity
In both cases:
Current flows from right to left.

## Slide 7
Sign convention: A positive current flowing one way is equivalent to a negative current flowing the other way.
Current (cont.)
+
+
+
+
1 [A]
Flow rate is 1 [C] per second
Velocity
-1 [A]
or
Note:
The blue arrow is called the reference direction arrow. It tells us the direction we measure the current in.
It is very useful in circuit theory to assume reference directions
and allow for negative current.
Equivalent!

## Slide 8
Mathematical definition of current
Current (cont.)
Reference direction arrow
Q = amount of charge (positive or negative) that crosses the plane in the direction of the reference arrow in time t.
I
Q
More generally,
Uniform current
Non-uniform current
(direction we are measuring I)

## Slide 9
Example
i(t)
Q
Find the charge Q(t) that crosses the dashed line going from left to right in the time interval (0, t) [s].

## Slide 10
Example (cont.)

## Slide 11
Note on Vector Notation
Review of vector notation:
Note: For complex vectors we have

## Slide 12
Current Density Vector J
The current-density vector points in the direction of current flow
(the direction of positive charge motion).
Consider a general “cloud” of charge density, where the charge density as well as the velocity of the charges may be different at each point.
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 13
The magnitude of the current-density vector J tells us the current density (current per square meter) that is crossing a small surface that is perpendicular to the current-density vector.
Current Density Vector (cont.)
Hence
+
+
+
+
+
+
+
+
+
+
+
+
I = the current crossing the surface S in the direction of the velocity vector.

## Slide 14
Current Density Vector (cont.)
Consider a small tube of moving charges inside the cloud:
+
+
+
+
+
+
+
+
+
+
+
+
Tube
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 15
Current Density Vector (cont.)
L = distance traveled by charges in time t.
or
Hence
so
+
+
+
+
Reference plane
Tube

## Slide 16
Current Density Vector (cont.)
Summary
Definition of J
Charge-current equation

## Slide 17
Current Crossing a Surface
This is the current crossing the surface S in the direction of the unit normal.
Note:
The surface S does not have to be perpendicular to the current density vector.
(small surface)

## Slide 18
Current Crossing Surface
Integrating over a surface,
Note:
The direction of the unit normal vector determines whether the current is measured going in or out.

## Slide 19
Example
Cloud of electrons
Ne = 8.47 1028 [electrons / m3]
(a) Find: current density vector inside the wire
The cloud of electrons is inside of a copper wire.
Hence
1) There are 8.47 1028 atoms / m3.
2) There is one electron/atom in the conduction band.
Notes:
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 20
Example (cont.)
(b) Find: current I in the wire for the given reference direction
Radius a = 1 [mm]
Note: The wire is neutral, but the positive nuclei do not move.
-
-
-
-
-
-

## Slide 21
Example (cont.)
Density of Cu: 8.94 [g/cm3]
Avogadro’s constant: 6.02214179301023 atoms/mol
1 mol = amount of material in grams equal to the atomic weight of atom
Atomic weight of Cu: 63.546 (atomic number is 29, but this is not needed)
1 electron per atom in the conduction band (Ne = atoms/m3)
Properties of copper (Cu)
Using knowledge of chemistry, calculate the value of Ne (that is used in the previous example).

## Slide 22
Example
Find the current I crossing the surface S in the upward direction.

## Slide 23
Example (cont.)
Note:
The integrand is separable, and the limits of integration are fixed numbers. Hence, we can split this into a product of two one-dimensional integrals.
Top view

## Slide 24
Example
Find the current I crossing the surface S in the upward direction.

## Slide 25
Example (cont.)
Note:
The integrand is separable, but the limits of integration are not fixed numbers. Hence, we cannot split this into a product of two one-dimensional integrals.
Top view

## Slide 26
Surface Current
Inside the actual conductor:
This is a useful concept for thin currents!
Metal plate
Uniform current

## Slide 27
Surface Current (cont.)
Current IC flowing across a path C:
Note:
For the unit normal pictured above, this will give us the current crossing the curve from left to right.

## Slide 28
Example
Find the current IC flowing across the path C (from left to right).
C = straight-line path of length L = 3 meters, making an angle of 30o from the z axis.
Hence, we have: