## Slide 1
Prof. David R. Jackson
Dept. Of ECE
Spring 2023
Notes 5
Grounding
ECE 3318
Applied Electricity and Magnetism
Notes prepared by the EM Group University of Houston

## Slide 2
Grounding
Grounding: connecting a conductor to the physical earth
Safety reasons
Noise reasons
Equipment
Water pipe
Earth
https://en.wikipedia.org/wiki/Ground_(electricity)
Grounding system

## Slide 3
Grounding (cont.)
Ensures that there is no voltage drop between equipment and ground.
Ensures that there is no static electric field outside of equipment.
Ensures that there is no static charge build up on equipment.
Grounding:
Equipment
Water pipe
+
-
Earth
Physical grounding is usually to underground pipes and conductors.

## Slide 4
Grounding (cont.)
Equipment
Ground
Ground symbol:
Note: Grounding is NOT is the same thing as choosing a reference point.
However, when a circuit is grounded, the ground is OFTEN chosen to be the reference point, and the voltage is usually assigned to be zero volts at the ground.

## Slide 5
Example
Note:
For most DC voltage sources, it is the negative terminal that is grounded (as shown here).
An unusual choice of reference point!
The potential of the earth is -12 [V] !
+
-

## Slide 6
Example (cont.)
This is the most common scenario:
Ground is chosen as the reference.
The reference voltage is chosen as zero.
+
-

## Slide 7
Grounding in Power Systems
Ground
Green
Hot (“Live”)
Black
Neutral
White
Note:
The neutral is grounded back at the
junction box.
Note that the neutral slot is larger than the “hot” slot.
Note:
The colors shown here are the usual standard in the U.S.

## Slide 8
The neutral wire is grounded back at the junction box.
Note:
The voltage of the neutral wire at the device is not exactly the same as that of ground, because the neutral wire has a resistance.
Grounding in Power Systems (cont.)
Ground
Hot
Neutral
+
-
V
I
Junction box
Wall
Device
Metal case
Cord

## Slide 9
Ground Protection
Ground
Hot
Neutral
A metal casing is normally connected to ground.
(We do not ground insulators.)
Metal casing
This gives protection if the hot comes loose and touches the case.

## Slide 10
GFCI (Ground Fault Circuit Interrupter)
The GFCI circuit trips when | Ih - In | > 5 [mA] (USA)
In normal operation, Ig = 0.
Hot
Neutral
GFCI

## Slide 11
GFCI (cont.)
Principle of operation: 1. Electromagnet with electronics 2. Current transformer secondary 3. Transformer core 4. Test switch L Live (hot) conductor N Neutral conductor
http://en.wikipedia.org/wiki/Residual-current_device
A solenoid (electromagnet) normally keeps the contacts (L and N) closed. When the sensing circuit detects a signal (due to an imbalance of the currents), the current to the solenoid stops, and the contacts open by spring action.

## Slide 12
GFCI (cont.)
http://en.wikipedia.org/wiki/Residual-current_device
Input (hot and neutral)
Output (hot and neutral)
Reset button
Contacts
Solenoid
Sensing coil
Sensing circuitry
Test button
Test wire

## Slide 13
Double Insulated Tool
The device has two layers of insulation (usually the case is an insulating plastic case). It does not require a ground.
Hot
Neutral
Plastic case
Symbol:

## Slide 14
Common Plugs (in US)
Two prong polarized plug
Three prong adapter (“cheater plug”)
Three prong (grounded) plug

## Slide 15
Safety Rules
Make sure all power tools and equipment are grounded or double insulated.
If a device has a three-prong connector (grounded plug) make sure that you do not defeat it by bypassing it (plugging it into a two-prong adapter).
For appliances with a two-prong connection that are not double-insulated (e.g., household lamps), the plug is usually polarized (one prong is larger than the other). Respect this and do not try to plug it in the wrong way, to minimize shock hazard.
For appliances with a two-prong connection that are not double-insulated (e.g., household lamps), be especially careful to avoid handling them in a wet environment. (The appliance can easily become “hot” if the wiring is faulty.)

## Slide 16
Grounding in Coax Systems
The outer conductor “shield” of the coax is grounded because it is connected to the metal chassis of the equipment, and this is grounded (via a three-prong plug).
Signal generator
Oscilloscope