##### DO NOT BEGIN THIS EXAM UNTIL TOLD TO START

# Name: __________________________________________

# Student Number: _________________________________

## Instructor: ________________________________________

#### ECE 2317

#### Applied Electricity and Magnetism

Exam 1

#### February 16, 2002

- This exam is closed book and closed notes. A calculator and one crib sheet (one 8.5” X 11” piece of paper) are allowed.

- Show all of your work. No credit will be given if the work required to obtain the solutions is not shown.

- Perform all your work on the paper provided.

- Write neatly. You will not be given credit for work that is not easily legible.

- Leave answers in terms of the parameters given in the problem.

- Show units in all of your final answers.

- Circle your final answers.

- If you have any questions, ask the instructors. You will not be given credit for work that is based on a wrong assumption.

- You will have a total of 90 minutes to work the entire exam.

_____/25  Prob. 1	_____/25  Prob. 3

_____/25  Prob. 2	_____/25  Prob. 4

TABLE OF INTEGRALS

TABLE OF COORDINATE SYSTEM FORMULAS

Problem 1 (25 pts)

A point charge having q = 1 [C] is at the origin. Find the vector force on this point charge due to a line segment of uniform charge density  [C/m] that is parallel to the x axis as shown below. The line segment has length L and is located at a height h above the x axis.

Total force vector =

________________________________________________________________________ [    ]

ROOM FOR EXTRA WORK

Problem 2 (25 pts)

A circular disk of radius a centered at the coordinate origin, and lying in the xy plane, has a surface charge density [C/m2].

- Find the total charge on the disk.

Total charge = ______________________ [    ]

- Find the electric field at (0,0,3).

E =___________________________________ [    ]

ROOM FOR EXTRA WORK

Problem 3 (25 pts)

A surface charge density [C/m2], where  is a constant, exists on the portion   of  a sphere of radius a as shown.  Find the total charge on this part of the sphere.

Total charge = ________________________________[  ]

ROOM FOR EXTRA WORK

Problem 4 (25 pts)

###### A point electrode is at the origin inside a large tank of saltwater. The electrode injects a total current of I0 [A], which spreads equally in all directions. This produces a current density vector in space that is described in spherical coordinates by

Calculate the total current I that crosses the circular area S shown below, flowing in the upward direction. Do this by performing an integration in cylindrical coordinates, over the area of the circle.

The circle lies in a plane that is parallel to the xy plane, and is centered on the z axis. The radius of the circle is a, and it lies at a height h above the xy plane.

Total current = _____________________________________________________ [    ]

ROOM FOR EXTRA WORK

# Text boxes

y

L

h

y

x

q

a

h

electrode

z

S

a

x