##### DO NOT BEGIN THIS EXAM UNTIL TOLD TO START

# Name: __________________________________________

#### ECE 2317

#### Applied Electricity and Magnetism

Exam 1

#### March 28, 2006

- This exam is open book and open notes. You may use any material that you wish, except that no device that can be used for communications is allowed (this includes cell phones and computers).

- Show all of your work. No credit will be given if the work required to obtain the solutions is not shown.

- Perform all your work on the exam in the space allowed.

- Write neatly. You will not be given credit for work that is not easily legible.

- Leave answers in terms of the parameters given in the problem.

- Show units in all of your final answers.

- Put your final answers in the spaces that are indicated.

- Double-check your answers. For simpler problems, partial credit may not be given.

- If you have any questions, ask the instructors. You will not be given credit for work that is based on a wrong assumption.

- Make sure you sign the academic honesty statement on the next page.

Academic Honesty Statement

I agree to abide by the UH Academic Honesty Policy during this exam. I understand that the punishment for violating this policy will be most severe, including the possibility of getting an F in the class and/or getting expelled from the University.

_______________________________________________

Signature

Grading (for instructor use only)

_____/40  Prob. 1

_____/30  Prob. 2

_____/20  Prob. 3

_____/10  Prob. 4

FORMULA SHEET

TABLE OF INTEGRALS

TABLE OF COORDINATE SYSTEM FORMULAS

Problem 1

A non-uniform line charge has a charge density . The line charge runs along the x axis from  to . Find the electric field vector at a point on the y axis located at

Please put your final answer in the space below, and show your work on the pages after this.

Final Answer:

_______________________________________________________________ [         ]

Show work here.

Show work here.

Problem 2

A point charge of q [C] is at the origin. A non-uniform volume charge density  exists inside of the spherical region that is defined by r < a. At  r  =  b > a  there is a spherical shell of uniform surface charge density .

Determine the electric field vector in all three regions:

(a)  r < a

(b)  a < r < b

(c)  r > b

Please put your final answer in the space below, and show your work on the pages after this.

Final Answer:

(a)  _______________________________________________________________ [         ]

(b)  _______________________________________________________________ [         ]

(b)  _______________________________________________________________ [         ]

Show work here.

Show work here.

Problem 3

An electric field is defined in rectangular coordinates as

.

(This is a valid electrostatic field.) Calculate the voltage drop VAB, where A is the point (1, 0, 0) in rectangular coordinates, and B is the point (0, 2, 0) in rectangular coordinates.

Please put your final answer in the space below, and show your work on the page after this.

Final Answer:

_______________________________________________________________ [         ]

Show work here.

Problem 4

A point charge of q = 10 [C] is centered inside of a conducting metal shell of radius 2 [m], as shown below. The metal shell has a total net charge of  -15 [C] on it. The metal shell is then grounded. How much charge flows off the metal shell down to ground?

Please put your final answer in the space below, and show your work on the page after this.

Final Answer:

_______________________________________________________________ [         ]

Show work here.

# Text boxes

b

B

A

y

x

r (0, d, 0)

h

y

2 [m]

x

d

-h

a