##### DO NOT BEGIN THIS EXAM UNTIL TOLD TO START

# Name: __________________________________________

# Student Number: _________________________________

## Instructor: ________________________________________

#### ELEE 2317

#### Applied Electricity and Magnetism

Final Exam, Part B

#### Dec. 6, 2000

- This exam is closed book and closed notes. A calculator and three-page formula sheet are allowed.

- Show all of your work. No credit will be given if the work required to obtain the solutions is not shown.

- Perform all your work on the exam paper provided.

- Write neatly. You will not be given credit for work that is not easily legible.

- Show units in all of your final answers, and express your answers in terms of the parameters given in the problem.

- Circle your final answers.

- If you have any questions, ask the instructors. You will not be given credit for work that is based on a wrong assumption.

- You will have a total of 180 minutes.

_____/20  Prob. 1B

_____/20  Prob. 2B

_____/20  Prob. 3B

ROOM FOR EXTRA WORK

Problem 1B (20 pts)

An engineer measures the resistance R between the inner and outer conductors of a coaxial cable, which has a length of L. The inner and outer radii of the coax are a and b, respectively. The engineer then wishes to know the conductivity of the material inside the coax, from this measurement.

Derive a formula for the conductivity ( of the material inside the coax, in terms of the measured resistance R and the dimensions of the coax.

(: ___________________________________[      ]

Problem 2B (20 pts)

A power line of radius a is at a height h above the ground, which may be modeled as an infinite ground plane at y = 0.

- Calculate the voltage drop VAB between the line and the ground, assuming an effective line charge density  [C/m] on the line. (A is the line, B is the ground.)

VAB:_________________________________________________[        ]

- Assuming that the air has a breakdown field strength of Ec [V/m], calculate the maximum voltage  that can be placed on the line before the air will break down.

:_________________________________________________[        ]

Problem 3B (20 pts)

Determine the magnetic field H at the point (x, 0, 0) due to the infinitely long wire in the z = 0 plane with two right-angle bends, as shown below (the wire goes to infinity in the -x and +x directions).   Find separately the fields , , and  due to each of the segments labeled #1, #2, and #3, respectively, and then find the total H by superposition.

Helpful integral:

:______________________[      ]

:______________________[      ]

:______________________[      ]

:____________________________________________________________[      ]

# Text boxes

#2

earth

h

#1

h

I

(x, 0, 0)

I

I

L

2a

y

b

x

#3

xx

xy