# Name:__________________________________________

# Student Number: _________________________________

ELEE 2317

Applied Electricity and Magnetism

Final Exam

May 4, 2000

PART B

- This exam is closed book and closed notes.  A calculator and 3 (8.5  ( 11 inch ) crib sheets may be used.

- Show all of your work.  No credit will be given if the work required to obtain a solution is not shown.

- Perform all your work on the paper provided.

- Write neatly.  You will not be given credit for work that is not easily legible

- Show units in all final answers.

- Circle your final answers.

- If you have any questions, ask the instructors.  You will not be given credit for work based on an incorrect assumption.

- You have a total of 180 minutes to complete the exam (parts A, B, and C).

_____/15  Prob. 1

_____/15  Prob. 2

Total  _______/30

Problem 1 (15 pts)

Below are listed (in random order) steps for finding the inductance and capacitance per unit length for a coaxial line with a hollow center conductor of radius a and a thin outer conductor of radius b.

- Determine the stored magnetic energy per unit length.

- Use Gauss's Law to determine the electric field between the conductors (sketch a figure showing the correct Gaussian surface).

- Assume a total current  [A] is carried on the surface of the inner conductor and a return current of the same magnitude is carried on the outer conductor.

- Divide the charge per unit length by the potential difference between the conductors.

- Use Ampere's Law to determine the magnetic field between the conductors (sketch a figure showing the correct Amperian path).

- Assume a total effective line charge density of [C/m] on the center conductor and  [C/m] on the outer conductor.

- Divide twice the stored magnetic energy per unit length by the current squared.

- Integrate the electric field to obtain the potential difference between the conductors.

Write in the step number below in the proper order to compute the inductance per unit length, , and after each step, carry out the calculation as indicated (if any).

Step 1 ______

Step 2 ______

Step 3 ______

Step 4 ______

= ________________

Room for additional work

Problem 2 (15 pts)

A rectangular loop is centered between two infinite, parallel wires as shown in the figure.  The wires are spaced a distance d apart and carry a current  as shown, and form a “loop” closed at infinity. Assume that all wires have a negligible radius.

Find the mutual inductance between the pair of loops.

____________________________________

Room for additional work

# Text boxes

W

## L

I2

I1

I1

d