##### DO NOT BEGIN THIS EXAM UNTIL TOLD TO START

# Name: __________________________________________

# Student Number: _________________________________

## Instructor: ________________________________________

#### ECE 2317

#### Applied Electricity and Magnetism

#### Final Exam

#### Spring 2001

- This exam is closed book and closed notes. A calculator and three crib sheets (3  8.5” X 11” pieces of paper) are allowed.

- Show all of your work. No credit will be given if the work required to obtain the solutions is not shown.

- Perform all your work on the paper provided.

- Write neatly. You will not be given credit for work that is not easily legible.

- Leave answers in terms of the parameters given in the problem.

- Show units in all of your final answers.

- Circle your final answers.

- If you have any questions, ask the instructors. You will not be given credit for work that is based on a wrong assumption.

- You will have a total of 180 minutes to work the entire exam.

_____/25  Prob. 1	_____/25  Prob. 4

_____/25  Prob. 2	_____/25  Prob. 5

_____/25  Prob. 3	_____/25  Prob. 6

ROOM FOR EXTRA WORK

Problem 1 (25 pts)

A hollow conducting sphere of radius a has a uniform surface charge density  [C/m2] on it. Outside the conducting sphere is a uniform volume charge density  [C/m3] that exists in free space, in the region b < r < c.

Calculate the potential at r = b, given that the potential is zero at r = 0.

### ROOM FOR EXTRA WORK

Problem 2 (25 pts)

A high-voltage power line runs above the earth as shown below. The power line carries a current of 1,000 [A] in the z direction. The power line is at a height of 50 [m] above the earth. The earth may be assumed to be nonmagnetic, so that it does not affect the magnetic field of the power line.

Calculate the magnetic flux density vector B at a point that is on the surface of the earth (the hollow dot), at a horizontal distance of 200 [m] from the power line. Express your answer in rectangular coordinates.

### ROOM FOR EXTRA WORK

Problem 3 (25 pts)

A constant current I [A] flows in the negative y direction, from the point (0, L, 0) to the origin, as  shown below.

Determine the magnetic field vector H at a point (0, 0, z) on the z axis. You may leave your answer in terms of a single integral.

### ROOM FOR EXTRA WORK

Problem 4 (25 pts)

Consider a one-meter length of coaxial cable as shown below. The inner conductor has a radius  a, the outer conductor has a radius  b, and the plastic material between the two conductors has a relative permittivity . Assume that the outer conductor is at a potential of Vb and the inner conductor is at a potential of Va.

- Solve for the potential function  for . Leave your answer in terms of Va and Vb.

- Find the electric field vector inside the coax. Leave your answer in terms of Va and Vb.

- Find the total charge on the inner conductor. Leave your answer in terms of Va and Vb.

- Using your answer to the above parts, find the capacitance of the one-meter length of coaxial cable.

- Now assume that the plastic material has a conductivity [S/m]. What is the resistance between the two conductors?

Note: The Laplacian in cylindrical coordinates is

.

### ROOM FOR EXTRA WORK

Problem 5 (25 pts)

An infinitely long solid wire of radius a carries a current I [A] in the z direction, as shown below. The current density may be assumed to be uniform inside the wire. The wire is made of copper, which is nonmagnetic ().

- Determine the magnetic field vector H at any point inside the wire.

- Determine the amount of magnetic energy stored inside a one-meter length of the wire.

- Determine the “internal inductance” of the one-meter length of wire. This is the inductance that accounts for magnetic energy stored inside the conductor only.

### ROOM FOR EXTRA WORK

Problem 6 (25 pts)

A rectangular-shaped conductor has a width W and a thickness t. This conductor sits above another conductor that has a width W and a very small thickness (which can be neglected). Both conductors are infinite in the z direction. The top conductor carries a total current of I1 [A] in the z direction. The bottom conductor carries a total current of I2 [A] in the -z direction. The width W is very large compared to the distance d, so that edge effects may be neglected.

Determine the magnetic field vector H in the following regions:

- y < 0

- y > d + t

- 0 < y < d

- d < y < d + t

### ROOM FOR EXTRA WORK

# Text boxes

PEC

a

b

c

y

x

###### I

L

z

(0, 0, z)

x

y

earth

50 [m]

200 [m]

1.0 [m]

z

I

a

x

y

Top View:

z

x

y

d

t

I1

I2

W