##### DO NOT BEGIN THIS EXAM UNTIL TOLD TO START

# Name: __________________________________________

# Student Number: _________________________________

#### ECE 2317

#### Applied Electricity and Magnetism

Final Exam

#### May 6, 2004

- This exam is closed book and closed notes. No materials are allowed other than something to write with. A formula sheet is included with the exam.

- Show all of your work. No credit will be given if the work required to obtain the solutions is not shown.

- Perform all your work on the exam in the space allowed.

- Write neatly. You will not be given credit for work that is not easily legible.

- Leave answers in terms of the parameters given in the problem.

- Show units in all of your final answers.

- Circle your final answers, and make sure they are clearly noticeable.

- If you have any questions, ask the instructor. You will not be given credit for work that is based on a wrong assumption.

- You will have a total of 180 minutes to work the entire exam.

- Make sure you sign the academic honesty statement on the next page.

Academic Honesty Statement

I agree to abide by the UH Academic Honesty Policy during this exam. I understand that the punishment for violating this policy will be most severe, including the possibility of getting an F in the class and/or getting expelled from the University.

_______________________________________________

Signature

Grading (for instructor use only)

_____/60  Prob. 1

_____/40  Prob. 2

_____/40  Prob. 3

_____/40  Prob. 4

_____/20  Prob. 5

Prob.1

An infinite solid wire of radius a carries a current I [A] in the z direction as shown below.  Because the current is a DC current, you may assume that it is distributed uniformly inside the cross section of the wire. Assume that the wire is nonmagnetic ().

a) Find the magnetic field vector H in the region  (inside the wire).

b) Find the magnetic stored energy in a length L of the wire.

c) Use the energy formula to calculate the inductance for a length L of the wire.

ROOM FOR WORK

Prob. 2

Consider two conducting bodies as shown below. It is desired to determine the capacitance C between them, when there is free space surrounding the conductors.

In order to determine the capacitance, an engineer immerses the two bodies in a large tank of water. The engineer measures a resistance of R between the two conductors when they are inside the tank.

The engineer then puts the same water into a testing cell as shown below, and measures a resistance of Rc between the two plates. The testing cell consists of two metal plates of area A [m2] separated by a distance h, with water between the two plates.

Find an expression for the capacitance C between the original two bodies in free space. Your answer should be in terms of R, Rc, A, and h.

Do this by using the capacitance-resistance analogy principle, which states that

.

In this formula G is the conductance between any two bodies when surrounded by a medium of conductivity (, and C is the capacitance between the same two bodies when surrounded by a dielectric of permittivity (.

ROOM FOR WORK

Prob. 3

A current I flows in a triangular loop as shown below. (The vertices of the equilateral triangle are labeled in the figure.) Find the magnetic field vector H at the point r that is located at the center of the loop, given by

.

ROOM FOR WORK

Prob. 4

Three spherical shells of uniform charge density in free space are arranged as shown below. The total charges on the shells are labeled in the figure. The inner shell has a total charge of Q [C], while each of the other two shells have a total charge of –Q/2 [C]. Determine the stored energy in the system.

ROOM FOR WORK

Prob. 5

Five point charges of 1 [C] are located at the vertices of a hexagon as shown below. One of the vertices of the hexagon does not have a point charge. This vertex is located at the point (1, 0 ,0).

Find the electric field vector at the origin.

ROOM FOR WORK

# Text boxes

-Q/2

-Q/2

Q

c

b

a

I

r

y

(1,0,0)

y

x

A

water

testing cell

h

B

A

I

a

x

z