Name:  _____________________________ (please print)

Signature: __________________________

Circle your class time:    10-11:30 PM, TuTh          11:30AM - 1PM, MW

DO NOT OPEN THIS BOOKLET UNTIL INSTRUCTED TO DO SO

ECE 3455 – Electronics

Exam 1

## February 28, 2004

1.  This exam is closed book.  You may have a crib sheet consisting of one 8½” x 11” sheet of paper written on both sides (or the equivalent area on another medium).  You may use any calculator, but no computers or laptops are allowed.

2.  Show all work necessary to complete the problem on these pages.  If you go on to another page, indicate clearly where your work can be found.  A solution without the work shown will receive no credit.

- Show all units in expressions and figures.

- Do not use red ink.  Do not use red pencil.

- You will have 90 minutes to work on this exam.

1  ________________/1

2 ________________/35

3 ________________/30

4 ________________/35

Total ________________/101

1)  {1 Point} On the front page, circle your class time.

Room for extra work

2)  {35 Points}  Three identical transresistance amplifiers, of the type shown in Figure 2, are connected together as shown in Figure 1.  Note that the numbers indicate the exact position of each of the terminals.

- Find the transconductance, .

- Find the input resistance seen by the source.

- Find the output resistance seen by the load.

- Find the equivalent transconductance amplifier, as seen by the source and the load.  Draw this equivalent, attach the source and load, and label il and vi.

Room for extra work

3)  {30 Points}  For the circuit shown below, find the poles and zeroes of the transfer function,  .  Indicate whether the poles or zeroes are multiple poles or zeroes, and how many there are at each frequency.

Room for extra work

4)  {35 Points}  The straight-line approximation to the phase Bode plot for a circuit is shown below.  It is known that

It is also known that all of the poles and zeroes for this circuit are in the range

,

except for two poles at  = 0.

Use the blank semi-log graph paper, on the page that follows the phase plot, to plot the straight-line approximation to the magnitude Bode plot for this circuit.  A spare copy of the semi-log graph paper is provided, in case you need it.  If you need to make any calculations, please show these calculations below.  At a minimum, please indicate in the space below the location of all poles and zeroes in this frequency range.

Solutions:

2)  {35 Points}  Three identical transresistance amplifiers, of the type shown in Figure 2, are connected together as shown in Figure 1.  Note that the numbers indicate the exact position of each of the terminals.

- Find the transconductance, .

- Find the input resistance seen by the source.

- Find the output resistance seen by the load.

- Find the equivalent transconductance amplifier, as seen by the source and the load.  Draw this equivalent, attach the source and load, and label il and vi.

See next page.

3)  {30 Points}  For the circuit shown below, find the poles and zeroes of the transfer function,  .  Indicate whether the poles or zeroes are multiple poles or zeroes, and how many there are at each frequency.

4)  {35 Points}  The straight-line approximation to the phase Bode plot for a circuit is shown below.  It is known that

It is also known that all of the poles and zeroes for this circuit are in the range

,

except for two poles at  = 0.

Use the blank semi-log graph paper, on the page that follows the phase plot, to plot the straight-line approximation to the magnitude Bode plot for this circuit.  A spare copy of the semi-log graph paper is provided, in case you need it.  If you need to make any calculations, please show these calculations below.  At a minimum, please indicate in the space below the location of all poles and zeroes in this frequency range.

The plot below is drawn starting at the right side, and working left, since that is where we were given a value for the magnitude of the transfer function.  On the far right, having passed z3, we know that the slope is zero, since we have passed three poles and three zeroes.

In the frequency range between p3 and z3, we must have a slope of –20[dB/dec].  To the left of that the slope must be zero, and to the left of z1 and z2, the slope must be –40[dB/dec], due to the two poles at  = 0.  We draw a succession of straight lines, using these slopes, to get the plot that follows.