5)  (18 Points)  A digital logic family has the characteristics described below.

a)  The output appears as the equivalent circuit in Fig. 7 when the output is in the high state.  The output appears the equivalent circuit in Fig. 8 when the output is in the low state.

b)  The input appears as the equivalent circuit in Fig. 9 when the input is in the high state.  The input appears the equivalent circuit in Fig. 10 when the input is in the low state.

c)  The gate dissipates 250[mW] when the output is in the high state, and dissipates 240[mW] when the output is in the low state.

d)  Assume room temperature operation,  = 100, and VA = .

e)  The lowest input voltage that behaves like a high input is 2[V].  The highest input voltage that behaves like a low input is -2[V].

Find the fanout for high and low noise margins of 1[V].