## Slide 1
Prof. David R. Jackson
Dept. of ECE
Notes 1
ECE 5317-6351
Microwave Engineering
Fall 2019
Waveguiding Systems
Adapted from notes by Prof. Jeffery T. Williams

## Slide 2
A waveguiding structure is one that carries a signal (or power) from one point to another.
There are three common types:
Transmission lines
Fiber-optic guides
Waveguides
Waveguiding Structures
Note:
An alternative to using waveguiding structures is wireless transmission using antennas.
(Wireless systems are discussed later. Antennas are discussed in ECE 5318.)

## Slide 3
Transmission Line
Has two conductors running parallel (one can be inside the other)
Can propagate a signal at any frequency (in theory)
Becomes lossy at high frequency
Can handle low or moderate amounts of power
Does not have signal distortion, unless there is loss (but there always is)
May or may not be immune to interference (shielding property)
Does not have Ez or Hz components of the fields (TEMz)
Properties
Coaxial cable (coax)
Twin lead
(shown connected to a 4:1 impedance-transforming balun)

## Slide 4
Transmission Line (cont.)
CAT 5 cable
(twisted pair)
The two wires of the transmission line are twisted to reduce interference and radiation from discontinuities.

## Slide 5
Transmission Line (cont.)
Transmission lines commonly met on printed-circuit boards
Microstrip
Stripline
Coplanar strips
Coplanar waveguide (CPW)

## Slide 6
Transmission Line (cont.)
Transmission lines are commonly met on printed-circuit boards.
A microwave integrated circuit.
Microstrip line

## Slide 7
Waveguides
Consists of a single hollow metal pipe
Can propagate a signal only at high frequency: f > fc
The width must be at least one-half of a wavelength
Has signal distortion, even in the lossless case
Immune to interference
Can handle large amounts of power
Has low loss (compared with a transmission line)
Has either Ez or Hz component of the fields (TMz or TEz)
Properties
http://en.wikipedia.org/wiki/Waveguide_(electromagnetism)

## Slide 8
Fiber-Optic Guide
Properties
Uses a dielectric rod
Operates at optical (infrared) frequencies
Can be made to have very low loss
Has minimal signal distortion
Has a very high bandwidth
Very immune to interference
Not suitable for high power
Has both Ez and Hz components of the fields (“hybrid mode”)

## Slide 9
Fiber-Optic Guide (cont.)
Two types of fiber-optic guides:
1) Single-mode fiber
2) Multi-mode fiber
Carries a single mode, as with the mode on a transmission line or waveguide. Requires the fiber diameter to be small relative to a wavelength.
Has a fiber diameter that is large relative to a wavelength. It operates on the principle of total internal reflection (critical angle effect).
Note: The carrier is at optical frequency, but the modulating (baseband) signal is often at microwave frequencies (e.g., TV, internet signal).

## Slide 10
Fiber-Optic Guide (cont.)
http://en.wikipedia.org/wiki/Optical_fiber
Higher index core region
Multi-mode Fiber