## Slide 1
Prof. David R. Jackson
Dept. of ECE
Notes 11
ECE 5317-6351
Microwave Engineering
Fall 2019
Waveguiding Structures Part 6:
Planar Transmission Lines
Adapted from notes by Prof. Jeffery T. Williams

## Slide 2
Planar Transmission Lines
er
Microstrip
er
Stripline
w
er
Coplanar Waveguide (CPW)
w
er
Conductor-backed CPW
er
Slotline
er
Conductor-backed Slotline

## Slide 3
Planar Transmission Lines (cont.)
Stripline is a planar version of coax.
Coplanar strips (CPS) is a planar version of twin lead.
er
Coplanar Strips (CPS)
er
Conductor-backed CPS

## Slide 4
Stripline
Common on circuit boards
Fabricated with two circuit boards
Homogenous dielectric
(perfect TEM mode*)
Field structure for TEM mode:
(also TE & TM Modes at high frequency)
TEM mode
Electric Field
Magnetic Field
* The mode is a perfect TEM mode if there is no conductor loss.

## Slide 5
Analysis of stripline is not simple.
TEM mode fields can be obtained from an electrostatic analysis (e.g., conformal mapping).
Stripline (cont.)
A closed stripline structure is analyzed in the Pozar book by using an approximate numerical method:
(to simulate stripline)

## Slide 6
Conformal Mapping Solution (R. H. T. Bates)
K = complete elliptic integral of the first kind
Exact solution (for t = 0):
Stripline (cont.)
R. H. T. Bates, “The characteristic impedance of the shielded slab line,” IEEE Trans. Microwave Theory and Techniques, vol. 4, pp. 28-33, Jan. 1956.

## Slide 7
Curve fitting this exact solution:
Effective width
Stripline (cont.)
Note:
The factor of 1/2 in front is from the parallel combination of two ideal PPWs.
Fringing term

## Slide 8
Inverting this solution to find w for given Z0:
Stripline (cont.)

## Slide 9
Attenuation
Dielectric Loss:
Stripline (cont.)
(TEM formula)

## Slide 10
Stripline (cont.)
Conductor Loss:
Note: We cannot let t  0 when we calculate the conductor loss.

## Slide 11
Stripline (cont.)
Note about conductor attenuation:
It is necessary to assume a nonzero conductor thickness in order to accurately calculate the conductor attenuation.
The perturbational method predicts an infinite attenuation if a zero thickness is assumed.
Practical note:
A standard metal thickness for PCBs is 0.7 [mils] (17.5 [m]), called “half-ounce copper”.
1 mil = 0.001 inch

## Slide 12
Inhomogeneous dielectric
 No TEM mode
TEM mode would require kz = k in each region, but kz must be unique!
Requires advanced analysis techniques
Exact fields are hybrid modes (Ez and Hz)
For h /0 << 1, the dominant mode is quasi-TEM.
Microstrip
Note: Pozar uses (W, d)

## Slide 13
Microstrip (cont.)
Figure from Pozar book
Part of the field lines are in air,
and part of the field lines are inside the substrate.
Note:
The flux lines get more concentrated in the substrate region as the frequency increases.

## Slide 14
Equivalent TEM problem:
Microstrip (cont.)
The effective permittivity gives the correct phase constant.
The effective strip width gives the correct Z0.
Equivalent TEM problem
Actual problem

## Slide 15
Microstrip (cont.)
Effective permittivity:
Limiting cases:
(narrow strip)
(wide strip)
Note:
This formula ignores “dispersion”, i.e., the fact that the effective permittivity is actually a function of frequency.

## Slide 16
Microstrip (cont.)
Characteristic Impedance:
Note:
This formula ignores the fact that the characteristic impedance is actually a function of frequency.

## Slide 17
Inverting this solution to find w for a given Z0:
where
Microstrip (cont.)

## Slide 18
More accurate formulas for characteristic impedance that account for dispersion (frequency variation) and conductor thickness:
Microstrip (cont.)

## Slide 19
Microstrip (cont.)
where
Note:

## Slide 20
Microstrip (cont.)
“A frequency-dependent solution for microstrip transmission lines," E. J. Denlinger, IEEE Trans. Microwave Theory and Techniques, Vol. 19, pp. 30-39, Jan. 1971.
Note:
The flux lines get more concentrated in the substrate region as the frequency increases.
Quasi-TEM region
Frequency variation
(dispersion)
Effective dielectric constant
7.0
8.0
9.0
10.0
11.0
12.0
Parameters: r = 11.7, w/h = 0.96, h = 0.317 cm
Frequency (GHz)
Note:
The phase velocity is a function of frequency, which causes pulse distortion.

## Slide 21
Attenuation
Dielectric loss:
“filling factor”
very crude (“parallel-plate”) approximation
Conductor loss:
Microstrip (cont.)
(More accurate formulas are given on next slide.)

## Slide 22
Microstrip (cont.)
More accurate formulas for conductor attenuation:
This is the number e = 2.71828 multiplying the term in parenthesis.

## Slide 23
Microstrip (cont.)
REFERENCES
L. G. Maloratsky, Passive RF and Microwave Integrated Circuits, Elsevier, 2004.
I. Bahl and P. Bhartia, Microwave Solid State Circuit Design, Wiley, 2003.
R. A. Pucel, D. J. Masse, and C. P. Hartwig, “Losses in Microstrip,” IEEE Trans. Microwave Theory and Techniques, pp. 342-350, June 1968.
R. A. Pucel, D. J. Masse, and C. P. Hartwig, “Corrections to ‘Losses in Microstrip’,” IEEE Trans. Microwave Theory and Techniques, Dec. 1968, p. 1064.

## Slide 24
TXLINE
This is a public-domain software for calculating the properties of some common planar transmission lines.
https://www.awr.com/software/options/tx-line