## Slide 1
Notes 21
ECE 5317-6351
Microwave Engineering
Fall 2019
Prof. David R. Jackson
Dept. of ECE
Quadrature Coupler and
Rat-Race Coupler
Adapted from notes by Prof. Jeffery T. Williams

## Slide 2
Quadrature (90o) Coupler
“A quadrature coupler is one in which the input is split into two signals (usually with a goal of equal magnitudes) that are 90 degrees apart in phase. Types of quadrature couplers include branchline couplers (also known as quadrature hybrid* couplers), Lange couplers and overlay couplers.”
http://www.microwaves101.com/encyclopedia/Quadrature_couplers.cfm
Taken from “Microwaves 101”
This coupler is very useful for obtaining circular polarization:
There is a 90o phase difference between ports 2 and 3.
Note:
The term “hybrid” denotes the fact that there is an equal (3 dB) power split to the output ports.

## Slide 3
90o Coupler
1
2
4
3
The quadrature hybrid is a lossless 4-port (the S matrix is unitary ).
All four ports are matched.
The device is reciprocal (the S matrix is symmetric.)
Port 4 is isolated from port 1, and ports 2 and 3 are isolated from each other.
Quadrature Coupler (cont.)

## Slide 4
The signal from port 1 splits evenly between ports 2 and 3, with a 90o phase difference.
The signal from port 4 splits evenly between ports 2 and 3, with a -90o phase difference.
The quadrature coupler is usually used as a splitter:
90o Coupler
1
2
4
3
+90o out of phase
2- 3 = 90o
-90o out of phase
2- 3 = -90o
Can be used to produce right-handed circular polarization.
Can be used to produce left-handed circular polarization.
Quadrature Coupler (cont.)
Note: A matched load is usually placed on port 4.

## Slide 5
Branch-Line Coupler
A microstrip realization of a quadrature hybrid (branch-line coupler) is shown here.
Notes:
We only need to study what happens when we excite port 1, since the structure is physically symmetric.
We use even/odd mode analysis (exciting ports 1 and 4) to figure out what happens when we excite port 1.
Quadrature Coupler (cont.)
An analysis of the branch-line coupler is given in the Appendix.

## Slide 6
Summary
Quadrature Coupler (cont.)
The input power to port 1 divides evenly between ports 2 and 3, with ports 2 and 3 being 90o out of phase.
Note: A matched load is usually placed on port 4.

## Slide 7
Quadrature Coupler (cont.)
A coupled-line coupler is one that uses coupled lines (microstrip, stripline) with no direct connection between all of the ports.
Please see the Pozar book for more details.
Port 1
Port 2
Port 3
Port 4
This coupler has a 90o phase difference between the output ports (ports 2 and 3), and can be used to obtain an equal (-3 dB) power split or another split ratio.

## Slide 8
Quadrature Coupler (cont.)
One feed port produces RHCP, the other feed port produced LHCP.
Circularly-polarized microstrip antennas can be fed with a 90o coupler.
Note: This is a better way (higher bandwidth) to get CP than with a simple 90o delay line.

## Slide 9: Photograph of a microstrip ring coupler Courtesy of M. D. Abouzahra, MIT Lincoln Laboratory
Rat-Race Ring Coupler (180o Coupler)
http://www.microwaves101.com/encyclopedia/ratrace_couplers.cfm
Taken from “Microwaves 101”
“Applications of rat-race couplers are numerous, and include mixers and phase shifters. The rat-race gets its name from its circular shape, shown below.”

## Slide 10
180o Coupler
1
2
4
3
The rat race is a lossless 4-port (the S matrix is unitary).
All four ports are matched.
The device is reciprocal (the S matrix is symmetric).
Port 4 is isolated from port 1, and ports 2 and 3 are isolated from each other.
Rat-Race Coupler (cont.)

## Slide 11
The signal from the “sum port”  (port 1) splits evenly between ports 2 and 3, in phase. This could be used as a power splitter (alternative to Wilkinson).
The rat race can be used as a splitter:
180o Coupler
1
2
4
3
In phase


180o out of phase
Note: A matched load is usually placed on port 4.
Rat-Race Coupler (cont.)
The signal from the “difference port”  (port 4) splits evenly between ports 1 and 2, 180o out of phase. This could be used as a balun.

## Slide 12
The signal from the sum port  (port 1) is the sum of the input signals 1 and 2.
The rat race can be used as a combiner:
180o Coupler
1
2
4
3


Signal 1 (V1)
Signal 2 (V2)
Rat-Race Coupler (cont.)
The signal from the difference port  (port 4) is the difference of the input signals 1 and 2.

## Slide 13
A microstrip realization is shown here.
Rat-Race Coupler (cont.)
An analysis of the rat-race coupler is given in the Appendix.

## Slide 14
Magic T
A waveguide realization of a 180o coupler is shown here, called a “Magic T.”
“Magic T”
Note the logo!
IEEE Microwave Theory and Techniques Society
Note: Irises are usually used to obtain matching at the ports.

## Slide 15
Monopulse Radar
Rat-Race couplers are often used in monpulse radar.
Four antennas
https://www.microwaves101.com/encyclopedias/monopulse-comparator-networks
Rat-Race:
Input from A
Input from B
Input from C
Input from D

## Slide 16
Monopulse Radar (cont.)
The difference signals are used to determine the azimuth and elevation of the target.
https://www.microwaves101.com/encyclopedias/monopulse-comparator-networks
The difference between the two antenna signals maps into the phase difference , which maps into the angle .

## Slide 17
Port 1 Excitation
“even” analysis

Appendix A
Here we analyze the quadrature coupler.
Input admittance of open-circuited stub:

## Slide 18
Port 1 Excitation
“odd” problem
Appendix A (cont.)

Input admittance of short-circuited stub:

## Slide 19
Consider the general case:
Quarter-wave line
Shunt load on line
.
In general:
Appendix A (cont.)

## Slide 20
Hence we have:
Appendix A (cont.)

## Slide 21
Continuing with the algebra, we have:
Appendix A (cont.)

## Slide 22
Hence we have:
Convert this to S parameters (use Table 4.2 in Pozar):
Note:
We are describing a two-port device here, in the even and odd mode cases.
Appendix A (cont.)
This is a 22 matrix, not a 44 matrix.

## Slide 23
Hence
By symmetry:
Appendix A (cont.)
Adding even and odd mode cases together:

## Slide 24
By symmetry and reciprocity:
Appendix A (cont.)

## Slide 25
By symmetry and reciprocity:
Appendix A (cont.)

## Slide 26
By symmetry and reciprocity:
Appendix A (cont.)

## Slide 27
Layout
Schematic
Here we analyze the Rat-Race Ring coupler.
Appendix B

## Slide 28
Port 1 Excitation
“even” problem

Appendix B (cont.)

## Slide 29

Appendix B (cont.)
Port 1 Excitation
“odd” problem

## Slide 30
Proceeding as for the 90o coupler, we have:
Appendix B (cont.)

## Slide 31
Converting from the ABCD matrix to the S matrix, we have:
Use Table 4.2 in Pozar
Note:
We are describing a two-port device here, in the even and odd mode cases.
Appendix B (cont.)
This is a 22 matrix, not a 44 matrix.

## Slide 32
For the S parameters coming from port 1 excitation, we then have:
Appendix B (cont.)

## Slide 33
Similarly, exciting port 2, and using symmetry and reciprocity, we have the following results (derivation omitted):
Appendix B (cont.)