## Slide 1
Prof. David R. Jackson
Dept. of ECE
Notes 6
ECE 5317-6351
Microwave Engineering
Fall 2019
Waveguiding Structures
Part 1: General Theory
Adapted from notes by Prof. Jeffery T. Williams

## Slide 2
In general terms, a waveguiding system is a system that confines electromagnetic energy and channels it from one point to another.
(This is opposed to a wireless system that uses antennas.)
Examples
Coax
Twin lead (twisted pair)
Printed circuit lines (e.g. microstrip)
Parallel plate waveguide
Rectangular waveguide
Circular waveguide
Waveguide Introduction
Note: In microwave engineering, the term “waveguide” is often used to mean rectangular or circular waveguide (i.e., a hollow pipe of metal).
Waveguides
Optical fiber (dielectric waveguide)
Transmission Lines

## Slide 3
General Notation for Waveguiding Systems
Assume ejt time dependence and homogeneous source-free materials.
Assume wave propagation in the  z direction:
Transverse (x,y) components
Note: Lower case letters denote 2-D fields (the z term is suppressed).
Example of waveguiding system (a waveguide)

## Slide 4
Helmholtz Equation
(complex)
where

## Slide 5
Helmholtz Equation
Vector Laplacian definition:
where

## Slide 6
Next, we examine the term on the right-hand side.
Helmholtz Equation (cont.)
So far we have:

## Slide 7
To do this, start with Ampere’s law:
In the time-harmonic (sinusoidal) steady state, there can never be any volume charge density inside of a linear, homogeneous, isotropic, source-free region that obeys Ohm’s law.
Helmholtz Equation (cont.)

## Slide 8
Vector Helmholtz equation
Hence, we have
Helmholtz Equation (cont.)

## Slide 9
Similarly, for the magnetic field, we have
Helmholtz Equation (cont.)

## Slide 10
Hence, we have
Helmholtz Equation (cont.)
Vector Helmholtz equation

## Slide 11
Summary
These equations are valid for a source-free, homogeneous, isotropic, linear material.
Vector Helmholtz equation
Helmholtz Equation (cont.)

## Slide 12
From the property of the vector Laplacian, we have
Recall:
Scalar Helmholtz equation
Helmholtz Equation (cont.)

## Slide 13
Assume a guided wave with a field variation F(z) in the z direction of the form
Field Representation
Then all four of the transverse (x and y) field components can be expressed in terms of the two longitudinal ones:
(This is a property of any guided wave.)

## Slide 14
Assume a source-free region with a variation
Field Representation: Proof
Take (x,y,z) components

## Slide 15
Combining 1) and 5):
Cutoff wavenumber
(real number, as discussed later)
Field Representation: Proof (cont.)
A similar derivation holds for the other three transverse field components.

## Slide 16
Summary of Results
These equations give the transverse field components in terms of the longitudinal components, Ez and Hz.
Field Representation (cont.)

## Slide 17
Therefore, we only need to solve the Helmholtz equations for the longitudinal field components (Ez and Hz).
Field Representation (cont.)
From table

## Slide 18
Types of guided waves:
Types of Waveguiding Systems
TEMz: Ez = 0, Hz = 0
TMz: Ez  0, Hz = 0
TEz: Ez = 0, Hz  0
Hybrid: Ez  0, Hz  0
Microstrip
h
w
er
TEMz
TMz , TEz
Hybrid
Hybrid

## Slide 19
Waveguides
Two types of modes: TEz , TMz
We assume that the boundary is PEC.
We assume that the inside is filled with a homogenous isotropic linear material (could be air)
An example of a waveguide
(rectangular waveguide)

## Slide 20
Transverse Electric (TEz) Waves
In general, Ex, Ey, Hx, Hy, Hz  0
To find the TEz field solutions (away from any sources), solve
The electric field is “transverse” (perpendicular) to z.
or

## Slide 21
Recall that the field solutions we seek are assumed to vary as
Transverse Electric (TEz) Waves (cont.)

## Slide 22
We need to solve the eigenvalue problem subject to the appropriate boundary conditions.
Transverse Electric (TEz) Waves (cont.)
(2D Eigenvalue problem)
(A proof of this may be found in the ECE 6340 notes.)
For this type of eigenvalue problem, the eigenvalue is always real.
Change notation

## Slide 23
Transverse Electric (TEz) Waves (cont.)
Hence, TEz modes exist inside of a waveguide (conducting pipe).
Neumann boundary condition
A solution to the eigenvalue problem can always be found for a PEC boundary (proof omitted).
Neumann boundary condition (see below)

## Slide 24
Once the solution for Hz is obtained, we use
TE wave impedance
For a wave propagating in the positive z direction (top sign):
Transverse Electric (TEz) Waves (cont.)
For a wave propagating in the negative z direction (bottom sign):

## Slide 25
For a wave propagating in the positive z direction, we also have:
Similarly, for a wave propagating in the negative z direction,
Transverse Electric (TEz) Waves (cont.)

## Slide 26
Summarizing both cases, we have
+ sign: wave propagating in the + z direction
- sign: wave propagating in the - z direction
Transverse Electric (TEz) Waves (cont.)

## Slide 27
Transverse Magnetic (TMz) Waves
In general, Ex, Ey, Ez ,Hx, Hy  0
To find the TEz field solutions (away from any sources), solve
or
The magnetic field is “transverse” (perpendicular) to z.

## Slide 28
Transverse Magnetic (TMz) Waves (cont.)
Recall that the field solutions we seek are assumed to vary as

## Slide 29
We need to solve the eigenvalue problem subject to the appropriate boundary conditions.
Transverse Electric (TEz) Waves (cont.)
(Eigenvalue problem)
(A proof of this may be found in the ECE 6340 notes.)
For this type of eigenvalue problem, the eigenvalue is always real.

## Slide 30
Transverse Magnetic (TMz) Waves (cont.)
A solution to the eigenvalue problem can always be found for a PEC boundary
(proof omitted).
Dirichlet boundary condition
Hence, TMz modes exist inside of a waveguide (conducting pipe).
Dirichlet boundary condition (see below)

## Slide 31
TM wave impedance
Once the solution for Ez is obtained, we use
For a wave propagating in the positive z direction (top sign):
For a wave propagating in the negative z direction (bottom sign):
Transverse Magnetic (TMz) Waves (cont.)

## Slide 32
For a wave propagating in the positive z direction, we also have:
Similarly, for a wave propagating in the negative z direction,
Transverse Magnetic (TMz) Waves (cont.)

## Slide 33
Summarizing both cases, we have
+ sign: wave propagating in the + z direction
- sign: wave propagating in the - z direction
Transverse Magnetic (TMz) Waves (cont.)

## Slide 34
Transverse ElectroMagnetic (TEM) Waves
From the previous table for the transverse field components, all of them are equal to zero if Ez and Hz are both zero.
Unless
For TEM waves
In general, Ex, Ey, Hx, Hy  0
Hence, we have

## Slide 35
Transverse ElectroMagnetic (TEM) Waves (cont.)
From EM boundary conditions, we have:
so
The current flows purely in the z direction.

## Slide 36
In a linear, isotropic, homogeneous source-free region,
In rectangular coordinates, we have
Notation:
Transverse ElectroMagnetic (TEM) Waves (cont.)
Hence, we have

## Slide 37
Also, for the TEMz mode, we have from Faraday’s law (taking the z component):
Note:
Using the formula for the z component of the curl of E, we have:
Hence
Transverse ElectroMagnetic (TEM) Waves (cont.)
Hence, we have:

## Slide 38
Hence
Transverse ElectroMagnetic (TEM) Waves (cont.)

## Slide 39
Since the potential function that describes the electric field in the cross-sectional plane is two dimensional, we can drop the “t” subscript if we wish:
Boundary Conditions:
This is enough to make the potential function unique.
Hence, the potential function is the same for DC as it is for a high-frequency microwave signal.
Transverse ElectroMagnetic (TEM) Waves (cont.)
The field of a TEM mode does not change shape with frequency:
it has the same shape as a DC field.
a
b
PEC conductors

## Slide 40
Notes:
A TEMz mode has an electric field that has exactly the same shape as a static (DC) field. (A similar proof holds for the magnetic field.)
This implies that the C and L for the TEMz mode on a transmission line are independent of frequency.
This also implies that the voltage drop between the two conductors of a transmission line carrying a TEMz mode is path independent.
A TEMz mode requires two or more conductors: a static electric field cannot exist inside of a waveguide (hollow metal pipe) due to the Faraday cage effect.
Transverse ElectroMagnetic (TEM) Waves (cont.)

## Slide 41
For a TEM mode, both wave impedances are the same:
Transverse ElectroMagnetic (TEM) Waves (cont.)
Note:  is complex for lossy media.

## Slide 42
TEM Solution Process
A) Solve Laplace’s equation subject to appropriate B.C.s.:
B) Find the transverse electric field:
C) Find the total electric field:
D) Find the magnetic field:
Note: The only frequency dependence is in the wavenumber kz = k.

## Slide 43
Note on Lossy Transmission Line
A TEM mode can have an arbitrary amount of dielectric loss.
A TEM mode cannot have conductor loss.
Inside conductors:
+ + + + + + +
- - - - - - - - - -
In practice, a small conductor loss will not change the shape of the fields too much, and the mode is approximately TEM.
If there is conductor loss,
there must be an Ez field.

## Slide 44
If there is only dielectric loss (an exact TEM mode):
Equate real and imaginary parts
Note on Lossy Transmission Line (cont.)

## Slide 45
From these two equations we have:
Equations for a TEM mode:
Note:
These formulas were assumed previously in Notes 3.
Note on Lossy Transmission Line (cont.)

## Slide 46
This general formula accounts for both dielectric and conductor loss:
Dielectric loss
Conductor loss
When R is present the mode is not exactly TEM, but we usually ignore this.
Note on Lossy Transmission Line (cont.)

## Slide 47
Summary
TEM Mode:

## Slide 48
Summary (cont.)
Transmission line mode (approximate TEM mode):
The mode requires two conductors.
The mode is purely TEM only when R = 0.

## Slide 49
Summary (cont.)
TEz Mode:
kc = real number (depends on geometry and mode number)
The mode can exist inside of a single pipe (waveguide).

## Slide 50
TMz Mode:
kc = real number (depends on geometry and mode number)
Summary (cont.)
The mode can exist inside a single pipe (waveguide).