ELEE 6340

FALL 1996

CLASS PROJECT

A microstrip patch antenna is shown below.

Assume that L is the resonant dimension of the patch, so that the surface current is

.

Give a detailed derivation of the far-field radiation pattern of the patch antenna. Show how to calculate the electric field radiated in the far-field and the power density in the far-field.

Write a computer program to calculate the far-field power pattern in dB. The pattern should be normalized so that the pattern has a value of 0 dB at the maximum. Include a hard copy of your program in an appendix.

Calculate and plot the E-plane (( = 0o) and H-plane (( = 90o) patterns for a patch with the following parameters:

patch parameters:

Make plots for the following substrate thicknesses:

.

Your plots should be in polar form, on a dB scale. Use -40 dB for the value at the center of your plot. Your plot should show the pattern for .

For each plot, include an output data file that shows the dB values at each angle in degrees, for ( = 0, 1, 2, ... 90o.  Remember that 0 dB should be the maximum.

Include a discussion of your results, commenting on the main features of the plots and how they change with substrate thickness.

The grading of the project will be based mainly on the following:

The accuracy of the plots and output data.

The quality and neatness of the write-up section, showing the derivation.

The quality and neatness of the plots.

The quality of the discussion about your results.