ECE 6341

Spring 2009

Project

Project Description

A microstrip antenna is placed on the surface of a rocket (see the figure below). The center of the patch is located on the x axis. The two radiating edges of the microstrip antenna are modeled as two slots, each having a one volt drop (V = 1) across the edge, measured from bottom to top. Therefore, for each slot the electric field is given by

,

where ( is the width of each slot. The slots may be assumed to be of infinitesimal width, so that . The electric field is assumed to be uniform across the width of the patch, in the ( direction.  The length of the microstrip antenna is L in the z direction (the two radiating edges, or slots, are located at z = L/2 and z = -L/2), and the width of the patch is W in the ( direction (the angle subtended by the two nonradiating edges is (( = W / a, with the slot fields existing in the region - (( / 2 < ( < (( / 2).

Assume the following parameters: f = 10 GHz, ,  with and .

Project Tasks:

- Determine the far field pattern components E( (r, (, () and E( (r, (, ().

- Write a program (in Mathcad, Matlab, Mathematica, Fortran, etc.) to calculate the radiation pattern |E(| versus ( for ( = ( / 2 (the xy plane). Make a polar plot of the normalized pattern |E(| (normalized to a value of 1.0 at the peak) for 0 < ( < 2(. Plot the normalized pattern in dB, so that the pattern is zero dB at the peak.

- Make a polar plot of the normalized pattern |E(| in dB for 1o < ( < 179o, for ( = 0 (the xz plane) for the same case as above. What happens to the far-field pattern as ( (  0 or (? Look at the formulation for E(  to explain your conclusion.

- Repeat parts (2) and (3) for a “wraparound” microstrip antenna, which has the same length L but the width W is now equal to the circumference of the rocket, so that W = 2(a.

Computational Note:

Please check to make sure that you have convergence in your summations when you calculate the far-field patterns!

# Text boxes

a

x

# L

# W

y

z