## Slide 1
Introduction to Microstrip Antennas
David R. Jackson
Dept. of ECE
University of Houston

## Slide 2
David R. Jackson
Dept. of ECE
N308 Engineering Building 1
University of Houston
Houston, TX 77204-4005
Phone: 713-743-4426
Fax: 713-743-4444
Email: djackson@uh.edu
Contact Information

## Slide 3
Purpose of Short Course
Provide an introduction to microstrip antennas.
Provide a physical and mathematical basis for understanding how microstrip antennas work.
Provide a physical understanding of the basic physical properties of microstrip antennas.
Provide an overview of some of the recent advances and trends in the area (but not an exhaustive survey – directed towards understanding the fundamental principles).

## Slide 4
Additional Resources
Some basic references are provided at the end of these viewgraphs.
You are welcome to visit a website that goes along with a course at the University of Houston on microstrip antennas (PowerPoint viewgraphs from the course may be found there, along with the viewgraphs from this short course).
ECE 6345: Microstrip Antennas
http://courses.egr.uh.edu/ECE/ECE6345/
Note:
You are welcome to use anything that you find on this website,
as long as you please acknowledge the source.

## Slide 5
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 6
Notation

## Slide 7
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 8
Overview of Microstrip Antennas
Also called “patch antennas”
One of the most useful antennas at microwave frequencies (f > 1 GHz).
It usually consists of a metal “patch” on top of a grounded dielectric substrate.
The patch may be in a variety of shapes, but rectangular and circular are the most common.
Microstrip line feed
Coax feed

## Slide 9
Overview of Microstrip Antennas
Common Shapes
Rectangular
Square
Circular
Elliptical
Annular ring
Triangular

## Slide 10
Invented by Bob Munson in 1972 (but earlier work by Dechamps goes back to 1953).
Became popular starting in the 1970s.
G. Deschamps and W. Sichak, “Microstrip Microwave Antennas,” Proc. of Third Symp. on USAF Antenna Research and Development Program, October 18–22, 1953.
R. E. Munson, “Microstrip Phased Array Antennas,” Proc. of Twenty-Second Symp. on USAF Antenna Research and Development Program, October 1972.
R. E. Munson, “Conformal Microstrip Antennas and Microstrip Phased Arrays,” IEEE Trans. Antennas Propagat., vol. AP-22, no. 1 (January 1974): 74–78.
Overview of Microstrip Antennas
History

## Slide 11
Advantages of Microstrip Antennas
Low profile (can even be “conformal,” i.e. flexible to conform to a surface).
Easy to fabricate (use etching and photolithography).
Easy to feed (coaxial cable, microstrip line, etc.).
Easy to incorporate with other microstrip circuit elements and integrate into systems.
Patterns are somewhat hemispherical, with a moderate directivity (about 6-8 dB is typical).
Easy to use in an array to increase the directivity.
Overview of Microstrip Antennas

## Slide 12
Disadvantages of Microstrip Antennas
Low bandwidth (but can be improved by a variety of techniques). Bandwidths of a few percent are typical. Bandwidth is roughly proportional to the substrate thickness and inversely proportional to the substrate permittivity.
Efficiency may be lower than with other antennas. Efficiency is limited by conductor and dielectric losses*, and by surface-wave loss**.
Only used at microwave frequencies and above (the substrate becomes too large at lower frequencies).
Cannot handle extremely large amounts of power (dielectric breakdown).
* Conductor and dielectric losses become more severe for thinner substrates.
** Surface-wave losses become more severe for thicker substrates (unless air or foam is used).
Overview of Microstrip Antennas

## Slide 13
Applications
Satellite communications
Microwave communications
Cell phone antennas
GPS antennas
Applications include:
Overview of Microstrip Antennas

## Slide 14
Microstrip Antenna Integrated into a System: HIC Antenna Base-Station for 28-43 GHz
Filter
Diplexer
LNA
PD
K-connector
DC supply Micro-D connector
Microstrip antenna
Fiber input with collimating lens
(Photo courtesy of Dr. Rodney B. Waterhouse)
Overview of Microstrip Antennas

## Slide 15
Overview of Microstrip Antennas
Arrays
Linear array (1-D corporate feed)
22 array
2-D 8X8 corporate-fed array
4  8 corporate-fed / series-fed array

## Slide 16
Wraparound Array (conformal)
(Photo courtesy of Dr. Rodney B. Waterhouse)
Overview of Microstrip Antennas
The substrate is so thin that it can be bent to “conform” to the surface.

## Slide 17
Note:
L is the resonant dimension (direction of current flow). The width W is usually chosen to be larger than L (to get higher bandwidth). However, usually W < 2L (to avoid problems with the (0,2) mode).
Overview of Microstrip Antennas
Rectangular patch
W = 1.5L is typical.
x
y
h
L
W
r
Js
Note:
The fields and current are approximately independent of y for the dominant (1,0) mode.

## Slide 18
Circular Patch
x
y
h
a
r
Overview of Microstrip Antennas
The location of the feed determines the direction of current flow and hence the polarization of the radiated field.

## Slide 19
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 20
Feeding Methods
Some of the more common methods for feeding microstrip antennas are shown.
The feeding methods are illustrated for a rectangular patch,
but the principles apply for circular and other shapes as well.

## Slide 21
Coaxial Feed
Note:
A feed along the centerline at y = W/2 is the most common
(this minimizes higher-order modes and cross-pol).
x
y
L
W
Feed at (x0, y0)
Surface current
x
z
Feeding Methods

## Slide 22
Advantages:
Simple
Directly compatible with coaxial cables
Easy to obtain input match by adjusting feed position
Disadvantages:
Significant probe (feed) radiation for thicker substrates
Significant probe inductance for thicker substrates (limits bandwidth)
Not easily compatible with arrays
Coaxial Feed
x
z
Feeding Methods
x
y
L
W
(The resistance varies as the square of the modal field shape.)

## Slide 23
Advantages:
Simple
Allows for planar feeding
Easy to use with arrays
Easy to obtain input match
Disadvantages:
Significant line radiation for thicker substrates
For deep notches, patch current and radiation pattern may show distortion
Inset Feed
Microstrip line
Feeding Methods

## Slide 24
An investigation has shown that the resonant input resistance varies as:
The coefficients A and B depend on the notch width S but (to a good approximation) not on the line width Wf .
Y. Hu, D. R. Jackson, J. T. Williams, and S. A. Long, “Characterization of the Input Impedance of the Inset-Fed Rectangular Microstrip Antenna,” IEEE Trans. Antennas and Propagation, Vol. 56, No. 10, pp. 3314-3318, Oct. 2008.
L
W
Wf
S
x0
Feeding Methods
Inset Feed
Less accurate approximation:

## Slide 25
Advantages:
Allows for planar feeding
Less line radiation compared to microstrip feed (the line is closer to the ground plane)
Can allow for higher bandwidth (no probe inductance, so substrate can be thicker)
Disadvantages:
Requires multilayer fabrication
Alignment is important for input match
Patch
Microstrip line
Feeding Methods
Proximity-coupled Feed
(Electromagnetically-coupled Feed)
Top view
Microstrip
line

## Slide 26
Advantages:
Allows for planar feeding
Can allow for a match even with high edge impedances, where a notch might be too large (e.g., when using a high permittivity substrate)
Disadvantages:
Requires accurate gap fabrication
Requires full-wave design
Patch
Microstrip line
Gap
Feeding Methods
Gap-coupled Feed
Top view
Microstrip
line
Patch

## Slide 27
Advantages:
Allows for planar feeding
Feed-line radiation is isolated from patch radiation
Higher bandwidth is possible since probe inductance is eliminated (allowing for a thick substrate), and also a double-resonance can be created
Allows for use of different substrates to optimize antenna and feed-circuit performance
Disadvantages:
Requires multilayer fabrication
Alignment is important for input match
Patch
Microstrip line
Slot
Feeding Methods
Aperture-coupled Patch (ACP)
Top view
Slot
Microstrip
line

## Slide 28
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 29
Basic Principles of Operation
The basic principles are illustrated here for a rectangular patch, but the principles apply similarly for other patch shapes.
We use the cavity model to explain the operation of the patch antenna.
Y. T. Lo, D. Solomon, and W. F. Richards, “Theory and Experiment on Microstrip Antennas,” IEEE Trans. Antennas Propagat., vol. AP-27, no. 3 (March 1979): 137–145.
h
PMC
z

## Slide 30
Basic Principles of Operation
The patch acts approximately as a resonant cavity (with perfect electric conductor (PEC) walls on top and bottom, and perfect magnetic conductor (PMC) walls on the edges).
Radiation is accounted for by using an effective loss tangent for the substrate.
In a cavity, only certain modes are allowed to exist, at different resonance frequencies.
If the antenna is excited at a resonance frequency, a strong field is set up inside the cavity, and a strong current on the (bottom) surface of the patch. This produces significant radiation (a good antenna).
Main Ideas:
h
PMC
z

## Slide 31
Basic Principles of Operation
As the substrate gets thinner the patch current radiates less, due to image cancellation (current and image are separated by 2h).
However, the Q of the resonant cavity mode also increases, making the patch currents stronger at resonance.
These two effects cancel, allowing the patch to radiate well even for thin substrates (though the bandwidth decreases).
A microstrip antenna can radiate well, even with a thin substrate,
because of resonance.
x
z

## Slide 32
On patch and ground plane:
Inside the patch cavity, because of the thin substrate,
the electric field vector is approximately independent of z.
Hence
h
z
Basic Principles of Operation
Thin Substrate Approximation

## Slide 33
Magnetic field inside patch cavity:
Basic Principles of Operation
Thin Substrate Approximation

## Slide 34
Note: The magnetic field is purely horizontal.
(The mode is TMz.)
h
z
Basic Principles of Operation
Thin Substrate Approximation

## Slide 35
The patch edge acts as an approximate open circuit.
h
PMC Model
or
PMC
h
Actual patch
Basic Principles of Operation
Magnetic-wall Approximation
x
y
L
W

## Slide 36
Hence,
h
PMC
(Neumann B.C.)
Basic Principles of Operation
Magnetic-wall Approximation
x
y
L
W

## Slide 37
Hence
From separation of variables:
(TMmn mode)
x
y
L
W
PMC
Basic Principles of Operation
Resonance Frequencies
We then have
Note:
We ignore the loss tangent of the substrate for the calculation of the resonance frequencies.

## Slide 38
Recall that
Hence
We thus have
x
y
L
W
PMC
Basic Principles of Operation
Resonance Frequencies

## Slide 39
Hence
(resonance frequency of (m,n) mode)
Basic Principles of Operation
Resonance Frequencies
x
y
L
W
PMC
where

## Slide 40
This mode is usually used because the
radiation pattern has a broadside beam.
The resonant length L is about 0.5 guided wavelengths in the x direction (see next slide).
x
y
L
W
Current
Basic Principles of Operation
Dominant (1,0) mode
This structure operates as a “fat planar dipole.”
The current is maximum in the middle of the patch, when plotted along x.

## Slide 41
The resonance frequency is mainly controlled by the
patch length L and the substrate permittivity.
Resonance Frequency of Dominant (1,0) Mode
Comment:
A higher substrate permittivity allows for a smaller antenna (miniaturization), but with a lower bandwidth.
Approximately, (assuming PMC walls)
This is equivalent to saying that the length L is one-half of a wavelength in the dielectric.
(1,0) mode:
Basic Principles of Operation

## Slide 42
The resonance frequency calculation can be improved by adding a
“fringing length extension” L to each edge of the patch to get an
“effective length” Le .
Note: Some authors use effective permittivity in this equation.
(This would change the value of Le.)
Basic Principles of Operation
Resonance Frequency of Dominant Mode
y
x
L
Le
L
L

## Slide 43
Hammerstad formula:
Note:
Even though the Hammerstad formula involves an effective permittivity, we still use the actual substrate permittivity in the resonance frequency formula.
Basic Principles of Operation
Resonance Frequency of Dominant Mode

## Slide 44
Note:
This is a good “rule of thumb” to give a quick estimate.
Basic Principles of Operation
Resonance Frequency of Dominant Mode

## Slide 45
W/ L = 1.5
r = 2.2
The resonance frequency has been normalized by the zero-order value (without fringing).
fN = f / f0
Results: Resonance Frequency
Basic Principles of Operation

## Slide 46
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 47
General Characteristics
The bandwidth is directly proportional to substrate thickness h.
However, if h is greater than about 0.05 0 , the probe inductance (for a coaxial feed) becomes large enough so that matching is difficult – the bandwidth will decrease.
The bandwidth is inversely proportional to r (a foam substrate gives a high bandwidth).
The bandwidth of a rectangular patch is proportional to the patch width W (but we need to keep W < 2L ; see the next slide).
Bandwidth

## Slide 48
Width Restriction for a Rectangular Patch
fc
f10
f01
f02
W = 1.5 L is typical.
General Characteristics
L
W

## Slide 49
Some Bandwidth Observations
For a typical substrate thickness (h /0 = 0.02), and a typical substrate permittivity (r = 2.2) the bandwidth is about 3%.
By using a thick foam substrate, bandwidth of about 10% can be achieved.
By using special feeding techniques (aperture coupling) and stacked patches, bandwidths of 100% have been achieved.
General Characteristics

## Slide 50
W/ L = 1.5
r = 2.2 or 10.8
Results: Bandwidth
The discrete data points are measured values.
The solid curves are from a CAD formula (given later).
General Characteristics

## Slide 51
The resonant input resistance is fairly independent of the substrate thickness h unless h gets small (the variation is then mainly due to dielectric and conductor loss).
The resonant input resistance is proportional to r.
The resonant input resistance is directly controlled by the location of the feed point (maximum at edges x = 0 or x = L, zero at center of patch).
Resonant Input Resistance
L
W
(x0, y0)
L
x
y
General Characteristics

## Slide 52
Note:
The patch is usually fed along the centerline (y0 = W / 2)
to maintain symmetry and thus minimize excitation of undesirable modes
(which cause cross-pol).
Desired mode: (1,0)
L
x
W
Feed: (x0, y0)
y
Resonant Input Resistance (cont.)
General Characteristics

## Slide 53
For a given mode, it can be shown that the resonant input resistance is proportional to the square of the cavity-mode field at the feed point.
For (1,0) mode:
L
x
W
(x0, y0)
y
General Characteristics
This is seen from the cavity-model eigenfunction analysis
(please see the reference).
Resonant Input Resistance (cont.)
Y. T. Lo, D. Solomon, and W. F. Richards, “Theory and Experiment on Microstrip Antennas,” IEEE Trans. Antennas Propagat., vol. AP-27, no. 3 (March 1979): 137–145.

## Slide 54
Hence, for (1,0) mode:
The value of Redge depends strongly on the substrate permittivity
(it is proportional to the permittivity).
For a typical patch, it is often in the range of 100-200 Ohms.
General Characteristics
L
x
W
(x0, y0)
y
Resonant Input Resistance (cont.)

## Slide 55
r = 2.2 or 10.8
W/L = 1.5
x0 = L/4
Results: Resonant Input Resistance
The solid curves are from a CAD formula (given later.)
L
x
W
(x0, y0)
y
y0 = W/2
General Characteristics
Region where loss is important

## Slide 56
Radiation Efficiency
The radiation efficiency is less than 100% due to
Conductor loss
Dielectric loss
Surface-wave excitation*
Radiation efficiency is the ratio of power radiated into space, to the total input power.
General Characteristics
*assuming the substrate is infinite

## Slide 57
Radiation Efficiency (cont.)
General Characteristics
surface wave
TM0
cos () pattern
x
y
Js

## Slide 58
Pr = radiated power
Ptot = total input power
Pc = power dissipated by conductors
Pd = power dissipated by dielectric
Psw = power launched into surface wave
Hence,
General Characteristics
Radiation Efficiency (cont.)

## Slide 59
Conductor and dielectric loss is more important for thinner substrates (the Q of the cavity is higher, and thus the resonance is more seriously affected by loss).
Conductor loss increases with frequency (proportional to f 1/2) due to the skin effect. It can be very serious at millimeter-wave frequencies.
Conductor loss is usually more important than dielectric loss for typical substrate thicknesses and loss tangents.
Rs is the surface resistance of the metal. The skin depth of the metal is .
Some observations:
General Characteristics
Radiation Efficiency (cont.)

## Slide 60
Surface-wave power is more important for thicker substrates or for higher-substrate permittivities. (The surface-wave power can be minimized by using a thin substrate or a foam substrate.)
For a foam substrate, a high radiation efficiency is obtained by making the substrate thicker (minimizing the conductor and dielectric losses). There is no surface-wave power to worry about.
For a typical substrate such as r = 2.2, the radiation efficiency is maximum for h / 0  0.02.
General Characteristics
Radiation Efficiency (cont.)

## Slide 61
r = 2.2 or 10.8
W/L = 1.5
Results: Efficiency (Conductor and dielectric losses are neglected.)
2.2
10.8
Note: CAD plot uses the Pozar formula (given later).
General Characteristics

## Slide 62
r = 2.2 or 10.8
W/L = 1.5
Results: Efficiency (All losses are accounted for.)
General Characteristics
Note: CAD plot uses the Pozar formula (given later).

## Slide 63
General Characteristics
Radiation Pattern
E-plane: co-pol is E
H-plane: co-pol is E
Note:
For radiation patterns, it is usually more convenient to place the origin at the middle of the patch
(this keeps the formulas as simple as possible).
x
y
L
W
E plane
H plane
Probe
Js

## Slide 64
Comments on radiation patterns:
The E-plane pattern is typically broader than the H-plane pattern.
The truncation of the ground plane will cause edge diffraction, which tends to degrade the pattern by introducing:
Rippling in the forward direction
Back-radiation
Pattern distortion is more severe in the E-plane, due to the angle dependence of the vertical polarization E on the ground plane.
(It varies as cos ()).
General Characteristics
Radiation Patterns (cont.)

## Slide 65
x
y
L
W
E plane
H plane
Edge diffraction is the most serious in the E plane.
General Characteristics
Radiation Patterns
Space wave
Js

## Slide 66
E-plane pattern
Red: infinite substrate and ground plane
Blue: 1 meter ground plane
Note:
The E-plane pattern “tucks in” and tends to zero at the horizon due to the presence of the infinite substrate.
General Characteristics
Radiation Patterns

## Slide 67
Red: infinite substrate and ground plane
Blue: 1 meter ground plane
H-plane pattern
General Characteristics
Radiation Patterns

## Slide 68
Directivity
The directivity is fairly insensitive to the substrate thickness.
The directivity is higher for lower permittivity, because the patch is larger.
General Characteristics

## Slide 69
r = 2.2 or 10.8
W/ L = 1.5
Results: Directivity (relative to isotropic)
General Characteristics

## Slide 70
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 71
CAD Formulas
CAD formulas for the important properties of the rectangular microstrip antenna will be shown.
D. R. Jackson, “Microstrip Antennas,” Chapter 7 of Antenna Engineering Handbook, 5th Ed., J. L. Volakis, Editor, McGraw Hill, 2019.
D. R. Jackson, S. A. Long, J. T. Williams, and V. B. Davis, “Computer-Aided Design of Rectangular Microstrip Antennas,” Ch. 5 of Advances in Microstrip and Printed Antennas, K. F. Lee and W. Chen, Eds., John Wiley, 1997.
D. R. Jackson and N. G. Alexopoulos, “Simple Approximate Formulas for Input Resistance, Bandwidth, and Efficiency of a Resonant Rectangular Patch,” IEEE Trans. Antennas and Propagation, Vol. 39, pp. 407-410, March 1991.
Radiation efficiency
Bandwidth (Q)
Resonant input resistance
Directivity

## Slide 72
where
Note: “hed” refers to a unit-amplitude horizontal electric dipole.
CAD Formulas
Radiation Efficiency
Comment:
The efficiency becomes small as the substrate gets thin,
if there is dielectric or conductor loss.

## Slide 73
where
Note: “hed” refers to a unit-amplitude horizontal electric dipole.
CAD Formulas
Radiation Efficiency (cont.)
Note: When we say “unit amplitude” here, we assume peak (not RMS) values.

## Slide 74
Hence, we have
Physically, this term is the radiation efficiency of a
horizontal electric dipole (hed) on top of the substrate.
CAD Formulas
Radiation Efficiency (cont.)

## Slide 75
The constants are defined as follows:
CAD Formulas
Radiation Efficiency (cont.)

## Slide 76
Improved formula for HED surface-wave power (due to Pozar)
D. M. Pozar, “Rigorous Closed-Form Expressions for the Surface-Wave Loss of Printed Antennas,” Electronics Letters, vol. 26, pp. 954-956, June 1990.
CAD Formulas
Note: The above formula for the surface-wave power is different from that given in Pozar’s paper by a factor of 2, since Pozar used RMS instead of peak values.
Note: x0 in this formula is not the feed location!

## Slide 77
BW is defined from the frequency limits f1 and f2 at which SWR = 2.0.
(multiply by 100 if you want to get %)
CAD Formulas
Bandwidth
Comments:
For a lossless patch, the bandwidth is approximately proportional to the patch width and to the substrate thickness. It is inversely proportional to the substrate permittivity.
For very thin substrates the bandwidth will increase for a lossy patch, but as the expense of efficiency.

## Slide 78
CAD Formulas
Quality Factor Q

## Slide 79
CAD Formulas
Q Components
The constants p and c1 were defined previously.

## Slide 80
Probe-feed Patch
CAD Formulas
Resonant Input Resistance
Comments:
For a lossless patch, the resonant resistance is approximately independent of the substrate thickness. For a lossy patch it tends to zero as the substrate gets very thin. For a lossless patch it is inversely proportional to the square of the patch width and it is proportional to the substrate permittivity.

## Slide 81
(Euler’s constant)
Approximate CAD formula for probe (feed) reactance (in Ohms)
a = probe radius
h = probe height
This is based on an infinite parallel-plate model.
CAD Formulas

## Slide 82
Feed (probe) reactance increases proportionally with substrate thickness h.
Feed reactance increases for smaller probe radius.
If the substrate gets too thick, the probe reactance will make it difficult to get an input match, and the bandwidth will suffer.
(Compensating techniques will be discussed later.)
Important point:
CAD Formulas
Observations:

## Slide 83
Results: Probe Reactance (Xf =Xp= Lp)
xr = 2 ( x0 / L) - 1
The normalized feed location ratio xr is zero at the center of the patch (x = L/2), and is 1.0 at the patch edge (x = L).
r = 2.2
W/L = 1.5
h = 0.0254 0
a = 0.5 mm
Center
Edge
Rectangular patch
L
W
(x0, y0)
L
x
y
Note: “exact” means the cavity model with all infinite modes.
CAD Formulas

## Slide 84
where
CAD Formulas
Directivity
The constants p and c1 were defined previously.

## Slide 85
For thin substrates:
(The directivity is essentially independent of the substrate thickness.)
CAD Formulas
Directivity (cont.)

## Slide 86
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 87
Input Impedance
Various models have been proposed over the years for calculating the
input impedance of a microstrip patch antenna.
Transmission line model
  The first model introduced
  Very simple
Cavity model (eigenfunction expansion)
  Simple yet accurate for thin substrates
  Gives physical insight into operation
CAD circuit model
  Extremely simple and almost as accurate as the cavity model
Spectral-domain method
  More challenging to implement
  Accounts rigorously for both radiation and surface-wave excitation
Commercial software
  Very accurate
  Can be time consuming

## Slide 88
Results for a typical patch show that the first three methods agree very well, provided the correct Q is used and the probe inductance is accounted for.
Input Impedance
Comparison of the Three Simplest Models
CAD Circuit model of patch
Transmission line model of patch
Cavity model (eigenfunction expansion) of patch

## Slide 89
Input Impedance
Comparison of CAD with Full-Wave
Results from full-wave analysis agree well with the simple CAD circuit model, except for a shift in resonance frequency.

## Slide 90
CAD Circuit Model for Input Impedance
The circuit model discussed assumes a probe feed.
Other circuit models exist for other types of feeds.
Note:
The mathematical justification of the CAD circuit model comes from a cavity-model eigenfunction analysis.
Input Impedance
Y. T. Lo, D. Solomon, and W. F. Richards, “Theory and Experiment on Microstrip Antennas,” IEEE Trans. Antennas Propagat., vol. AP-27, no. 3 (March 1979): 137–145.

## Slide 91
Near the resonance frequency, the patch cavity can be approximately modeled as a resonant RLC circuit.
The resistance R accounts for radiation and losses.
A probe inductance Lp is added in series, to account for the “probe inductance” of a probe feed.
Lp
R
C
L
Zin
Probe
Patch cavity
Probe-fed Patch
Input Impedance

## Slide 92
BW is defined here by SWR < 2.0 when the RLC circuit is fed by a matched line (Z0 = R).
Lp
R
C
L
Zin
Input Impedance

## Slide 93
R is the input resistance at the resonance of the patch cavity
(the frequency that maximizes Rin).
Input Impedance
Lp
R
C
L
(resonance of RLC circuit)

## Slide 94
The input resistance is determined once we know four parameters:
f0: the resonance frequency of the patch cavity
R: the input resistance at the cavity resonance frequency f0
Q: the quality factor of the patch cavity
Lp: the probe inductance
(R, f0, Q)
Zin
CAD formulas for all of these four parameters have been given earlier.
Input Impedance
Lp
R
C
L

## Slide 95
Input Impedance
Typical plot of input impedance
Without probe inductance
With probe inductance

## Slide 96
Results: Input Resistance vs. Frequency
r = 2.2
W/L = 1.5
L = 3.0 cm
Frequency where the input resistance is maximum (f0):
Rin = R
Rectangular patch
Input Impedance
Note: “exact” means the cavity model will all infinite modes.

## Slide 97
Results: Input Reactance vs. Frequency
r = 2.2
W/L = 1.5
L = 3.0 cm
Frequency where the input resistance is maximum (f0)
Frequency where the input impedance is real
Shift due to probe reactance
Rectangular patch
Input Impedance
Xp
Note: “exact” means the cavity model will all infinite modes.

## Slide 98
Optimization to get exactly 50  at the desired resonance frequency:
Input Impedance
Vary the length L first until you find the value that gives an input reactance of zero at the desired frequency.
Then adjust the feed position x0 to make the real part of the input impedance 50  at this frequency.

## Slide 99
Design a probe-fed rectangular patch antenna on a substrate having a relative permittivity of 2.33 and a thickness of 62 mils (0.1575 cm). (This is Rogers RT Duroid 5870.) Choose an aspect ratio of W / L = 1.5. The patch should resonate at the operating frequency of 1.575 GHz (the GPS L1 frequency). Ignore the probe inductance in your design, but account for fringing at the patch edges when you determine the dimensions. At the operating frequency the input impedance should be 50  (ignoring the probe inductance). Assume an SMA connector is used to feed the patch along the centerline (at y = W / 2), and that the inner conductor of the SMA connector has a radius of 0.635 mm. The copper patch and ground plane have a conductivity of  = 3.0 107 S/m and the dielectric substrate has a loss tangent of tan = 0.001.
1) Calculate the following:
  The final patch dimensions L and W (in cm)
  The feed location x0 (distance of the feed from the closest patch edge, in cm)
  The bandwidth of the antenna (SWR < 2 definition, expressed in percent)
  The radiation efficiency of the antenna (accounting for conductor, dielectric, and surface-wave loss, and expressed in percent)
  The probe reactance Xp at the operating frequency (in )
  The expected complex input impedance (in ) at the operating frequency, accounting for the probe inductance
  Directivity
  Gain
Design Example

## Slide 100
  2) Find (f0, R, Xp, and Q) and plot the input impedance vs. frequency using the CAD circuit model.
  3) Keep W/L = 1.5, but now vary the length L of the patch and the feed position x0 until you find the value that makes the input impedance exactly 50+j(0)  at 1.575 GHz.
Design Example
Continued

## Slide 101
Design Example
  1) L = 6.071 cm, W = 9.106 cm
  2) x0 = 1.832 cm
  3) BW = 1.23%
  4) er = 82.9%
  5) Xp = 11.1 
  6) Zin = 50.0 + j(11.1) 
  7) D = 5.85 (7.67 dB)
  8) G = (D)(er) = 4.85 (6.86 dB)
Results from the CAD formulas:
x
y
L
W
Feed at (x0, y0)
y0 = W/2
Part 1
Results

## Slide 102
f0 = 1.575 109 Hz
R = 50 
Q = 57.5
Xp = 11.1 
Results from the CAD formulas:
Design Example
Part 2
Rin
Xin
f (GHz)

x
y
L
W
Feed at (x0, y0)
y0 = W/2
Results

## Slide 103
L = 6.083 cm
x0 = 1.800 cm
After optimization:
Design Example
Part 3
x
y
L
W
Feed at (x0, y0)
y0 = W/2
Note:
f (GHz)

At 1.575 GHz
Results

## Slide 104
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 105
Radiation Pattern
Patch
Probe
Coax feed
Note:
The origin is placed at the center of the patch,
at the top of the substrate, for the pattern calculations.
There are two models often used for calculating the radiation pattern:
Electric current model
Magnetic current model

## Slide 106
Patch
Probe
Coax feed
Electric current model:
We keep the physical currents flowing on the patch (and feed).
Radiation Pattern

## Slide 107
Patch
Probe
Coax feed
Magnetic current model:
We apply the equivalence principle and invoke the (approximate) PMC condition
at the edges.
Radiation Pattern
Equivalence surface
The equivalent surface current is approximately zero on the top surface (weak fields) and the sides (PMC). We can ignore it on the ground plane (it does not radiate).

## Slide 108
Theorem
The electric and magnetic models yield identical patterns
at the resonance frequency of the cavity mode.
Assumption:
The electric and magnetic current models are based on the fields of a single cavity mode, corresponding to an ideal cavity with PMC walls.
D. R. Jackson and J. T. Williams, “A Comparison of CAD Models for Radiation from Rectangular Microstrip Patches,” Intl. Journal of Microwave and Millimeter-Wave Computer Aided Design, vol. 1, no. 2, pp. 236-248, April 1991.
Radiation Pattern

## Slide 109
Comments on the Substrate Effects
The substrate can be neglected to simplify the far-field calculation.
When considering the substrate, it is most convenient to assume an infinite substrate (in order to obtain a closed-form solution).
Reciprocity can be used to calculate the far-field pattern of electric or magnetic current sources inside of an infinite layered structure.
When an infinite substrate is assumed, the far-field pattern always goes to zero at the horizon.
D. R. Jackson and J. T. Williams, “A Comparison of CAD Models for Radiation from Rectangular Microstrip Patches,” Intl. Journal of Microwave and Millimeter-Wave Computer Aided Design, vol. 1, no. 2, pp. 236-248, April 1991.
Radiation Pattern

## Slide 110
Comments on the Two Models
For the rectangular patch, the electric current model is the simplest since there is only one electric surface current (as opposed to four edges).
For the rectangular patch, the magnetic current model allows us to classify the “radiating” and “nonradiating” edges.
Radiation Pattern
Note:
On the nonradiating edges, the magnetic currents are in opposite directions across the centerline (x = 0).
L
x
W
y
“Radiating edges”
“Nonradiating edges”

## Slide 111
(The formula is based on the electric current model.)
The origin is at the center of the patch.
L
h
Infinite ground plane and substrate
x
The probe is on the x axis.
y
L
W
E-plane
H-plane
x
(1,0) mode
Radiation Pattern
Rectangular Patch Pattern Formula

## Slide 112
The “hex” pattern is for a
horizontal electric dipole in the x direction,
sitting on top of the substrate.
The far-field pattern can be determined by reciprocity.
x
y
L
W
Radiation Pattern
D. R. Jackson and J. T. Williams, “A Comparison of CAD Models for Radiation from Rectangular Microstrip Patches,” Intl. Journal of Microwave and Millimeter-Wave Computer Aided Design, vol. 1, no. 2, pp. 236-248, April 1991.

## Slide 113
where
Radiation Pattern
Note: To account for lossy substrate, use

## Slide 114
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Radiation pattern
Input Impedance
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 115
Circular Polarization
Three main techniques:
Single feed with “nearly degenerate” eigenmodes (compact but small CP bandwidth).
Dual feed with delay line or 90o hybrid phase shifter (broader CP bandwidth but uses more space).
Synchronous subarray technique (produces high-quality CP due to cancellation effect, but requires even more space).
The techniques will be illustrated with a rectangular patch.

## Slide 116
L
W
Basic principle: The two dominant modes (1,0) and (0,1) are excited with equal amplitude, but with a 45o phase.
The feed is on the diagonal.
The patch is nearly
(but not exactly) square.
Circular Polarization
Single Feed Method
(1,0)
(0,1)

## Slide 117
Design equations:
Top sign for LHCP, bottom sign for RHCP.
The resonant input resistance of the CP patch at fCP is the same as what a linearly-polarized patch fed at the same position would be.
L
W
x
y
(SWR < 2 )
The optimum CP frequency is the average of the x and y resonance frequencies.
The frequency fCP is also the resonance frequency:
Circular Polarization
(1,0)
(0,1)

## Slide 118
Other Variations
Patch with slot
Patch with truncated corners
Note: Diagonal modes are used as degenerate modes
L
L
x
y
L
L
x
y
Circular Polarization

## Slide 119
Here we compare bandwidths (impedance and axial-ratio):
Linearly-polarized (LP) patch:
Circularly-polarized (CP) single-feed patch:
The axial-ratio bandwidth is small when using the single-feed method.
W. L. Langston and D. R. Jackson, “Impedance, Axial-Ratio, and Receive-Power Bandwidths of Microstrip Antennas,” IEEE Trans. Antennas and Propagation, vol. 52, pp. 2769-2773, Oct. 2004.
Circular Polarization

## Slide 120
Phase shift realized with delay line:
Circular Polarization
Dual-Feed Method
L
L
x
y
P
P+g/4
RHCP

## Slide 121
Phase shift realized with 90o quadrature hybrid (branchline coupler)
Circular Polarization
This gives us a higher bandwidth than the simple power divider,
but requires a load resistor.
L
L
x
y
g/4
RHCP
g/4
Feed
50 Ohm load

## Slide 122
Multiple elements are rotated in space and fed with phase shifts.
0o
-90o
-180o
-270o
Because of symmetry, radiation from higher-order modes (or probes)
tends to be reduced, resulting in good cross-pol.
Circular Polarization
Synchronous Rotation

## Slide 123
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 124
Circular Patch
x
y
h
a
r

## Slide 125
a
PMC
From separation of variables:
Jm = Bessel function of first kind, order m.
Circular Patch
Resonance Frequency

## Slide 126
a
PMC
(nth root of Jm Bessel function)
This gives us
Circular Patch
Resonance Frequency

## Slide 127
n / m | 0 | 1 | 2 | 3 | 4 | 5
1 | 3.832 | 1.841 | 3.054 | 4.201 | 5.317 | 5.416
2 | 7.016 | 5.331 | 6.706 | 8.015 | 9.282 | 10.520
3 | 10.173 | 8.536 | 9.969 | 11.346 | 12.682 | 13.987
Dominant mode: TM11
Table of values for
Circular Patch
Resonance Frequency

## Slide 128
Dominant mode: TM11
y
x
a
Circular patch
Square patch
The circular patch is somewhat similar to a square patch.
W = L
x
y
Circular Patch

## Slide 129
Fringing extension
“Long/Shen Formula”:
a
PMC
a + a
or
L. C. Shen, S. A. Long, M. Allerding, and M. Walton, "Resonant Frequency of a Circular Disk Printed-Circuit Antenna," IEEE Trans. Antennas and Propagation, vol. 25, pp. 595-596, July 1977.
Circular Patch

## Slide 130
(The patterns are based on the magnetic current model.)
(The edge voltage has a maximum of one volt.)
a
y
x
E-plane
H-plane
In patch cavity:
The probe is on the x axis.
2a
h
Infinite GP and substrate
x
The origin is at the center of the patch.
Patterns
Circular Patch

## Slide 131
where
Patterns
Circular Patch
Note: To account for lossy substrate, use

## Slide 132
a
Input Resistance
Circular Patch

## Slide 133
where
Psp = power radiated into space by circular patch with maximum edge voltage of one volt.
er = radiation efficiency
Input Resistance (cont.)
Circular Patch

## Slide 134
CAD Formula:
Circular Patch
Input Resistance (cont.)

## Slide 135
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 136
Improving Bandwidth
Some of the techniques that have been successfully developed are illustrated here.
The literature may be consulted for additional designs and variations.

## Slide 137
L-shaped probe:
Capacitive “top hat” on probe:
Top view
Improving Bandwidth
Probe Compensation
As the substrate thickness increases the probe inductance limits the bandwidth – so we compensate for it.

## Slide 138
SSFIP: Strip Slot Foam Inverted Patch (a version of the ACP).
Microstrip substrate
Patch
Microstrip line
Slot
Foam
Patch substrate
Bandwidths greater than 25% have been achieved.
Increased bandwidth is due to the thick foam substrate and also a dual-tuned resonance (patch+slot).
Improving Bandwidth
Note: There is no probe inductance to worry about here.
J.-F. Zürcher and F. E. Gardiol, Broadband Patch Antennas, Artech House, Norwood, MA, 1995.

## Slide 139
Bandwidth increase is due to thick low-permittivity antenna substrates and a dual or triple-tuned resonance.
Bandwidths of 25% have been achieved using a probe feed.
Bandwidths of 100% have been achieved using an ACP feed.
Microstrip substrate
Coupling patch
Microstrip line
Slot
Patch substrates
Top Patch
Improving Bandwidth
Stacked Patches

## Slide 140
Bandwidth (S11 = -10 dB) is about 100%
Stacked patch with ACP feed
Improving Bandwidth
Stacked Patches
(Photo courtesy of Dr. Rodney B. Waterhouse)

## Slide 141
Stacked patch with ACP feed
Two extra loops are observed on the Smith chart.
Stacked Patches
Improving Bandwidth
(Photo courtesy of Dr. Rodney B. Waterhouse)

## Slide 142
Radiating Edges Gap Coupled Microstrip Antennas (REGCOMA).
Non-Radiating Edges Gap Coupled Microstrip Antennas (NEGCOMA)
Four-Edges Gap Coupled Microstrip Antennas (FEGCOMA)
Bandwidth improvement factor:
REGCOMA: 3.0, NEGCOMA: 3.0, FEGCOMA: 5.0?
Mush of this work was pioneered by K. C. Gupta.
Improving Bandwidth
Parasitic Patches

## Slide 143
Radiating Edges Direct Coupled Microstrip Antennas (REDCOMA).
Non-Radiating Edges Direct Coupled Microstrip Antennas (NEDCOMA)
Four-Edges Direct Coupled Microstrip Antennas (FEDCOMA)
Bandwidth improvement factor:
REDCOMA: 5.0, NEDCOMA: 5.0, FEDCOMA: 7.0
Improving Bandwidth
Direct-Coupled Patches

## Slide 144
The introduction of a U-shaped slot can give a significant bandwidth (10%-40%).
(This is due to a double resonance effect, with two different modes.)
“Single Layer Single Patch Wideband Microstrip Antenna,” T. Huynh and K. F. Lee, Electronics Letters, Vol. 31, No. 16, pp. 1310-1312, 1986.
Improving Bandwidth
U-Shaped Slot

## Slide 145
A 44% bandwidth was achieved.
Y. X. Guo, K. M. Luk, and Y. L. Chow, “Double U-Slot Rectangular Patch Antenna,” Electronics Letters, Vol. 34, No. 19, pp. 1805-1806, 1998.
Improving Bandwidth
Double U-Slot

## Slide 146
A modification of the U-slot patch.
A bandwidth of 34% was achieved (40% using a capacitive “washer” to compensate for the probe inductance).
B. L. Ooi and Q. Shen, “A Novel E-shaped Broadband Microstrip Patch Antenna,” Microwave and Optical Technology Letters, vol. 27, No. 5, pp. 348-352, 2000.
Improving Bandwidth
E Patch

## Slide 147
Multi-Band Antennas
General Principle:
Introduce multiple resonance paths into the antenna.
A multi-band antenna is sometimes more desirable than a broadband antenna, if multiple narrow-band channels are to be covered.

## Slide 148
Dual-band E patch
High-band
Low-band
Low-band
Feed
Dual-band patch with parasitic strip
Low-band
High-band
Feed
Multi-Band Antennas

## Slide 149
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Radiation pattern
Input Impedance
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 150
Miniaturization
High Permittivity
Quarter-Wave Patch
PIFA
Capacitive Loading
Slots
Meandering
Note: Miniaturization usually comes at a price of reduced bandwidth!
Usually, bandwidth is proportional to the volume of the patch cavity,
as we will see in the examples.

## Slide 151
The smaller patch has about one-fourth the bandwidth of the original patch.
L
W
(Bandwidth is inversely proportional to the permittivity.)
Size reduction
Miniaturization
High Permittivity
(Same aspect ratio)

## Slide 152
L
W
Ez = 0
The new patch has about one-half the bandwidth of the original patch.
Neglecting losses:
Short-circuit vias
W
Note: 1/2 of the radiating magnetic current
Miniaturization
Quarter-Wave patch

## Slide 153
The new patch has about one-half the bandwidth of the original quarter-wave patch, and hence one-fourth the bandwidth of the regular patch.
(Bandwidth is proportional to the patch width.)
A quarter-wave patch with the same aspect ratio W/L as the original patch
Width reduction
L
W
Ez = 0
Short-circuit vias
W
Miniaturization
Smaller Quarter-Wave patch

## Slide 154
Fewer vias actually gives more miniaturization!
(The edge has a larger inductive impedance: explained on the next slide.)
W
W
Use fewer vias
Miniaturization
Quarter-Wave Patch with Fewer Vias

## Slide 155
Short
Open
Inductance
The Smith chart provides a simple explanation for the length reduction.
Miniaturization
Quarter-Wave Patch with Fewer Vias

## Slide 156
A single shorting strip or via is used.
This antenna can be viewed as a limiting case of the via-loaded patch,
or as an LC resonator.
Feed
Shorting strip or via
Top view
Miniaturization
Planar Inverted F (PIFA)

## Slide 157
The capacitive loading allows for the length of the PIFA to be reduced.
Feed
Shorting plate
Top view
Miniaturization
PIFA with Capacitive Loading

## Slide 158
The patch has a monopole-like pattern
Feed
c
b
Patch
Metal vias
2a
(Hao Xu Ph.D. dissertation, University of Houston, 2006)
The patch operates in the (0,0) mode, as an LC resonator
Miniaturization
Circular Patch Loaded with Vias

## Slide 159
Example: Circular Patch Loaded with 2 Vias
Unloaded: resonance frequency = 5.32 GHz.
(Miniaturization factor = 4.8)
Miniaturization
Circular Patch Loaded with Vias

## Slide 160
The slot forces the current to flow through a longer path,
increasing the effective dimensions of the patch.
Top view
Linear
CP
0o
90o
Miniaturization
Slotted Patch

## Slide 161
Meandering forces the current to flow through a longer path, increasing the effective dimensions of the patch.
Meandering also increases the capacitance of the PIFA line.
Feed
Via
Meandered quarter-wave patch
Feed
Via
Meandered PIFA
Miniaturization
Meandering

## Slide 162
Outline
Overview of microstrip antennas
Feeding methods
Basic principles of operation
General characteristics
CAD Formulas
Input Impedance
Radiation pattern
Circular polarization
Circular patch
Improving bandwidth
Miniaturization
Reducing surface waves and lateral radiation

## Slide 163
Reducing Surface and Lateral Waves
Reduced Surface Wave (RSW) Antenna
SIDE VIEW
z
b
h
x
Shorted annular ring
Ground plane
Feed
a
r0
TOP VIEW
a
r
o
b
Feed
  D. R. Jackson, J. T. Williams, A. K. Bhattacharyya, R. Smith, S. J. Buchheit, and S. A. Long,
  “Microstrip Patch Designs that do Not Excite Surface Waves,” IEEE Trans. Antennas Propagat.,
  vol. 41, No 8, pp. 1026-1037, August 1993.

## Slide 164
Reducing surface-wave excitation and lateral radiation reduces edge diffraction and mutual coupling.
Reducing Surface and Lateral Waves
Edge diffraction degrades the radiation pattern on a finite ground plane.
Mutual coupling causes an desirable coupling between antennas.

## Slide 165
Reducing surface-wave excitation and lateral radiation reduces edge diffraction.
Space-wave radiation (desired)
Lateral radiation (undesired)
Surface waves (undesired)
Diffracted field at edge
Reducing Surface and Lateral Waves

## Slide 166
TM11 mode:
At edge:
a
x
y
Reducing Surface and Lateral Waves
Reducing the Surface Wave Excitation

## Slide 167
Surface-Wave Excitation:
(z > h)
Set
a
x
y
Substrate
Reducing Surface and Lateral Waves

## Slide 168
For TM11 mode:
Patch resonance:
Note:
The RSW patch is too big to be resonant.
Hence
a
x
y
Substrate
Reducing Surface and Lateral Waves

## Slide 169
The radius a is chosen to make the patch resonant:
Reducing Surface and Lateral Waves
SIDE VIEW
z
b
h
x
Shorted annular ring
Ground plane
Feed
a
r0
TOP VIEW
a
r
o
b
Feed

## Slide 170
Space-Wave Field:
(z = h)
Set
Assume no substrate outside of patch
(or very thin substrate):
a
x
y
Ground plane
Reducing Surface and Lateral Waves
Reducing the Lateral Radiation

## Slide 171
For a thin substrate:
The same design reduces both surface-wave fields and lateral-radiation fields.
a
x
y
Substrate
Reducing Surface and Lateral Waves
Note: The diameter of the RSW antenna is found from
Note:
The size is approximately independent of the permittivity (the patch cannot be miniaturized by choosing a higher permittivity!).

## Slide 172
Conventional
RSW
Measurements were taken on a 1 m diameter circular ground plane at 1.575 GHz.
E-plane Radiation Patterns
Measurement
Theory (infinite GP)
Reducing Surface and Lateral Waves

## Slide 173
Reducing surface-wave excitation and lateral radiation reduces mutual coupling.
Space-wave radiation
Lateral radiation
Surface waves
Reducing Surface and Lateral Waves

## Slide 174
Reducing surface-wave excitation and lateral radiation reduces mutual coupling.
“Mutual Coupling Between Reduced Surface-Wave Microstrip Antennas,” M. A. Khayat, J. T. Williams, D. R. Jackson, and S. A. Long, IEEE Trans. Antennas and Propagation, Vol. 48, pp. 1581-1593, Oct. 2000.
E-plane
Reducing Surface and Lateral Waves
1/r
1/r3

## Slide 175
References
General references about microstrip antennas:
Microstrip Antenna Design Handbook, R. Garg, P. Bhartia, I. J. Bahl, and A. Ittipiboon, Editors, Artech House, 2001.
Microstrip Patch Antennas: A Designer’s Guide, R. B. Waterhouse, Kluwer Academic Publishers, 2003.
Advances in Microstrip and Printed Antennas, K. F. Lee, Editor, John Wiley, 1997.
Microstrip Patch Antennas, K. F. Fong Lee and K. M. Luk, Imperial College Press, 2011.
Microstrip and Patch Antennas Design, 2nd Ed., R. Bancroft, Scitech Publishing, 2009.

## Slide 176
References (cont.)
General references about microstrip antennas (cont.):
Millimeter-Wave Microstrip and Printed Circuit Antennas, P. Bhartia, Artech House, 1991.
The Handbook of Microstrip Antennas (two volume set), J. R. James and P. S. Hall, INSPEC, 1989.
Microstrip Antenna Theory and Design, J. R. James, P. S. Hall, and C. Wood, INSPEC/IEE, 1981.
Microstrip Antennas: The Analysis and Design of Microstrip Antennas and Arrays, D. M. Pozar and D. H. Schaubert, Editors, Wiley/IEEE Press, 1995.
CAD of Microstrip Antennas for Wireless Applications, R. A. Sainati, Artech House, 1996.

## Slide 177
Computer-Aided Design of Rectangular Microstrip Antennas, D. R. Jackson, S. A. Long, J. T. Williams, and V. B. Davis, Ch. 5 of Advances in Microstrip and Printed Antennas, K. F. Lee, Editor, John Wiley, 1997.
More information about the CAD formulas presented here for the rectangular patch may be found in:
References (cont.)
Microstrip Antennas, D. R. Jackson, Ch. 7 of Antenna Engineering Handbook, J. L. Volakis, Editor, McGraw Hill, 2007.

## Slide 178
References devoted to broadband microstrip antennas:
Compact and Broadband Microstrip Antennas, K.-L. Wong, John Wiley, 2003.
Broadband Microstrip Antennas, G. Kumar and K. P. Ray, Artech House, 2002.
Broadband Patch Antennas, J.-F. Zürcher and F. E. Gardiol, Artech House, 1995.
References (cont.)

## Slide 179
The End