## Slide 1
ECE 6382
Green’s Functions
David R. Jackson
Fall 2023
Notes 19
x

## Slide 2
Green’s Functions
Green's Mill in Sneinton (Nottingham), England, the mill owned by Green's father. The mill was renovated in 1986 and is now a science centre.
George Green (1793-1841)
The Green's function method is a powerful and systematic method for determining a solution to a problem with a known forcing function on the RHS.
The Green’s function is the solution to a “point” or “impulse” forcing function.
It is similar to the idea of an “impulse response” in circuit theory (where we deal with time instead of space).

## Slide 3
Green’s Functions (cont.)
Consider the following second-order linear differential equation:
or
where
( f is a “forcing” function.)
(self-adjoint)

## Slide 4
Green’s Functions (cont.)
Problem to be solved:
or

## Slide 5
Green’s Functions (cont.)
We can think of the forcing function f (x) as being broken into many small rectangular pieces.
Using superposition, we add up the solution from each small piece.
Each small piece can be represented as a delta function in the limit as the width approaches zero.
Note:
The (x) function becomes a  (x) function in the limit as x  0.
N pulses

## Slide 6
Green’s Functions (cont.)
From superposition:

## Slide 7
Green’s Functions (cont.)
The solution to the original differential equation (from superposition) is then
The Green’s function G(x, x) is defined as the solution with a
delta-function at x = x for the RHS.
x

## Slide 8
Green’s Functions (cont.)
There are two general methods for constructing Green’s functions.
Method 1:
Find the solution to the homogenous equation to the left and right of the delta function, and then enforce boundary conditions at the location of the delta function.
The Green’s function is assumed to be continuous.
The derivative of the Green’s function is allowed to be discontinuous.
The functions u1 and u2 are solutions of the homogenous equation.
Note: u1 satisfies the left BC, u2 satisfies the right BC.
x

## Slide 9
Green’s Functions (cont.)
Method 2:
Use the method of eigenfunction expansion.
Eigenvalue problem:
We then have:
or
Note:
The eigenfunctions are orthogonal (L is self-adjoint).

## Slide 10
Green’s Functions (cont.)
Method 1
Integrate both sides of the above DE over the delta function:
x

## Slide 11
Green’s Functions (cont.)
Method 1 (cont.)
Also, we have (from continuity of the Green’s function):
x

## Slide 12
Green’s Functions (cont.)
Method 1 (cont.)
We then have:
where
x
Also,

## Slide 13
Green’s Functions (cont.)
Method 1 (cont.)
We then have:
x

## Slide 14
Green’s Functions (cont.)
Method 2
The Green’s function is expanded as a series of eigenfunctions.
where
The eigenfunctions corresponding to distinct eigenvalues are orthogonal (from Sturm-Liouville theory).
or
x
a
b
n=1
n=2
n=3
n=4

## Slide 15
Green’s Functions (cont.)
Method 2 (cont.)
Orthogonality
Delta-function property
Multiply both sides by m*(x) w(x) and then integrate from a to b.
x
a
b
n=1
n=2
n=3
n=4

## Slide 16
Green’s Functions (cont.)
Method 2 (cont.)
Therefore, we have (relabeling m  n):
Hence
x
a
b
n=1
n=2
n=3
n=4

## Slide 17
Application: Transmission Line
A short-circuited transmission line resonator with a distributed current source.
The distributed current source is a surface current.
+
-
Green’s function problem:

## Slide 18
An illustration of the Green’s function (for voltage):
Application: Transmission Line (cont.)
The total voltage due to the distributed current source (surface current) is then:
+
-

## Slide 19
Take the derivative of the first and substitute from the second:
Telegrapher’s equations for a distributed current source:
(Please see Appendix A.)
Application: Transmission Line (cont.)
Note: j is used instead of i here.
L = inductance/meter
C = capacitance/meter

## Slide 20
Hence
where
Application: Transmission Line (cont.)
or
Therefore:

## Slide 21
Application: Transmission Line (cont.)
Compare with:
Therefore:
Note: The self-adjoint property required the operator to be real, which is not the case here since w(z) is not real. However, we can multiply both sides of the equation by j to make the operator real, and then divide the final answer by j at the end. This process does not affect the final result, so it is not done here.

## Slide 22
Application: Transmission Line (cont.)
The general solution of the homogeneous equation is:
Method 1
+
-
Homogeneous equation:

## Slide 23
Application: Transmission Line (cont.)
The Green’s function is:
+
-

## Slide 24
Application: Transmission Line (cont.)
The final form of the Green’s function is:
where
+
-

## Slide 25
Application: Transmission Line (cont.)
The eigenvalue problem is
Method 2
+
-
This may be written as
where
Note:
A minus sign in introduced in the eigenvalue problem for convenience.

## Slide 26
Application: Transmission Line (cont.)
We then have:
The solution is:
Note: We do not need to consider n = 0 (trivial eigenfunction).

## Slide 27
Application: Transmission Line (cont.)
We then have:
where

## Slide 28
Application: Transmission Line (cont.)
The final solution is then:

## Slide 29
Summary
Application: Transmission Line (cont.)
Method 1
Method 2

## Slide 30
Application: Transmission Line (cont.)
Other possible Green’s functions for the transmission line:
We solve for the Green’s function that gives us the current I (z) due to the 1A parallel current source.
We solve for the Green’s function giving the voltage due a 1V series voltage source instead of a 1A parallel current source.
We solve for the Green’s function giving the current to due a 1V series voltage source instead of a 1A parallel current source.

## Slide 31: Cavity Model for Patch Antenna
Next we use the cavity model and the method of eigenfunction expansion to solve for the input impedance of the rectangular microstrip patch antenna.
I0 current feed at (x0, y0)

## Slide 32: Cavity Model
Note:
L is often chosen from Hammerstad’s formula.
W is often chosen from Wheeler’s formula.
Note: The coordinates (x0, y0) are measured from the corner of the physical patch.
Accounting for fringing:
(Wheeler formula)
(Hammerstad formula)
PMC
PEC
Physical patch

## Slide 33: Cavity Model (cont.)
Assume no z variation (the probe current is constant in the z direction.)
PMC
PEC
Accounting for loss and radiation:

## Slide 34: Cavity Model (cont.)
CAD Formulas for Q Factors*
where
*Derived in ECE 6345.

## Slide 35: Cavity Model (cont.)
CAD Formulas for Q Factors (cont.)

## Slide 36: Helmholtz Equation for Ez
We first derive the Helmholtz equation for Ez.
Substituting Faraday’s law for H into Ampere’s law, we have

## Slide 37
Hence
Denote
Then
Feed (impressed) current
Helmholtz Equation for Ez (cont.)
We take it here to be a filamentary source (zero radius).

## Slide 38: Mathematical Problem
The function  is really a 2-D Green’s function, if the feed current is filamentary.

## Slide 39: Eigenvalue Problem
Eigenvalue problem:
The original eigenvalue problem is thus reduced to this simpler “reduced” eigenvalue problem.
New notation:

## Slide 40
Introduce eigenfunctions of the 2-D Laplace operator:
For a rectangular patch we have, from separation of variables (or guessing),
Note:
The eigenvalues are real and the eigenvalues are orthogonal.
Eigenvalue Problem (cont.)

## Slide 41: Eigenfunction Expansion
Assume an “eigenfunction expansion”:
Hence
Using the properties of the eigenfunctions, we have
This must satisfy

## Slide 42
Note that the eigenfunctions are orthogonal, so that
Define
Multiply the previous equation by and integrate.
We then have
Note: The eigenfunctions are real, so we can drop the conjugate here if we want.
Eigenfunction Expansion (cont.)

## Slide 43
Hence, we have (removing the primes in the notation)
Recall:
The field inside the patch cavity is then given by
Eigenfunction Expansion (cont.)
so

## Slide 44
For the rectangular patch:
where
We need:
Eigenfunction Expansion (cont.)

## Slide 45
so
Eigenfunction Expansion (cont.)

## Slide 46
For a filamentary feed current we have:
Eigenfunction Expansion (cont.)
Hence, we have

## Slide 47
The final form for the field inside the patch cavity is then given by:
Eigenfunction Expansion (cont.)

## Slide 48
Substituting in for all of the terms, we have:
Note: It is not obvious, but the field goes to infinity when
Final Field Inside Cavity
Note:
It is usually the (1,0) mode that is resonant.

## Slide 49
Using the Green's function notation, we have (setting I0 = 1):
Green’s Function
For an arbitrary impressed current excitation inside the cavity, we then have:

## Slide 50: Input Impedance
To calculate the input impedance, we need to consider a nonzero radius of the feed probe.
Note: Because the probe is made of PEC, there is a surface current on it.
Feed probe

## Slide 51
We first calculate the electric field Ez inside the patch cavity due to the probe.
It is convenient to use a strip model of the probe.
Input Impedance (cont.)

## Slide 52
For a “Maxwell” strip current assumption, we have:
Note: The total probe current is I0 amps.
Input Impedance (cont.)

## Slide 53
For a uniform strip current assumption, we have:
Note: The total probe current is I0 amps.
Input Impedance (cont.)
(We will use this model.)

## Slide 54
Input Impedance (cont.)
(arbitrary impressed volumetric current in cavity)
(arbitrary impressed surface current on a contour)
(strip current)
(uniform strip current model)
Terms that need to be integrated
Field inside cavity due to probe:

## Slide 55
Input Impedance (cont.)
Integrates to zero (odd)
Integration over the strip current:

## Slide 56
Input Impedance (cont.)
The field inside the cavity due to the strip probe current is then:
We next use the field inside the cavity to find the input impedance. We first calculate the complex power going into the patch, which is the complex power radiated by the probe current.

## Slide 57
Input Impedance (cont.)
We need this integral:

## Slide 58
The final result is:
Note:
We cannot assume a probe of zero radius,
or else the series will not converge – the input reactance will be infinite.
Input Impedance (cont.)

## Slide 59
Circuit Model
(1,0 mode resonator)
Probe (feed) inductance
(accounts for all modes (m,n)  (1,0))
Resonance frequency:
This formula, which describes the above circuit model, comes from approximating the input impedance formula. (Please see Appendix B.)

## Slide 60
Results
Patch
Feed
Freq. (GHz)
Freq. (GHz)
Freq. (GHz)
Zin ()
Zin ()
Zin ()

## Slide 61
Appendix A
Allow for distributed sources
v+
v -
+
-
+
-
z
i+
i-
This appendix presents a derivation of the telegrapher’s equations with distributed sources.

## Slide 62
Appendix A (cont.)

## Slide 63
Appendix A (cont.)

## Slide 64
In the phasor domain:
Appendix A (cont.)

## Slide 65: Appendix B
We can write each (m,n) term of the series for Zin as:
where

## Slide 66
or
Next, use:
  Also, define
Appendix B (cont.)

## Slide 67
Then
or
Appendix B (cont.)

## Slide 68
For , we have:
This is the formula for the input impedance of a parallel RLC circuit.
(This justifies the RLC model near resonance.)
Appendix B (cont.)
All of the non-resonant terms in the infinite series for Zin (m, n  1,0) are slowing varying near the resonance frequency of the (1,0) mode, and are nearly imaginary, and can thus get lumped together into a “probe reactance” term.