## Slide 1: The Function Generator and the Oscilloscope
Dr. Len Trombetta
ECE 2100

## Slide 2: Sinusoid Basics
General form of the sinusoid:
v(t) = Vm sin(2pf t + f) [V]
Vm is the amplitude
f is the frequency
f is the phase
2Vm = Vpp (peak-to-peak)
t
We usually write w = 2pf, and w is the angular frequency. But note that what you set on the function generator is f, not w.
v(t)
Vm
Vpp
In the ECE curriculum, you will be using sinusoids…EVERYWHERE!

## Slide 3: Sinusoid Basics
A sinusoid may also have a dc offset.
v(t) = Vm sin(2pf t) [V] + Vdc
v(t)
t
Vdc
0

## Slide 4: Function Generator
Power
Let’s explore basic function generator properties...

## Slide 5: Displays and Output
The frequency will be displayed here…
…and the amplitude here.
You won’t get an output until you press “Output”.
BNC to BNC
We connect Output to the oscilloscope using a BNC-to-BNC cable.
scope

## Slide 6: Amplitude
Use the keypad and the Vpp button…
…or…
…the wheel and the “ten’s place” buttons.
To adjust the amplitude:
v(t)
Vm
t
v(t) = Vm sin(2pf t) [V]

## Slide 7: Frequency
Use the keypad and the Hz, kHz, or MHz button…
…or…
…the wheel and the “ten’s place” buttons.
To adjust the frequency:
v(t)
t
T
v(t) = Vm sin(2pf t) [V]
T = 1/f

## Slide 8: Waveform (Function)
A ramp with a 50% asymmetry is a triangle wave…

## Slide 9: Oscilloscope
From Function Generator
Power
The oscilloscope displays input signal as voltage vs. time.
voltage
time
(You don’t have these inputs.)

## Slide 10: Home Depot Theory Revisited
The FG and the OScope have tons of features, many of which we will not need in this course. You may never use some of them, but you never know, so…
Based on the Home Depot Theory of lab practice, you should explore these features on your own so that you know what’s available.

## Slide 11: Activity
Connect the function generator to the oscilloscope input channel 1 using a BNC-to-BNC cable. Press “Default Setup”, and “Channel 1”. You may or may not get a reasonable display… let’s explore further.
Default Setup
Channel 1

## Slide 12: Activity
Make sure the Offset is 0.
You won’t get an output until you press “Output”.
scope
You may still not get a reasonable display…

## Slide 13: Scale Factors
Vertical scale factor (in Volts/Div)
Horizontal scale factor (in sec/Div)
f = 1/T
T
20 mV/
500 uS/
Vpp
scale factor adjustments
You may have to adjust your horizontal and vertical scale factors to get a good “picture”.

## Slide 14: Activity
4. Calculate the period from the frequency set on the FG. Convince yourself that the signal frequency and amplitude are those stated on the function generator display.
2. Adjust the horizontal and vertical scale factors so that you get a reasonable display – something easy to look at!
T
20 mV/
500 uS/
Vpp
1. Set the function generator for a 60 [kHz] sinusoid with an amplitude of 1.5 [V].
3. Change the scale factors to see how the display is changed on the ‘scope.

## Slide 15: dc Offset
Use the keypad and the Vpp button…
…or…
…the wheel and the “ten’s place” buttons.
To adjust the offset: be sure the instrument displays “Offset” and not “LoLevel”.
v(t)
t
v(t) = Vm sin(2pf t) [V] + Vdc
Vdc
0

## Slide 16
Does your scope reflect the new signal? That depends on “coupling”…
Set a 1.0 [V] offset on your function generator.
v(t)
t
Vdc
0
Activity

## Slide 17: Coupling
Whether or not you observe the dc component on the scope depends on the coupling.
1. Select whichever channel your signal is connected to.
2. Toggle through the coupling options:
dc: dc AND ac components are displayed.
ac: only the ac component is displayed.
coupling options

## Slide 18: Still not getting a good picture???
This is a “triggering” problem. We’ll cover this at a later date. For now…
Use the Magic Button

## Slide 19: For Lab III…
You’ll want to know about a few things to do Lab IV:
T-Connector
The Op Amp (operational amplifier): You’ll learn about this in Electronics (ECE 3355/3155)
RMS values: an alternative measure of amplitude

## Slide 20: The “T” Connector
output connected to BNC “T”
The three BNC connectors are in parallel, effectively providing two FGEN outputs. Typically one will go to the scope and the other will be your circuit input.
scope
circuit input

## Slide 21: For Lab IV you will need to wire an Op Amp:
LM741: a generic operational amplifier. This figure is from the data sheet, which we will take a look at in class.

## Slide 22: The Op Amp
The op amp has certain limitations:
It will not output currents larger than about 20 [mA].
This will not be a problem for Lab IV because the output current will be less than that value.
There is a limitation on how high a frequency you can apply to the input and still get an output.
This will not be a problem in Lab IV for parts 1 – 9. However, in part 10 we will explore this issue using a LabVIEW .vi to perform a frequency sweep, and to measure the op amp output as a function of frequency.

## Slide 23: Triggering
We will go into more detail later but for now, to get a stable trace:
1. Press the input channel you’re using; press Trigger.
2. Source: Whatever channel you’re using to input
3. Trigger Type: Edge
4. Adjust trigger level knob for a stable trace.
Trigger
Trigger Level

## Slide 24: Triggering 101
When the oscilloscope is properly triggered, the image is “stable” because it is displayed the same way each time it sweeps across the screen. If the triggering is not correct, the image looks garbled , like it is “running” across the screen.
Trigger Menu
Trigger Level

## Slide 25: External Triggering
An external trigger signal is provided by the SYNC output of the function generator. This provides a square wave of 1Vpp amplitude at the frequency of the MAIN waveform. So as long as your signal is coming from MAIN, the scope knows exactly when to trigger!
SYNC