## Slide 1: ECE 2201 Circuit Analysis I
Lecture Set #4
The Node-Voltage Method
Version 13
Dr. Dave Shattuck
Associate Professor, ECE Dept.

## Slide 2: The Node Voltage Method

## Slide 3: Overview of this Part
In this lecture set, we will cover the following topics:
Some basic definitions
The steps for writing the Node-Voltage Equations
Tips on picking the best reference node
How to handle dependent sources
Notes: You can click on the blue text to jump to the subject that you want to learn about now.

## Slide 4: Textbook Coverage
This material is covered in your textbook in the following sections:
Electric Circuits 10th Ed. by Nilsson and Riedel: Sections 4.1 through 4.3
Notes: You should also read these sections in your text. This material is intended to complement your textbook coverage, not replace it.

## Slide 5: Some Basic Definitions
Node – a place where two or more components meet
Essential Node – a place where three or more components meet
Reference Node – a special essential node that we choose as a reference point for voltages
You may be familiar with the word node from its use as a location in computer networks. It has a similar meaning there, a place where computers are connected.
Review Nodes
Skip Review of Nodes

## Slide 6: Some Review – Nodes
A node is defined as a place where two or more components are connected.
The key thing to remember is that we connect components with wires. It doesn’t matter how many wires are being used; it only matters how many components are connected together.
How many nodes are there in this circuit here?

## Slide 7: How Many Nodes – Correct Answer
In the example circuit schematic given here, there are three nodes. These nodes are shown in dark blue here.
Some students count more than three nodes in a circuit like this. When they do, it is usually because they have considered two points connected by a wire to be two nodes.
There are also three essential nodes. Each of these three nodes has at least 3 components connected to it.
Notes: The nodes are the darker blue shapes. The shape is unimportant to us; we can draw the circuit in many ways. The key here, for example, is that a voltage source, a current source, and a resistor called RF are connected to the bottom node.

## Slide 8: How Many Nodes – Wrong Answer
In the example circuit schematic given here, the two red nodes are really the same node. There are not four nodes.
Remember, two nodes connected by a wire were really only one node in the first place.
Wire connecting two nodes means that these are really a single node.
Notes: Remember, two nodes connected by a wire were not really two nodes at all. It is all one node.

## Slide 9: The Node-Voltage Method (NVM)
The Node-Voltage Method (NVM) is a systematic way to write all the equations needed to solve a circuit, and to write just the number of equations needed. The idea is that any other current or voltage can be found from these node voltages.
This method is not that important in very simple circuits, but in complicated circuits it gives us an approach that will get us all the equations that we need, and no extras.
It is also good practice for the writing of KCL and KVL equations. Many students believe that they know how to do this, but make errors in more complicated situations. Our work on the NVM will help correct some of those errors.
The Node-Voltage Method is a system. And like the sprinkler system here, the goal is be sure that nothing gets missed, and everything is done correctly. We want to write all the equations, the minimum number of equations, and nothing but correct equations.

## Slide 10: The Node-Voltage Method (NVM)
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
We will explain these steps by going through several examples.
Review KCL Equations
Skip KCL Review

## Slide 11: Kirchhoff’s Current Law (KCL) – a Review
The algebraic (or signed) summation of currents through any closed surface must equal zero.
For this set of material, we will always assign a positive sign to a term that refers to a reference current that leaves a closed surface, and a negative sign to a term that refers to a reference current that enters a closed surface.

## Slide 12: Kirchhoff’s Current Law (KCL) – a Review Example
For this set of material, we will always assign a positive sign to a term that refers to a current that leaves a node, and a negative sign to a term that refers to a current that enters a node.
In this example, we have already assigned reference polarities for all of the currents for the nodes indicated in darker blue.
For this circuit, and using my rule, we have the following equation:
Notes: The node that we are using here is highlighted in darker blue.

## Slide 13: NVM – 1st Example
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
For most students, it seems to be best to introduce the NVM by doing examples. We will start with simple examples, and work our way up to complicated examples. Our first example circuit is given here.

## Slide 14: NVM – 1st Example – Step 1
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
We need to find all the essential nodes, and only the essential nodes. How many are there?
Notes: Answer this question before going to the next slide.

## Slide 15: NVM – 1st Example – Step 1(Done)
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
There are three essential nodes, each of which is shown in red on the diagram below.

## Slide 16: NVM – 1st Example – Step 2
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
We could choose any of the three essential nodes as the reference node. However, there are better choices. Remember that we need to write a KCL equation for each essential node, except for the reference node. The best idea, then, is to pick the node with the most connections, to eliminate the most difficult equation. Here this is the bottom node. It is labeled to show that it is the reference node.
This symbol is used to designate the reference node. There are different symbols used for this designation. This choice of symbols is not important. Making a designation is important.

## Slide 17: NVM – 1st Example – Step 2 Note
Among the symbols that you might see to designate the reference node are the ones shown below. The choice we use is the one used in most textbooks.
Actually, each of these symbols has a specific meaning in a formal circuit schematic. However, for our purposes here, the distinction is not important.
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.

## Slide 18: NVM – 1st Example – Step 3
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
We have defined the node voltages, vA and vB. They are shown in red. For clarity, we have also named the nodes themselves, A and B.
Note: As with any voltage, the polarity must be defined. We have defined the voltages by showing the voltages with a “+” and “-” sign for each. Strictly speaking, this should not be necessary. The words in step 3 make the polarity clear. Some texts do not label the voltages on the schematic. For clarity, we will label the voltages in these notes.

## Slide 19: NVM – 1st Example – Step 4, Part 1
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
Now, we need to write a KCL equation for each non-reference essential node. That means an equation for A and one for B. Let’s start with A. The equation is:

## Slide 20: NVM – 1st Example – Step 4, Part 2
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
Now, we need to write a KCL equation for each non-reference essential node. That means an equation for A and one for B. Let’s start with A. The equation is:

## Slide 21: NVM – Currents Explained 1
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
The first term comes from Ohm’s Law. The voltage vA is the voltage across R1. Thus, the current shown in green is vA/R1, out of node A, and thus has a + sign in this equation.

## Slide 22: NVM – Currents Explained 2
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
The current through the current source is, by definition, given by the value of that current source. Since the reference polarity of the current is entering node A, it has a “-” sign.

## Slide 23: NVM – Currents Explained 3
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
This current expression also comes from Ohm’s Law. The voltage vX is the voltage across the resistor R2, and results in a current in the polarity shown.
To prove to yourself that vX = vA – vB, take KVL around the loop shown. The voltage at A with respect to B, is vA – vB, where vA and vB are both node voltages.

## Slide 24: NVM – 1st Example – Step 4, Part 3
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
The KCL equation for the A node was:
The KCL equation for the B node is:
Be very careful that you understand the signs of all these terms. One of the big keys in these problems is to get the signs correct. If you have questions, review this material.

## Slide 25: NVM – 1st Example – Step 4 – Notes
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
Some notes that may be helpful:
We are actually writing KCL for the closed surfaces shown. You might want to actually sketch in your diagrams a closed surface like this, so that you don’t miss any currents.
When we write these equations using the conventions we picked, the A node equation has a positive sign associated with all the terms with vA, and a negative sign with all other node-voltage terms. This is a good way to check your equations.

## Slide 26: NVM – 1st Example – Step 5
The Node-Voltage Method steps are:
Find the essential nodes.
Define one essential node as the reference node.
Define the node voltages, at the essential nodes with respect to the reference node. Label them.
Apply KCL for each non-reference essential node.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
There are no dependent sources in this circuit, so we can skip step 5. We should now have the same number of equations (2) as unknowns (2), and we can solve.
Note that we have assumed that all the values of the resistors and sources have been given. If not, we will need to get more information before we can solve.

## Slide 27: NVM – 2nd Example
Our second example circuit is given here. Numerical values are given in this example. Let’s find the current iX shown, using the Node-Voltage Method.

## Slide 28: NVM – 2nd Example – Step 1
We have 4 essential nodes. We marked them in red in this slide, but will not mark them in the slides that follow. On your diagrams, you can always draw them. Remember that two nodes connected by a wire were really only one node.

## Slide 29: NVM – 2nd Example – Step 2
We have chosen the bottom right node as the reference node. This choice is a reasonable one, since it has 5 components connected to it, more than any other essential node.

## Slide 30: NVM – 2nd Example – Step 3
We have defined the three node voltages. Note that each node voltage is the voltage at the essential node with respect to the reference node.

## Slide 31: NVM – 2nd Example – Step 4
Now, we write KCL equations for nodes A, B, and C. These are given here. We have labeled each equation with the name of the node for which it was written.

## Slide 32: NVM – 2nd Example – Step 5
Hopefully, it is now clear why we needed step 5. Until this point, we have 3 equations and 5 unknowns. We need two more equations.
We get these equations by writing equations for iX and vX, using KCL, KVL and Ohm’s Law, and using the node-voltages already defined. If we have to define new variables, it will mean we need more equations. Let’s write the two equations we need:
Now, we have 5 equations and 5 unknowns.

## Slide 33: NVM – 2nd Example – Solution
We have the following equations.

## Slide 34: How many node-voltage equations do I need to write?
This is a very important question. It is a good idea to figure this out before beginning a problem. Then, you will know how many equations to write before you are done.
The fundamental rule is this: If there are ne essential nodes, you need to write ne-1 equations. Remember that one essential node is the reference node, and we do not write a KCL equation for the reference node.
If there are dependent sources present, then the number of equations has to increase. In general, each dependent source introduces a variable which is unknown. If v is the number of variables that dependent sources depend on, then you need to write ne -1+v equations.
Go back to Overview slide.

## Slide 35: What do we do when we have voltage sources?
This is another important question. In general, a voltage source requires some special attention, since the current through it depends entirely on what it is connected to.
We will develop a set of plans for dealing with this situation. We will lay out these plans in the next set of lecture notes.
Go back to Overview slide.