## Slide 1: ECE 2201 Circuit Analysis
Lecture Set #6
The Mesh-Current Method
Version 21
Dr. Dave Shattuck
Associate Professor, ECE Dept.

## Slide 2: Mesh-Current Method

## Slide 3: Overview
In this lecture set, we will cover the following topics:
Some basic definitions
The steps for writing the Mesh-Current Equations
How to handle dependent sources
Notes: You can click on the blue text to jump to the subject that you want to learn about now.

## Slide 4: Textbook Coverage
This material is covered in your textbook in the following sections:
Electric Circuits 8th Ed. by Nilsson and Riedel: Sections 4.1, & 4.5 through 4.8
Notes: You should also read these sections in your text. This material is intended to complement your textbook coverage, not replace it.

## Slide 5: Some Basic Definitions
Closed Path – a closed loop which follows components and wires. This definition effectively defines paths as following components and wires.
Mesh – a closed path that does not enclose any other closed paths
Planar Circuit – a circuit that can be drawn in a plane, that is, without wires that cross without touching
Different textbooks use slightly different definitions for these terms. If the difference is confusing, stick with your book. The key is to be able to find meshes, and most students find this to be fairly easy with practice.

## Slide 6: Some Review – Closed Loops
A closed loop can be defined in this way: Start at any node and go in any direction and end up where you start. This is a closed loop.
Note that this loop does not have to follow components and wires. It can jump across open space. Often we will follow components, but we will also have situations where we need to jump between nodes that have no connections.

## Slide 7: How Many Closed Loops – Infinity?
How many closed loops are there in this circuit? This is actually a kind of trick question. The way we have defined closed loops here, the answer is that there are an infinite number of ways to draw closed loops.
Rather, we should ask how many closed paths are there following the elements shown?
Notes: Think about your answer before going on to the next slide.

## Slide 8: How Many Closed Paths? – 6
How many closed paths are there following the elements shown?
The answer is 6.
We will show the closed paths on the following slides. Note which are meshes and which are not meshes.

## Slide 9: Closed Path #1
Here is closed path #1. It is shown in red.
It does not enclose any other closed paths. This is a mesh.

## Slide 10: Closed Path #2
Here is closed path #2. It is shown in red.
It does enclose another closed path. (In fact, it encloses three meshes.) This is not a mesh.

## Slide 11: Closed Path #3
Here is closed path #3. It is shown in red.
It does not enclose any other closed paths. This is a mesh.

## Slide 12: Closed Path #4
Here is closed path #4. It is shown in red.
It does not enclose any other closed paths. This is a mesh.

## Slide 13: Closed Path #5
Here is closed path #5. It is shown in red.
It does enclose another closed path (in fact, two). This is not a mesh.

## Slide 14: Closed Path #6
Here is closed path #6. It is shown in red.
It does enclose another closed path (in fact, it encloses two). This is not a mesh.
In summary, we have three meshes in this circuit.

## Slide 15: The Mesh-Current Method (MCM)
The Mesh-Current Method (MCM) is a systematic way to write all the equations needed to solve a circuit, and to write just the number of equations needed. It only works with planar circuits. The idea is that any other current or voltage can be found from these mesh-currents.
This method is not that important in very simple circuits, but in complicated circuits it gives us an approach that will get us all the equations that we need, and no extras.
It is also good practice for the writing of KCL and KVL equations. Many students believe that they know how to do this, but make errors in more complicated situations. Our work on the MCM will help correct some of those errors.
The Mesh-Current Method is a system. Like the sewer system here, the goal is be sure that everything is collected correctly. We want to write all the equations, the minimum number of equations, and nothing but correct equations. (However, we don’t want to smell as bad!)

## Slide 16: The Steps in the Mesh-Current Method (MCM)
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary. (If we cannot do this, we cannot use the MCM.)
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
We will explain these steps by going through several examples.
Review KVL Equations
Skip KVL Review

## Slide 17: Kirchhoff’s Voltage Law (KVL) – a Review
The algebraic (or signed) summation of voltages around a closed loop must equal zero. Since a mesh is a closed loop, KVL will hold for meshes.
For this set of material, we will always go around loops clockwise. We will assign a positive sign to a term that refers to a reference voltage drop, and a negative sign to a term that refers to a reference voltage rise.

## Slide 18: Kirchhoff’s Voltage Law (KVL) – an Example
For this set of material, we will always go around loops clockwise. We will assign a positive sign to a term that refers to a voltage drop, and a negative sign to a term that refers to a voltage rise.
In this example, we have already assigned reference polarities for all of the voltages for the loop indicated in red.
For this circuit, and using our rule, starting at the bottom, we have the following equation:

## Slide 19: Kirchhoff’s Voltage Law (KVL) – Notes
For this set of material, we will always go around loops clockwise. We will assign a positive sign to a term that refers to a voltage drop, and a negative sign to a term that refers to a voltage rise.
Some students like to use the following handy mnemonic device: Use the sign of the voltage that is on the side of the voltage that you enter. This amounts to the same thing.
As we go up through the voltage source, we enter the negative sign first. Thus, vA has a negative sign in the equation.

## Slide 20: MCM – 1st Example
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
For most students, it seems to be best to introduce the MCM by doing examples. We will start with simple examples, and work our way up to complicated examples. Our first example circuit is given here.

## Slide 21: MCM – 1st Example – Step 1
We need to redraw the circuit in planar form. This means that if we have any wires which are crossing without being connected, we need to move components around. This moving must not change any connections. We do this until all crossings are gone. If we cannot do this, we cannot use the MCM.
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
This circuit is already drawn in planar form. We can skip step 1 with this circuit.

## Slide 22: MCM – 1st Example – Step 2
We have assumed that it will be easy for you to identify the meshes in a circuit. Most students find this to be easy. They look for what some call “window panes” in the circuit. In this circuit, there are three meshes. We define the mesh currents by labeling them, showing the polarity using an arrow.
This symbol is used to designate the mesh current. We will choose a reference polarity which is clockwise in this material, but the choice is arbitrary.
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.

## Slide 23: MCM – 1st Example – Step 2 Note
A mesh current is thought of as a current that flows only around that mesh. The idea is that of charges which flow only in that subcircuit. In places where the meshes come together, both mesh currents flow simultaneously. In resistor R1, two mesh currents, iA and iB, are flowing.
Some students ask whether mesh currents are real, or whether they exist. This depends upon your definition. If you define something as being real if you can measure it, then mesh currents are not real. The mesh current iB in this circuit can not be measured directly.
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
Notes: {Note: it would be good if the mesh current arrows (the three red circular arrows) were animated in this slide.}

## Slide 24: Mesh Currents Aren’t Real???
Please don’t let the issue of the reality of mesh currents bother you. One can debate whether they exist or not, but it is a moot point. It doesn’t matter whether they exist or not.
We can use them to find real answers. That is all that matters.
Think for a moment about the square root of minus one, or j, where
There is no square root of negative numbers. There is no doubt that j does not exist, no doubt that it is imaginary. Still, we use it to solve for real answers. It is a tool. It does not matter whether it exists or not.

## Slide 25: MCM – 1st Example – Step 3 – Part 1
Now, we need to write a KVL equation for each mesh. That means three equations. Let’s start with mesh A. The equation is:
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
Do each of these voltage terms make sense? If not, go here to have them explained. If all four terms are clear to you, skip this explanation.

## Slide 26: Step 3 – Part 1 – Explanation
Let’s make sure that we understand where this equation comes from. As we go around the closed path that is the mesh, we have four voltages. Using Ohm’s Law, we can show that the voltages across the resistors are functions of the currents through them.
Notes: {Note: it would be good if the mesh current arrows (the three red circular arrows) were animated in this slide.}

## Slide 27: Step 3 – Part 1 – Explanation 2
Here, we have labeled the branch currents and voltages for each term of the equation. A branch current is the current in the component, which is the summation of the mesh currents that go through that branch, being careful about the signs. Note that in this circuit, i2 = iA, i1 = (iA - iB), and i5 = iA.
Notes: {Note: it would be good if the mesh current arrows (the three red circular arrows) were animated in this slide.}

## Slide 28: MCM – 1st Example – Step 3 – Part 2
Next, let’s write a KVL for mesh B. The equation is:
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.

## Slide 29: MCM – 1st Example – Step 3 – Part 3
Finally, we write a KVL equation for mesh C. The equation is:
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.

## Slide 30: MCM – 1st Example – Step 3 – Notes
Some notes that may be helpful:
We have named the meshes for the mesh currents that are in them.
When we write these equations using the conventions we picked, the A mesh equation has a positive sign associated with all the terms with iA, and a negative sign with all other mesh-current terms. This is a good way to check your equations.
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.

## Slide 31: MCM – 1st Example – Step 4
There are no dependent sources in this circuit, so we can skip step 4. We should now have the same number of equations (3) as unknowns (3), and we can solve.
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary.
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
Note that we have assumed that all the values of the resistors and sources have been given. If not, we need more information before we can solve.

## Slide 32: MCM – 2nd Example
Our second example circuit is given here. Numerical values are given in this example. Let’s find the current iX shown, using the Mesh-Current Method.

## Slide 33: MCM – 2nd Example – Step 1
This circuit is already drawn in planar form, so we may skip step 1.

## Slide 34: MCM – 2nd Example – Step 2
We have defined the mesh currents for the three meshes in this circuit. As is our practice, we have defined them to be clockwise.

## Slide 35: MCM – 2nd Example – Step 3
Now, we write KVL equations for nodes A, B, and C. These are given here. We have labeled each equation with the name of the mesh for which it was written.

## Slide 36: MCM – 2nd Example – Step 4
Hopefully, it is now clear why we needed step 4. Until this point, we have 3 equations and 5 unknowns. We need two more equations.
Now, we have 5 equations and 5 unknowns.
We get these equations by writing equations for iX and vX, using KCL, KVL and Ohm’s Law, and using the mesh currents already defined. Let’s write the two equations we need:

## Slide 37: MCM – 2nd Example – Solution
We have the following equations.

## Slide 38: How many mesh-current equations do I need to write?
This is a very important question. It is a good idea to figure this out before beginning a problem. Then, you will know how many equations to write before you are done.
The fundamental rule is this: If there are nm meshes, you need to write nm equations. Remember that we write a KVL equation for each mesh.
If there are dependent sources present, then the number of equations has to increase. In general, each dependent source introduces a variable which is unknown. If v is the number of variables that dependent sources depend on, then you need to write nm+v equations.
Go back to Overview slide.

## Slide 39: What do we do when we have current sources?
This is another important question. In general, a current source requires some special attention, since the voltage across it depends entirely on what it is connected to.
We will develop a set of plans for dealing with this situation. We will lay out these plans in the next part.
Go back to Overview slide.

## Slide 40: Mesh-Current Method with Current Sources

## Slide 41: Overview of this Part
In this part, we will cover the following topics:
Current sources in the Mesh-Current Method
Current sources as a part of one mesh
Current sources as a part of two meshes
Notes: You can click on the blue text to jump to the subject that you want to learn about now.

## Slide 42: Textbook Coverage
This material is covered in your textbook in the following sections:
Electric Circuits 8th Ed. by Nilsson and Riedel: Section 4.7
Notes: You should also read these sections in your text. This material is intended to complement your textbook coverage, not replace it.

## Slide 43: The Steps in the Mesh-Current Method (MCM)
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary. (If we cannot do this, we cannot use the MCM.)
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
We will explain these steps by going through several examples.

## Slide 44: Current Sources and the MCM
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary. (If we cannot do this, we cannot use the MCM.)
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.
A problem arises when using the MCM when there are current sources present. The problem is in Step 3. The voltage across a current source can be anything; the voltage depends on what the current source is connected to. Therefore, it is not clear what to write for the KVL expression. We could introduce a new voltage variable, but we would rather not introduce another variable. In addition, if all we do is directly write KVL equations, we cannot include the value of the current source.

## Slide 45: Current Sources and the MCM – Solution
The solution for what to do when there is a current source present depends on how it appears. There are two possibilities. We will handle each of them in turn. The two possibilities are:
A current source as a part of only one mesh
A current source as a part of two meshes
The Mesh-Current Method steps are:
Redraw the circuit in planar form, if necessary. (If we cannot do this, we cannot use the MCM.)
Define the mesh currents, by labeling them. This includes showing the polarity of each mesh current.
Apply KVL for each mesh.
Write an equation for each current or voltage upon which dependent sources depend, as needed.

## Slide 46: MCM – Current Source as a Part of Only One Mesh
Again, it seems to be best to study the MCM by doing examples. Our next example circuit is given here. We will go through the entire solution, but our emphasis will be on step 3. Note that here the current sources iS1 and iS2 are each a part of only one mesh.

## Slide 47: MCM – Current Source as a Part of Only One Mesh – Step 1
The first step is to redraw the circuit in planar form. This circuit is already in planar form, and this step can be skipped for this circuit.

## Slide 48: MCM – Current Source as a Part of Only One Mesh – Step 2
The second step is to define the mesh currents. This has been done in the circuit below.

## Slide 49: MCM – Current Source as a Part of Only One Mesh – Step 3 – Part 1
The third step is to write KVL for meshes A, B, C, and D. We can write KVL equations for meshes B and C using the techniques we have already, but for A and D we will get into trouble since the voltages across the current sources are not known, and cannot be easily given in terms of the mesh currents.

## Slide 50: MCM – Current Source as a Part of Only One Mesh – Step 3 – Part 2
We can write KVL equations for meshes B and C using the techniques we had already, but for meshes A and D we will get into trouble. However, we do know something useful; the current sources determine each of the mesh currents in meshes A and D. This can be used to get the equations we need.

## Slide 51: MCM – Current Source as a Part of Only One Mesh – Step 3 – Part 3
We can write the following equations:
These equations indicate that the mesh current iA is equal to the current source iS1, and that the mesh current iD is equal to but opposite in sign of the current source iS2. Take care about the signs in these equations.

## Slide 52: MCM – Current Source as a Part of Only One Mesh – Step 4
There are no dependent sources here, so we are done.

## Slide 53: MCM – Current Source as a Part of Two Meshes
Again, it seems to be best to study the MCM by doing examples. Our next example circuit is given here. We will go through the entire solution, but our emphasis will be on step 3. Note that here the current source iS is a part of two meshes.

## Slide 54: MCM – Current Source as a Part of Two Meshes – Steps 1 and 2
Since we have done similar circuits already, we have completed steps 1 and 2 in this single slide. It was already drawn in planar form. We defined three mesh currents.

## Slide 55: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 1
Now we want to write KVL equations for the three meshes, A, B, and C. However, we will have difficulties writing the equations for meshes B and C, because the current source can have any voltage across it. In addition, we note that iS is not equal to iB, nor to -iB, nor is it equal to iC.

## Slide 56: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 2
We are going to take a very deliberate approach to this case, since many students find it difficult. To start, we will assume that we were willing to introduce an additional variable. (We will later show that we do not have to, but this is just to explain the technique.) We define the voltage across the current source to be vX.

## Slide 57: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 3
Now, we can write KVL equations for meshes B and C, using vX.

## Slide 58: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 4
Now, remember that we did not want to use the variable vX. If we examine the equations that we have just written, we note that we can eliminate vX by adding the two equations together. We add the B equation to the C equation, and get:

## Slide 59: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 5
Next, we examine this new equation that we have titled B+C. If we look at the circuit, this is just KVL applied to a closed path that surrounds the current source. The correspondence between voltages and KVL terms is shown with colors.

## Slide 60: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 6
The large closed path that includes the current source is called a Supermesh. We will call the KVL equation that we write for this closed path a Supermesh Equation.
Supermesh
Supermesh Equation

## Slide 61: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 7
The Supermesh Equation is fine, but it is not enough. With the equation for mesh A, and for variable iX, we still only have three equations, and four unknowns. We need one more equation.
Supermesh
Supermesh Equation

## Slide 62: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 8
We need one more equation. We now note that we have not used the value of the current source, which we expect to influence the solution somehow. Note that the current source determines the difference between iB and iC.

## Slide 63: MCM – Current Source as a Part of Two Meshes – Step 3 – Part 9
The current source determines the difference between iB and iC. We can use this to write the fourth equation we need. We write the following equation.

## Slide 64: MCM – Current Source as a Part of Two Meshes – Steps 3&4 – Part 10
To complete the set of equations, we write the KVL equation for mesh A, and an equation for variable iX. That gives us four equations in four unknowns, or

## Slide 65: MCM – Current Source as a Part of Two Meshes – Steps 3&4 – Part 11
To summarize our approach then, when we have a current source as a part of two meshes, we will
write one equation applying KVL to a supermesh around the current source, and
write an equation using the current source to relate the two mesh currents.

## Slide 66: MCM – Current Source as a Part of Two Meshes – Steps 3&4 – Part 12
Constraint Equation
Supermesh Equation
We write:
one equation applying KVL to a supermesh around the current source, and
one equation using the current source to relate the two mesh currents.

## Slide 67: How many mesh-current equations do we need to write?
This has not changed. The presence or absence of current sources does not change the rules about the number or equations. In addition, it does not matter whether the current sources are dependent or independent.
The fundamental rule is this: If there are nm meshes, you need to write nm equations.
If there are dependent sources present, then the number of equations has to increase. In general, each dependent source introduces a variable which is unknown. If v is the number of variables that dependent sources depend on, then you need to write nm+v equations.
Go back to Overview slide.
Go to next notes slide.

## Slide 68: What do we do when we have current sources?
Our steps when we have current sources depend on how the current sources appear.
If the current source is a part of only one mesh, we set that mesh current equal to the current source, being careful about the polarity.
If the current source is a part of two meshes, we
  write a supermesh equation using a closed path around the source (supermesh equation), and
  write an equation using the current source and the two mesh currents (constraint equation).
Go back to Overview slide.

## Slide 69
Example Problem: Use the mesh-current method to write a set of equations that could be used to solve the circuit below. Do not attempt to simplify the circuit. Do not attempt to solve the equations.