## Slide 1: ECE 2201 Circuit Analysis
Lecture Set #7
Source Transformations
Version 18
Dr. Dave Shattuck
Associate Professor, ECE Dept.

## Slide 2: Overview Source Transformations
In this lecture set, we will cover the following topics:
Equivalent circuits review
Source transformations
Some additional transformations
Example of source transformations
Notes: You can click on the links to jump to the subject that you want to learn about now.

## Slide 3: Textbook Coverage
This material is covered in your textbook in the following sections:
Electric Circuits 8th Ed. by Nilsson and Riedel: Section 4.9
Notes: You should also read these sections in your text. This material is intended to complement your textbook coverage, not replace it.

## Slide 4: Equivalent Circuits Review
Source Transformations are another example of equivalent circuits. To use them well, it is important that we follow the rules for equivalent circuits. This will help us avoid problems.

## Slide 5: Equivalent Circuits: A Definition
Imagine that we have a circuit, and a portion of the circuit can be identified, made up of one or more parts. That portion can be replaced with another set of components, if we do it properly. We call these portions equivalent circuits.
Two circuits are considered to be equivalent if they behave the same with respect to the things to which they are connected. One can replace one circuit with another circuit, and everything else cannot tell the difference.
We will use a metaphor for equivalent circuits here. This metaphor is that of jigsaw puzzle pieces. The idea is that two different jigsaw puzzle pieces with the same shape can be thought of as equivalent, even though they are different. The rest of the puzzle does not “notice” a difference. This is analogous to the case with equivalent circuits.

## Slide 6: Equivalent Circuits: A Caution
Two circuits are considered to be equivalent if they behave the same with respect to the things to which they are connected. The properties (voltage, current, power) within the circuit may be different.
It is important to keep this concept in mind. A common error for beginners is to assume that voltages, currents, or powers within a pair of equivalent circuits are equal. They may not be. These voltages, currents, or powers are only required to be equal if they can be identified outside the equivalent circuit.
Go back to Overview slide.

## Slide 7: Source Transformations Defined
The equivalent circuits called the source transformation can be defined as follows:
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by

## Slide 8: Notation
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by
We have used the symbol “~” to indicate equivalence here. Some textbooks use a double-sided arrow (Û or «), or even a single-sided arrow (Þ or ®), to indicate this same thing.

## Slide 9: Note 1
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by
This equivalence can go in either direction. That is, we can replace the circuit on the right with the one on the left, or the other way around. Neither one is simpler; we just prefer one or the other in some situations.

## Slide 10: Note 2
This equation is not really Ohm’s Law. It looks like Ohm’s Law, and has the same form. However, it should be noted that Ohm’s Law relates voltage and current for a resistor. This relates the values of sources and resistances in two different equivalent circuits. However, if you wish to remember this by relating it to Ohm’s Law, that is fine.
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by

## Slide 11: Note 3
The polarities of the sources with respect to the terminals is important. If the reference polarity for the voltage source is as given here (voltage drop from A to B), then the reference polarity for the current source must be as given here (current flow from B to A). This is one good reason for naming the terminals of these equivalents.
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by

## Slide 12: Note 4
As with all equivalent circuits, these two are equivalent only with respect to the things connected to the equivalent circuits. For example, when these two equivalent circuits are connected to an open circuit, in one the resistor dissipates power, and in the other it does not.
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by

## Slide 13: Note 5
These equivalent circuits hold for dependent sources as well as independent sources. The key is that the variable, which the dependent sources depend on, must remain intact. That is, the voltage or current that the dependent sources use must be outside of the circuit being replaced.
A portion of a circuit where we have a voltage source in series with a resistance is equivalent to current source in parallel with a resistance. The resistances for these two equivalents are equal. These two cases are equivalent as long as the resistances are equal and if the voltage source and current source are related by
Go back to Overview slide.

## Slide 14: Other Useful Transformations
There are some other useful transformations, relating to sources, that can be defined at this point. These transformations do not have a common name, and in a sense they derive from the definitions of ideal voltage sources and ideal current sources. Still, since they are equivalent circuits relating sources, that have much the same form as source transformations, they are listed in the slides that follow.

## Slide 15: Other Useful Transformations – 1
Voltage sources in series can be replaced by a single voltage source, where the value of the equivalent source is equal to the algebraic sum of the voltage sources it is replacing. An example is shown here with two sources with random polarities.
As with all equivalent circuits, these two are equivalent only with respect to the things connected to the equivalents.

## Slide 16: Other Useful Transformations – 2
Current sources in parallel can be replaced by a single current source, where the value of the equivalent source is equal to the algebraic sum of the current sources it is replacing. An example is shown here with two sources with random polarities.
As with all equivalent circuits, these two are equivalent only with respect to the things connected to the equivalents.

## Slide 17: Other Useful Transformations – 3
A voltage source in parallel with anything can be replaced by that voltage source. The “anything” can be a resistor, a current source, or any other combination of elements. If the “anything” is a voltage source, the two voltage sources must be equal for KVL to hold.
As with all equivalent circuits, these two are equivalent only with respect to the things connected to the equivalents.

## Slide 18: Other Useful Transformations – 4
A current source in series with anything can be replaced by that current source. The “anything” can be a resistor, a voltage source, or any other combination of elements. If the “anything” is a current source, the two current sources must be equal for KCL to hold.
As with all equivalent circuits, these two are equivalent only with respect to the things connected to the equivalents.

## Slide 19: Notes
These equivalent circuits can go in either direction. That is, we can replace the circuit on the right with the one on the left, or the other way around.
The polarities of the sources with respect to the terminals are important. This is one good reason for naming the terminals of these equivalents.
As with all equivalent circuits, these are equivalent only with respect to the things connected to the equivalent circuits.
These equivalent circuits hold for dependent sources as well as independent sources. The key is that the variable, which the dependent sources depend on, must remain intact. That is, the voltage or current that the dependent sources use must be outside of the circuit being replaced.
Go back to Overview slide.

## Slide 20: Example Problem
We wish to solve for the voltage vX in the circuit given below. While we could certainly solve this by writing a series of KVL and KCL equations, we are going to solve it instead by using a series of equivalent circuits and simplify the circuit down step by step.

## Slide 21: Example Problem – Step 1
We wish to solve for the voltage vX in the circuit given below. We note that we have a voltage source, vS, in series with a resistor, R1. We can replace them with a current source in parallel with a resistor. When we do, we will have current sources in parallel and resistors in parallel, which we can simplify further. So, let’s take the first step.

## Slide 22: Example Problem – Step 2
We want to replace the voltage source in series with a resistor, with a current source in parallel with a resistor. Here, we have made this replacement. Note that we now have two current sources in parallel, and two resistors in parallel. Since the voltage we are looking for is outside these combinations, we can replace them with their equivalents. That is our next step.

## Slide 23: Example Problem – Step 3
We have replaced the parallel current sources and parallel resistors with their equivalents. Now, we can note that we have a current source in parallel with a resistor. We could replace this with a voltage source in series with a resistor, and then we could simplify the circuit further. Let’s do this.

## Slide 24: Example Problem – Step 4
We have replaced the current source in parallel with a resistor with a voltage source in series with a resistor. At this point, we have three resistors in series, and we want the voltage across one of them. This means that we use the voltage divider rule, and write,
Go back to Overview slide.
Go to Comments slide.

## Slide 25: Example Problem – Solution
The solution for this problem then is
Go back to Overview slide.
Go to Comments slide.

## Slide 26: Why Are Source Transformations Needed?
This is a good question. In fact, it should be pointed out that these transformations are not necessary. Rather, they are like many other aspects of circuit analysis in that they allow us to solve circuits more quickly and more easily. They are used in cases where we want to be able to combine elements using other equivalent circuit simplifications.
One key in applying these equivalents is to get the proper sources in the proper polarities in the equivalents and equations. We recommend that you name the terminals each time, on the circuit diagrams, to help you get these polarities right.
Go back to Overview slide.

## Slide 27: Example Problem