Name:  _____________________________ (please print)

Signature: __________________________

ECE 2300 – Quiz #1 – 1PM Section

February 11, 2008

Keep this quiz closed and face up until you are told to begin.

1.  This quiz is closed book, closed notes.  You may use one 8.5” x 11” crib sheet, or its equivalent.

2.  Show all work on these pages.  Show all work necessary to complete the problem.  A solution without the appropriate work shown will receive no credit.  A solution which is not given in a reasonable order will lose credit.

3.  It is assumed that your work will begin on the same page as the problem statement.  If you choose to begin your work on another page, you must indicate this on the page with the problem statement, with a clear indication of where the work can be found.  If your work continues on to another page, indicate clearly where your work can be found.  Failure to indicate this clearly will result in a loss of credit.

4.  Show all units in solutions, intermediate results, and figures.  Units in the quiz will be included between square brackets.

5.  Do not use red ink.  Do not use red pencil.

6.  You will have 30 minutes to work on this quiz.

________________/20

Room for extra work

The device shown in Figure 1 can be modeled as an independent current source in parallel with a resistance.  This device has the relationship between voltage and current shown in Figure 2.

a)  Find a model for this device that will be valid in the range of 
2[V] < vQ < 5[V].  Draw your model, labeling terminals A and B on your model.

b)  The device is connected in the circuit shown in Figure 3.  Find the power absorbed by the device in this circuit.  Note the device terminals shown in Figure 3.

Room for extra work

ECE 2300 -- Quiz #1 – February 11, 2008 – Solution

The device shown in Figure 1 can be modeled as an independent current source in parallel with a resistance.  This device has the relationship between voltage and current shown in Figure 2.

a)  Find a model for this device that will be valid in the range of 
2[V] < vQ < 5[V].  Draw your model, labeling terminals A and B on your model.

b)  The device is connected in the circuit shown in Figure 3.  Find the power absorbed by the device in this circuit.  Note the device terminals shown in Figure 3.