## Slide 1: ECE 2202 Circuit Analysis II
Dr. Dave Shattuck
Associate Professor, ECE Dept.
Lecture Set #2
Inductors and Capacitors
Version 25
Shattuck@uh.edu
713 743-4422

## Slide 2: Lecture Set #2 Inductors and Capacitors

## Slide 3: Overview of this Lecture Inductors and Capacitors
In this lecture, we will cover the following topics:
Defining equations for inductors and capacitors
Power and energy storage in inductors and capacitors
Parallel and series combinations
Basic rules for inductors and capacitors
Notes: You can click on the links to jump to the subject that you want to learn about now.

## Slide 4: Textbook Coverage
Approximately this same material is covered in the Nilsson and Riedel textbook in the following sections:
Electric Circuits 7th Ed. by Nilsson and Riedel: Sections 6.1 through 6.3
Electric Circuits 10th Ed. by Nilsson and Riedel: Sections 6.1 through 6.3
Notes: You should also read these sections in your text. This material is intended to complement your textbook coverage, not replace it.

## Slide 5: Basic Elements, Review
We are now going to pick up the remaining basic circuit elements that we will be covering in this course.

## Slide 6: Circuit Elements
In circuits, we think about basic circuit elements that are the basic “building blocks” of our circuits. This is similar to what we do in Chemistry with chemical elements like oxygen or nitrogen.
A circuit element cannot be broken down or subdivided into other circuit elements.
A circuit element can be defined in terms of the behavior of the voltage and current at its terminals.

## Slide 7: The 5 Basic Circuit Elements
There are 5 basic circuit elements:
Voltage sources
Current sources
Resistors
Inductors
Capacitors
We defined the first three elements previously. We will now introduce inductors or capacitors.
Notes: The first three elements were introduced in Part 3 of Module 1.

## Slide 8: Inductors
An inductor is a two-terminal circuit element that has a voltage across its terminals which is proportional to the derivative of the current through its terminals.
The coefficient of this proportionality is the defining characteristic of an inductor.
An inductor is the device that we use to model the effect of magnetic fields on circuit variables. The energy stored in magnetic fields has effects on voltage and current. We use the inductor component to model these effects.
In many cases a coil of wire can be modeled as an inductor.

## Slide 9: Inductors – Definition and Units
An inductor obeys the expression
where vL is the voltage across the inductor, and iL is the current through the inductor, and LX is called the inductance.
In addition, it works both ways. If something obeys this expression, we can think of it, and model it, as an inductor.
The unit ([Henry] or [H]) is named for Joseph Henry, and is equal to a [Volt-second/Ampere].
There is an inductance whenever we have magnetic fields produced, and there are magnetic fields whenever current flows. However, this inductance is often negligible except when we wind wires in coils to concentrate the effects.

## Slide 10: Schematic Symbol for Inductors
The schematic symbol that we use for inductors is shown here.
This is intended to indicate that the schematic symbol can be labeled either with a variable, like LX, or a value, with some number, and units. An example might be 390[mH]. It could also be labeled with both.

## Slide 11: Inductor Polarities
Previously, we have emphasized the important of reference polarities of current sources and voltages sources. There is no corresponding polarity to an inductor. You can flip it end-for-end, and it will behave the same way.
However, similar to a resistor, direction matters in one sense; we need to have defined the voltage and current in the passive sign relationship to use the defining equation the way we have it here.
Notes: {I need a link here to the passive sign convention discussion in DPKC_Mod01_Part02.}

## Slide 12: Passive and Active Sign Relationship for Inductors
The sign of the equation that we use for inductors depends on whether we have used the passive sign relationship or the active sign relationship.
Passive Sign Relationship
Active Sign Relationship

## Slide 13: Defining Equation, Integral Form, Derivation
The defining equation for the inductor,
can be rewritten in another way. If we want to express the current in terms of the voltage, we can integrate both sides. We get
We pick t0 and t for limits of the integral, where t is time, and t0 is an arbitrary time value, often zero. The inductance, LX, is constant, and can be taken out of the integral. To avoid confusion, we introduce the dummy variable s in the integral. We get
We finish the derivation in the next slide.

## Slide 14: Defining Equations for Inductors
We can take this equation and perform the integral on the right hand side. When we do this we get
Thus, we can solve for iL(t), and we have two defining equations for the inductor,
and
Remember that both of these are defined for the passive sign relationship for iL and vL. If not, then we need a negative sign in these equations.

## Slide 15: Defining Equations for Inductors, Active and Passive
and
For the passive sign relationship for iL and vL.
For the active sign relationship for iL and vL.
and

## Slide 16: Note 1
The implications of these equations are significant. For example, if the current is not changing, then the voltage will be zero. This current could be a constant value, and large, and an inductor will have no voltage across it. This is counter-intuitive for many students. That is because they are thinking of actual coils, which have some finite resistance in their wires. For us, an ideal inductor has no resistance; it simply obeys the laws below.
We might model a coil with both an inductor and a resistor, but for now, all we need to note is what happens with these ideal elements.
and

## Slide 17: Step Change
Ask the Step Change question.
and

## Slide 18: Note 2
The implications of these equations are significant. Another implication is that we cannot change the current through an inductor instantaneously. If we were to make such a change, the derivative of current with respect to time would be infinity, and the voltage would have to be infinite. Since it is not possible to have an infinite voltage, it must be impossible to change the current through an inductor instantaneously.
and

## Slide 19: Function of s?
Ask the Function of s question.
and

## Slide 20: Function of s?
In the Function of s question, the grade on this is entirely based on participation.
and

## Slide 21: Note 3
Some students are troubled by the introduction of the dummy variable s in the integral form of this equation, below. It is not really necessary to introduce a dummy variable. It really doesn’t matter what variable is integrated over, because when the limits are inserted, that variable goes away.
and
The independent variable t is in the limits of the integral. This is indicated by the iL(t) on the left-hand side of the equation.
Remember, the integral here is not a function of s. It is a function of t.
This is a constant.

## Slide 22: Energy in Inductors, Derivation
We can take the defining equation for the inductor, and use it to solve for the energy stored in the magnetic field associated with the inductor. First, we note that the power is voltage times current, as it has always been. So, we can write,
Now, we can multiply each side by dt, and integrate both sides to get
Note, that when we integrated, we needed limits. We know that when the current is zero, there is no magnetic field, and therefore there can be no energy in the magnetic field. That allowed us to use 0 for the lower limits. The upper limits came since we will have the energy stored, wL, for a given value of current, iL. The derivation continues on the next slide.

## Slide 23: Energy in Inductors, Formula
We had the integral for the energy,
Now, we perform the integration. Note that LX is a constant, independent of the current through the inductor, so we can take it out of the integral. We have
We simplify this, and get the formula for energy stored in the inductor,

## Slide 24: Notes
We took some mathematical liberties in this derivation. For example, we do not really multiply both sides by dt, but the results that we obtain are correct here.
Note that the energy is a function of the current squared, which will be positive. We will assume that our inductance is also positive, and clearly ½ is positive. So, the energy stored in the magnetic field of an inductor will be positive.
These three equations are useful, and should be learned or written down.
Go back to Overview slide.

## Slide 25: Capacitors
A capacitor is a two-terminal circuit element that has a current through its terminals which is proportional to the derivative of the voltage across its terminals.
The coefficient of this proportionality is the defining characteristic of a capacitor.
A capacitor is the device that we use to model the effect of electric fields on circuit variables. The energy stored in electric fields has effects on voltage and current. We use the capacitor component to model these effects.
In many cases the idea of two parallel conductive plates is used when we think of a capacitor, since this arrangement facilitates the production of an electric field.

## Slide 26: Capacitors – Definition and Units
A capacitor obeys the expression
where vC is the voltage across the capacitor, and iC is the current through the capacitor, and CX is called the capacitance.
In addition, it works both ways. If something obeys this expression, we can think of it, and model it, as an capacitor.
The unit ([Farad] or [F]) is named for Michael Faraday, and is equal to a [Ampere-second/Volt]. Since an [Ampere] is a [Coulomb/second], we can also say that a [F] = [C/V].
There is a capacitance whenever we have electric fields produced, and there are electric fields whenever there is a voltage between conductors. However, this capacitance is often negligible.

## Slide 27: Schematic Symbol for Capacitors
The schematic symbol that we use for capacitors is shown here.
This is intended to indicate that the schematic symbol can be labeled either with a variable, like CX, or a value, with some number, and units. An example might be 100[mF]. It could also be labeled with both.

## Slide 28: Capacitor Polarities
Previously, we have emphasized the important of reference polarities of current sources and voltages sources. There is no corresponding polarity to an capacitor. For most capacitors, you can flip them end-for-end, and they will behave the same way. An exception to this rule is an electrolytic capacitor, which must be placed so that the voltage across it will be in the proper polarity. This polarity is usually marked on the capacitor.
In any case, similar to a resistor, direction matters in one sense; we need to have defined the voltage and current in the passive sign relationship to use the defining equation the way we have it here.
Notes: {I need a link here to the passive sign convention discussion in DPKC_Mod01_Part02.}

## Slide 29: Passive and Active Sign Relationship for Capacitors
The sign of the equation that we use for capacitors depends on whether we have used the passive sign relationship or the active sign relationship.
Passive Sign Relationship
Active Sign Relationship

## Slide 30: Defining Equation, Integral Form, Derivation
The defining equation for the capacitor,
can be rewritten in another way. If we want to express the voltage in terms of the current, we can integrate both sides. We get
We pick t0 and t for limits of the integral, where t is time, and t0 is an arbitrary time value, often zero. The capacitance, CX, is constant, and can be taken out of the integral. To avoid confusion, we introduce the dummy variable s in the integral. We get
We finish the derivation in the next slide.

## Slide 31: Defining Equations for Capacitors
We can take this equation and perform the integral on the right hand side. When we do this we get
Thus, we can solve for vC(t), and we have two defining equations for the capacitor,
and
Remember that both of these are defined for the passive sign relationship for iC and vC. If not, then we need a negative sign in these equations.

## Slide 32: Defining Equations for Capacitors
and
If we have the passive sign relationship for iC and vC then we have
and
If we have the active sign relationship for iC and vC then we have negative signs in these equations.

## Slide 33: Note 1
The implications of these equations are significant. For example, if the voltage is not changing, then the current will be zero. This voltage could be a constant value, and large, and a capacitor will have no current through it.
For many students this is easier to accept than the analogous case with the inductor. This is because practical capacitors have a large enough resistance of the dielectric material between the capacitor plates, so that the current flow through it is generally negligible.
and

## Slide 34: Note 2
The implications of these equations are significant. Another implication is that we cannot change the voltage across a capacitor instantaneously. If we were to make such a change, the derivative of voltage with respect to time would be infinity, and the current would have to be infinite. Since it is not possible to have an infinite current, it must be impossible to change the voltage across a capacitor instantaneously.
and

## Slide 35: Note 3
Some students are troubled by the introduction of the dummy variable s in the integral form of this equation, below. It is not really necessary to introduce a dummy variable. It really doesn’t matter what variable is integrated over, because when the limits are inserted, that variable goes away.
and
The independent variable t is in the limits of the integral. This is indicated by the vC(t) on the left-hand side of the equation.
Remember, the integral here is not a function of s. It is a function of t.
This is a constant.

## Slide 36: Energy in Capacitors, Derivation
We can take the defining equation for the capacitor, and use it to solve for the energy stored in the electric field associated with the capacitor. First, we note that the power is voltage times current, as it has always been. So, we can write,
Now, we can multiply each side by dt, and integrate both sides to get
Note, that when we integrated, we needed limits. We know that when the voltage is zero, there is no electric field, and therefore there can be no energy in the electric field. That allowed us to use 0 for the lower limits. The upper limits came since we will have the energy stored, wC, for a given value of voltage, vC. The derivation continues on the next slide.

## Slide 37: Energy in Capacitors, Formula
We had the integral for the energy,
Now, we perform the integration. Note that CX is a constant, independent of the voltage across the capacitor, so we can take it out of the integral. We have
We simplify this, and get the formula for energy stored in the capacitor,

## Slide 38: Notes
We took some mathematical liberties in this derivation. For example, we do not really multiply both sides by dt, but the results that we obtain are correct here.
Note that the energy is a function of the voltage squared, which will be positive. We will assume that our capacitance is also positive, and clearly ½ is positive. So, the energy stored in the electric field of an capacitor will be positive.
These three equations are useful, and should be learned or written down.
Go back to Overview slide.

## Slide 39: Series Inductors Equivalent Circuits
Two series inductors, L1 and L2, can be replaced with an equivalent circuit with a single inductor LEQ, as long as

## Slide 40: More than 2 Series Inductors
This rule can be extended to more than two series inductors. In this case, for N series inductors, we have

## Slide 41: Series Inductors Equivalent Circuits: A Reminder
Two series inductors, L1 and L2, can be replaced with an equivalent circuit with a single inductor LEQ, as long as
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.)

## Slide 42: Series Inductors Equivalent Circuits: Initial Conditions
Two series inductors, L1 and L2, can be replaced with an equivalent circuit with a single inductor LEQ, as long as
To be equivalent with respect to the “rest of the circuit”, we must have any initial condition be the same as well. That is, iLEQ(t0) must equal iL1(t0).

## Slide 43: Parallel Inductors Equivalent Circuits
Two parallel inductors, L1 and L2, can be replaced with an equivalent circuit with a single inductor LEQ, as long as

## Slide 44: More than 2 Parallel Inductors
This rule can be extended to more than two parallel inductors. In this case, for N parallel inductors, we have
The product over sum rule only works for two inductors.

## Slide 45: Parallel Inductors Equivalent Circuits: A Reminder
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.)
Two parallel inductors, L1 and L2, can be replaced with an equivalent circuit with a single inductor LEQ, as long as

## Slide 46: Parallel Inductors Equivalent Circuits: Initial Conditions
To be equivalent with respect to the “rest of the circuit”, we must have any initial condition be the same as well. That is,

## Slide 47: Parallel Capacitors Equivalent Circuits
Two parallel capacitors, C1 and C2, can be replaced with an equivalent circuit with a single capacitor CEQ, as long as

## Slide 48: More than 2 Parallel Capacitors
This rule can be extended to more than two parallel capacitors. In this case, for N parallel capacitors, we have

## Slide 49: Parallel Capacitors Equivalent Circuits: A Reminder
This rule can be extended to more than two parallel capacitors. In this case, for N parallel capacitors, we have
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.)

## Slide 50: Parallel Capacitors Equivalent Circuits: Initial Conditions
Two parallel capacitors, C1 and C2, can be replaced with an equivalent circuit with a single inductor CEQ, as long as
To be equivalent with respect to the “rest of the circuit”, we must have any initial condition be the same as well. That is, vCEQ(t0) must equal vC1(t0).

## Slide 51: Series Capacitors Equivalent Circuits
Two series capacitors, C1 and C2, can be replaced with an equivalent circuit with a single inductor CEQ, as long as

## Slide 52: More than 2 Series Capacitors
This rule can be extended to more than two series capacitors. In this case, for N series capacitors, we have
The product over sum rule only works for two capacitors.

## Slide 53: Series Capacitors Equivalent Circuits: A Reminder
Two series capacitors, C1 and C2, can be replaced with an equivalent circuit with a single capacitor CEQ, as long as
Remember that these two equivalent circuits are equivalent only with respect to the circuit connected to them. (In yellow here.)

## Slide 54: Series Capacitors Equivalent Circuits: Initial Conditions
To be equivalent with respect to the “rest of the circuit”, we must have any initial condition be the same as well. That is,

## Slide 55: Inductor Rules and Equations
For inductors, we have the following rules and equations which hold:

## Slide 56: Inductor Rules and Equations – dc Note
For inductors, we have the following rules and equations which hold:
The phrase dc may be new to some students. By “dc”, we mean that nothing is changing. It came from the phrase “direct current”, but is now used in many additional situations, where things are constant. It is used with more than just current.

## Slide 57: Capacitor Rules and Equations
For capacitors, we have the following rules and equations which hold:

## Slide 58: Why do we cover inductors? Aren’t capacitors good enough for everything?
This is a good question. Capacitors, for practical reasons, are closer to ideal in their behavior than inductors. In addition, it is easier to place capacitors in integrated circuits, than it is to use inductors. Therefore, we see capacitors being used far more often than we see inductors being used.
Still, there are some applications where inductors simply must be used. Transformers are a case in point. When we find these applications, we should be ready, so that we can handle inductors.
Go back to Overview slide.

## Slide 59
The circuit shown below has a switch which closed at t = 0. The voltages v1 and v2 were measured before the switch was closed, and it was found that
In addition, for time greater than zero, it was determined that
Explore the energy stored in the capacitors for t < 0, and for t = ¥.
Example Problem #1

## Slide 60
Example Problem #2
The switch shown had been open for a long time, then closed at t = 0, and opened again at 50[ms]. a) Find iX (0-).
b) Find iX (0+).
c) Find vX (0-).
d) Find vX (0+).

## Slide 61
Example Problem #2
The switch shown had been open for a long time, then closed at t = 0, and opened again at 50[ms]. a) Find iX (0-).
b) Find iX (0+).
c) Find vX (0-).
d) Find vX (0+).
a) iX(0-) = 336.4[mA]
b) iX(0+) = -56.63[mA]
c) vX(0-) = 0
d) vX(0+) = 2.20[V]

## Slide 62
For the circuit shown, the switch had been in position a for a long time before moving to position b at t = 0. The voltage vX before t = 0 was constant, and equal to -7.34[V].
a) Find vW(0-).
b) Find vW(0+).
c) Find iW(0-).
d) Find iW(0+).
Example Problem #3

## Slide 63
For the circuit shown, the switch had been in position a for a long time before moving to position b at t = 0. The voltage vX before t = 0 was constant, and equal to -7.34[V].
a) Find vW(0-).
b) Find vW(0+).
c) Find iW(0-).
d) Find iW(0+).
Example Problem #3
a) vW(0-) = -4.96[V]
b) vW(0+) = -4.96[V]
c) iW(0-) = 0
d) iW(0+) = 5.2[A]

## Slide 64
In the circuit shown, the switch was closed for a long time, before it was opened at t = 0. Find vX(10[ms]).
Example Problem #4