## Slide 1: ECE 2202 Circuit Analysis II
Dr. Dave Shattuck
Associate Professor, ECE Dept.
Lecture Set #6
Complex Numbers
Version 23
Shattuck@uh.edu
713 743-4422

## Slide 2: Lecture Set #6 Complex Numbers

## Slide 3: Overview of this Lecture Complex Numbers
In this lecture, we will cover the following topic:
Review of Complex Numbers

## Slide 4: Review of Complex Numbers – 1
A complex number is a number that is a function of the square root of minus one. We use the symbol “j” to represent this,
Remember that j does not exist. It is a figment of our imagination. It is just a tool we use to get solutions that do exist.

## Slide 5: Review of Complex Numbers – 2
Complex numbers can be expressed as having a real part, and an imaginary part. The imaginary part is the coefficient of j. The real part is the part that is not a coefficient of j. Thus, in the example given here, for the complex number A,
the real part is 3, and the imaginary part is 4.
Remember that the both the real part and the imaginary part are themselves real numbers.

## Slide 6: Review of Complex Numbers – 3
Complex numbers can also be expressed as having a magnitude, and a phase. For example, in the complex number A,
the real part is 3, the imaginary part is 4, the magnitude is 5, and the phase is 53.13[degrees]. Remember that all four parts are real numbers.

## Slide 7: Review of Complex Numbers – 4
It is easiest to think of this in terms of a plot, where the horizontal axis (abscissa) is the real component, and the vertical axis (ordinate) is the imaginary component. So, if we were to plot our complex number A in this complex plane, we would get

## Slide 8: Review of Complex Numbers – 5
We can get the relationships between these values from our trigonometry courses, just looking at the right triangle given here. For review, they are all given here.

## Slide 9: Review of Complex Numbers – 6
We can get the relationships between these values from our trigonometry courses, just looking at the right triangle given here. For review, they are all given here.
This equation can give the wrong value with some calculators. Make sure you are in the correct quadrant.

## Slide 10: Review of Complex Numbers – 7
We often use a short hand notation for complex numbers, using an angle symbol instead of the complex exponential. Specifically, we write

## Slide 11: Review of Complex Numbers – 8
The form using x and y is called the rectangular form, and the form using M and f is called the polar form of the complex number. Generally, we want to be able to move between forms and perform addition, subtraction, multiplication and division, quickly and easily.
The rules are:
to add or subtract, we add or subtract the real parts and the imaginary parts; and
to multiply or divide, we multiply or divide the magnitudes, and add or subtract the phases.
You may have a calculator or computer that does this for you. If so, practice this, because it will come in handy. However, you also need to know these rules.

## Slide 12: Review of Complex Numbers – 9
The rules are:
to add or subtract, we add or subtract the real parts and the imaginary parts; and
to multiply or divide, we multiply or divide the magnitudes, and add or subtract the phases.
For example, if you are multiplying by a complex number with a phase of 90[degrees], you know that the product will be in the next quadrant from the starting point, moving counter-clockwise. This kind of insight will be important.

## Slide 13: Review of Complex Numbers – 10
Many students use TI calculators. Here are some hints and suggestions, if you use them.
It is recommended that you put your calculator in degree mode. This makes notation using the angle symbol work properly.
When you use that angle symbol, the number must be put inside parentheses, that is inside (here).

## Slide 14: Review of Complex Numbers – 11
Many students use TI calculators. Here are some hints and suggestions, if you use them.
You can switch between rectangular form and polar form with the “black right pointing triangle, conversion” symbol. That is, you would have something like this:

## Slide 15: Review of Complex Numbers – 12
There is an operation called taking a complex conjugate. When you take a complex conjugate, you change the sign of the imaginary part, or change the sign of the phase. This will be important. Some complex conjugate examples are given below. We show the complex conjugate operation with a raised asterisk. Three examples are

## Slide 16: Review of Complex Numbers – 13
When you multiply a complex number by its complex conjugate, you get a real number, with a magnitude equal to magnitude of the original number, squared, as seen in the two examples

## Slide 17: Review of Complex Numbers – 14
When you have one complex equation, that has two real unknowns, you can solve for the real unknowns by writing two of the following real equations:
The real parts of both sides of an equation must be equal.
The imaginary parts of both sides of an equation must be equal.
The magnitudes of both sides of an equation must be equal.
The phases of both sides of an equation must be equal.
An example follows. We have the equation

## Slide 18: Review of Complex Numbers – 15
When you have one complex equation, that has two real unknowns, you can solve for the real unknowns by writing two of the following real equations:
The real parts of both sides of an equation must be equal.
The imaginary parts of both sides of an equation must be equal.
The magnitudes of both sides of an equation must be equal.
The phases of both sides of an equation must be equal.

## Slide 19: Review of Complex Numbers – 16
When you have one complex equation, that has two real unknowns, you can solve for the real unknowns by writing two of the following real equations:
The real parts of both sides of an equation must be equal.
The imaginary parts of both sides of an equation must be equal.
The magnitudes of both sides of an equation must be equal.
The phases of both sides of an equation must be equal.

## Slide 20: What is the Point to This?
This is a good question. We will use the magnitude and phase of a complex number to get the magnitude and phase of a sinusoid in the solution of a particular class of problems.
We will develop a set of rules for doing this. We will lay out this class of problems in the next lecture set.