## Slide 1: ECE 2202 Circuit Analysis II
Dr. Dave Shattuck
Associate Professor, ECE Dept.
Lecture Set #7
Phasors
Version 23
Shattuck@uh.edu
713 743-4422

## Slide 2: Lecture Set #7 Phasors: Sinusoidal Circuits – Background Concepts

## Slide 3: Overview of this Lecture Sinusoidal Circuits – Background Concepts
In this lecture, we will cover the following topics:
Introduction to Sinusoidal Circuit Analysis
Sinusoid Review
Definition of RMS
Definition of “Steady State”

## Slide 4: Textbook Coverage
Approximately this same material is covered in the Nilsson and Reidel textbook in the following sections:
Electric Circuits 6th Edition by Nilsson and Riedel: Sections 9.1 through 9.3, B.1 through B.6
Electric Circuits 10th Edition by Nilsson and Riedel: Sections 9.1 through 9.3, B.1 through B.6

## Slide 5: Sinusoidal Circuit Analysis (Phasors)
The subject of Sinusoidal Circuit Analysis is profound and very important to an understanding of the how electrical engineers view circuits, circuit analysis, and the parts of electrical engineering that use circuits.
This method involves two profound paradigms, or ways of thinking about, circuits:
The use of complex numbers to aid in the solution of differential equations, and
Fourier’s Theorem about the breakdown of signals into sinusoids.
The power of current calculators and computers makes the techniques of Sinusoidal Circuit Analysis even more important, by making the mathematics even easier. The key is to understand what the answers that our calculators give us really mean.

## Slide 6: Sinusoidal Circuit Analysis What are Phasors?
A phasor is a transformation of a sinusoidal voltage or current. Using phasors, and the techniques of phasor analysis, solving circuits with sinusoidal sources gets much easier. We will explain this more, later in the course.
Despite the similarity of the terms, the phasors we use here have nothing to do with the “phasors” which were used in the popular Star Trek TV shows and movies.
While they seem difficult at first, and beginning students may feel as though they have been shot with a “phasor set to stun”, our goal is to show that phasors make analysis so much easier that it is worth the trouble to understand what they are all about.

## Slide 7: AC Circuit Analysis Using Transforms
The fundamental idea about phasor analysis is that circuits that have sinusoidal sources can be solved much more easily if we use a technique called transformation.

## Slide 8: The Transform Solution Process
In a transform solution, we transform the problem into another form. Once transformed, the solution process is easier. The solution process uses complex numbers, but is otherwise straightforward.
The solution obtained is a transformed solution, which must then be inverse transformed to get the answer.

## Slide 9: The Transform Solution Process – Note
In a transform solution, we transform the problem into another form, solve, and inverse transform to get the answer.
It is surprising that a process that uses three steps is faster and easier than a process that uses one step, but the steps are so much easier, it is still true.

## Slide 10: Fourier’s Theorem
The power of the phasor transform approach is magnified when Fourier’s Theorem is considered. Fourier’s Theorem is a subject which is usually covered in depth later in the electrical engineering curriculum. For now, we will simply state the specific application of Fourier’s Theorem to circuit analysis:
Any voltage or current, as a function of time,
can be represented by, and
is equivalent to,
a summation of sinusoids with different frequencies, phases and amplitudes.
This means that we can get any voltage or any current, just by adding up sine waves. It also means that if we know how to handle sine waves, we know how to handle any voltage or current.

## Slide 11: The Limitations
The power of phasor transform analysis combined with the implications of Fourier’s Theorem is significant. There are a couple of big limitations, however.
The number of sinusoidal components, or sinusoids, that one needs to add together to get a voltage or current waveform, is generally infinite. To repeat a phasor analysis technique an infinite number of times can become time consuming.
The phasor analysis technique only gives us part of the solution. It gives us the part of the solution that holds after a long time, also called the steady-state solution.
However, the phasor analysis technique is very useful. This steady state solution is often all we want to know. Just as important, we begin to think about how circuits work in terms of sinusoidal components, and to think about how the phasor analysis works. This is perhaps the most important part of the technique. These ways of thinking are called paradigms.

## Slide 12: Sinusoid Review
A sinusoid is a sine wave or a cosine wave.
Sinusoids can represent many functions, but we will concentrate on voltages or currents, as a function of time.

## Slide 13: Some Review – Sinusoids – 1
This figure shows a cosine and a sine function, plotted as a function of time. The period, T, is the time between two corresponding points on the periodic function. In this plot, the period is 100 [ms].
Chart: Cosine and Sine Plots cos(62.8[rad/s]t) and sin(62.8[rad/s]t)

## Slide 14: Some Review – Sinusoids – 2
Chart: Cosine and Sine Plots cos(62.8[rad/s]t) and sin(62.8[rad/s]t)
The period, T, of the sinusoid can be expressed in terms of the angular frequency, w, as shown below,
The angular frequency is typically given with units of [radians/second]. In this plot, w = 62.8[rad/s].

## Slide 15: Some Review – Sinusoids – 3
A general sinusoid can have a horizontal placement in any possible position with respect to the origin of the time axis. These different positions are called different phases.
Chart: Cosine with Phase Shift cos(wt + f) = cos(62.8[rad/s]t + 114.6°)

## Slide 16: Some Review – Sinusoids – 4
Chart: Cosine with Phase Shift cos(wt + f) = cos(62.8[rad/s]t + 114.6°)
The figure below shows a particular sinusoid. Note that the phase, which here is 114.6° or 2.00[rad], after dividing byw represents the time shift to the left along the time axis.
The time shift in this plot is -(2/62.8), or t0 = -31.8[ms].
t0

## Slide 17: Some Review – Sinusoids – 5
Chart: Cosine with Phase Shift cos(wt + f) = cos(62.8[rad/s]t + 114.6°)
The phase has angular units, usually either radians or degrees.
The time shift in this plot is -(2[rad]/62.8[rad/s]), or t0 = -31.8[ms].
t0

## Slide 18: Some Review – Sinusoids – 6
A general sinusoid has the following equation. Note that in this equation there are three parameters, the amplitude (Xm), the frequency (w), and the phase (f). The time, t, is the independent variable. The sine function is just as good as the cosine function, but in electrical engineering the cosine function is used more often. This typical equation is given as
Chart: Cosine with Phase Shift Xmcos(wt + f) = 2.7cos(62.8[rad/s]t + 114.6°)
For the example in this plot, Xm = 2.7 (This amplitude has units that depend on the function), w = 62.8[rad/s], and f = 114.6 °.
t0

## Slide 19: Some Review – Sinusoids – Note 1
Chart: Cosine with Phase Shift Xmcos(wt + f) = 2.7cos(62.8[rad/s]t + 114.6°)
A few notes about the general sinusoid equation follow. First, note that the value t0 is the time at which the argument of the cosine function is zero. In other words, if you set (wt+f) equal to zero, and solve for t, you get a value of time which here has been called t0. This is the time shift of the cosine, which has been moved by f/w to the left.
t0

## Slide 20: Some Review – Sinusoids – Note 2
Chart: Cosine with Phase Shift Xmcos(wt + f) = 2.7cos(62.8[rad/s]t + 114.6°)
A few notes about the general sinusoid equation follow. Second, note that the argument of the cosine function must have angle units. Often, engineers use [radians/second] for w, but then use [degrees] for f. This seems foolish, because if you want to evaluate x(t), you then need to convert one or the other. However, in many applications we do not actually evaluate x(t). We use x(t) in other ways, so this is not as big a problem as might be imagined. Still, it is important to pay attention to units, as always.
t0

## Slide 21: Some Review – Sinusoids – Note 3
Chart: Cosine with Phase Shift Xmcos(wt + f) = 2.7cos(62.8[rad/s]t + 114.6°)
A few notes about the general sinusoid equation follow. Third, note that the phrase “in phase” can be used with two or more sinusoids. When two or more sinusoids have the same phase shift, or the same phase, we say that those sinusoids are in phase. When they do not have the same phase, we will say that they are out of phase.
t0

## Slide 22: Definition of RMS – Introduction
We have chosen this point to define a common and important term, the rms value of a voltage or current. The rms value, also called the effective value, has the most meaning in terms of power calculations, and many texts wait to introduce it until the power calculations are performed.
However, it is a basic characteristic of a periodic voltage or current. Also, it is used in many other areas, such as the readings on voltmeters and ammeters. If you are going to measure sinusoidal voltages or currents with a meter, you should understand rms, since the results are usually given as rms values.
We will introduce rms values again in the sinusoidal power lectures. We hope that by doing this, we will double the chances that students will understand this fundamental and important concept.

## Slide 23: Definition of RMS
The rms value, also called the effective value, is the root-mean-square value. We can take the rms value of any periodic function.
The rms value is obtained by taking the square root of the mean value of the squared function.
To get this, we take the function and square it. Then we take the average value, or mean value, of that squared function. Then, we take the square root of that average value. So, to get an rms value, you go in reverse order, s, m, and then r.
The purpose of an rms value is to get a single value that can be used in power calculations, when the average value of the power is desired.

## Slide 24: Derivation of RMS – Part 1
The rms value is also called the effective value because it yields a single value that can be used in power calculations, when the average value of the power is desired. It is a value that is effectively like a dc value, for power calculations, in that it can be used in the power formula like a dc value.
The power for periodic functions is also a periodic function, and changes with time. But, if we don’t care about the changes, and only want the average value, we can use rms values, and make the calculations easier.
This is the basis for the derivation of the rms value formula.

## Slide 25: Derivation of RMS – 2
Before doing the derivation, let’s think about an application as we have seen it. Think about the wall plugs in your home. You may be aware that these wall plugs supply a voltage of 110[Volts]. (This is approximate, and depends on what country you are in.)
Questions: What does this mean? Isn’t the voltage sinusoidal in home wiring? Is this the amplitude of the sine wave?
Answers: The 110[V] is an rms value. Yes, the voltage is sinusoidal. No, the amplitude is not 110[V]. Rather, it is an effective value, that can be multiplied directly by the rms value of the current to get the power consumed by the device you connect to the socket.
Example: When you have a 60[Watt] light bulb plugged into a wall socket, and we want the current, we would use

## Slide 26: Derivation of RMS – 3
We want the effective values that could be used in power calculations, for average power, in the formula
We will do the derivation for a resistance, since we want the formula to work with the resistance power formulas. Let’s arbitrarily choose to work with the voltage. What we want to get is a value that will work in the formula,
With T as the period, the average value of the power is obtained by the formula,

## Slide 27: Derivation of RMS – 4
Now, to get the formula, we simply set the two equations from the previous slide equal to each other,
Now, we need to simplify. The resistance is assumed not to be a function of time, and so can be taken out of the integral. When we multiply both sides by R, we get

## Slide 28: Derivation of RMS – 5
Finally, we can solve for the rms value of the voltage, by taking the square root of both sides,
This is the result that we have been working toward. We only need to interpret this result. We have taken the voltage, v(t), and squared it. Then, by integrating it over a period and dividing by the period, we are taking the mean value of the squared function. Finally, we take the square root of the mean value of the squared function. We call this rms.

## Slide 29: Derivation of RMS – 6
The derivation for the rms value for currents works very similarly, and yields
Note: In these notes we rarely show derivations. However, in this case, a full derivation of the rms formula has been shown. The reasons are that the derivation shows that the rms value can be obtained for any periodic function, not just for sinusoids. It also shows why we have the formula that we use; it arises out of the goal of being able to use this value in power calculations, using a simple, familiar formula.

## Slide 30: RMS Value of a Sinusoid
The rms value for a general periodic function, x(t), is
Now, this was derived for any periodic function. The function must be periodic for the formula for the mean value to apply.
If we perform the calculus to get the rms value for a sinusoid, we find the rms value is equal to the zero-to-peak value (or amplitude) divided by the square root of 2, or
Remember, this only holds for sinusoids!

## Slide 31: Definition of “Steady State” – 1
Only the steady state value of a solution is obtained with the phasor transform technique. The steady state portion of the solution is the part of the solution that remains after a long time.
The meaning of this may or may not be obvious to you. If it is not, we will try to make it clearer by taking a fairly simple example.
Imagine the circuit here has a sinusoidal source. What is the current that results for t > 0?
This is about as simple as any nontrivial problem we could consider, and its result is representative of the kinds of results we can get.
Notes: This approach to explaining the meaning of steady-state portion of the solution to a circuit is modeled after that in Electric Circuits, 6th Ed., by Nilsson and Riedel, published by Prentice-Hall.

## Slide 32: Definition of “Steady State” – 2
If the source is sinusoidal, it must have the form,
Imagine the circuit here has a sinusoidal source. What is the current that results for t > 0?
This is a differential equation, first order, with constant coefficients, and a sinusoidal forcing function. We know, as well, that the current at t = 0 is zero. In this case, the solution of i(t), for t > 0, can be shown to be
Applying Kirchhoff’s Voltage Law around the loops we get the differential equation,
Notes: If you do not remember enough of your differential equations course to derive this result, do not worry. The solution itself is only given to show the form of the solution.

## Slide 33: Definition of “Steady State” – 3
The solution of i(t), for t > 0, can be shown to be
This part of the solution varies with time as a decaying exponential. In fact, you may recognize that it has a time constant t = L/R. After several time constants, it will die away and become relatively small. We call this part of the solution the transient response.
This part of the solution varies with time as a sinusoid. In fact, you may recognize that it is a sinusoid with the same frequency as the source, but with different amplitude and phase. This part of the solution does not die out with time. We call this part of the solution the steady-state response.

## Slide 34: Definition of “Steady State” – 4
Thus, the steady-state solution of i(t) is the part of the solution that does not die out with time. We show that here with the subscript SS to indicate that this is only the steady-state portion of the solution,
Our goal with phasor transforms to is to get this steady-state part of the solution, and to do it as easily as we can. Note that the steady state solution, with sinusoidal sources, is sinusoidal with the same frequency as the source.
Thus, all we need to do is to find the amplitude and phase of the solution.

## Slide 35: How does all this fit together?
This is a good question. At this point it must seem like a series of strange, literally unreal, and unrelated subjects. However, while the numbers are not all real, the subjects are related. Note that unknown parts of the sinusoidal steady-state solution are the magnitude and the phase of the sinusoid. Also, a complex number can be thought of in terms of a magnitude and a phase. We will use the magnitude and phase of a complex number to get the magnitude and phase of the sinusoid in the solution we want.
We will develop a set of rules for doing this. We will lay out these rules and steps in the next lecture.

## Slide 36: How does all this fit together?
This is a good question. At this point it must seem like a series of strange, literally unreal, and unrelated subjects. However, while the numbers are not all real, the subjects are related. We will use the magnitude and phase of a complex number to get the magnitude and phase of the sinusoid in the solution in certain kinds of problems.
It doesn’t matter whether the method is real or not. The solution is real. Any method that gets us the correct solution quickly, is a good method. Woody Allen tells a joke about this.
We need the eggs.

## Slide 37: Joke: What are paradigms?
About 20 cents.
Get it? “Pair a dimes?” Okay, so it is not very funny…