## Slide 1: ECE 2202 Circuit Analysis
Dr. Dave Shattuck
Associate Professor, ECE Dept.
Lecture Set #8
Phasor Analysis
Version 13

## Slide 2: Lecture Set 8 AC Circuits – Phasor Analysis

## Slide 3: Overview AC Circuits – Phasor Analysis
In this part, we will cover the following topics:
Definition of Phasors
Circuit Elements in Phasor Domain
Phasor Analysis
Example Solution without Phasors
Example Solution with Phasors

## Slide 4: Textbook Coverage
This material is introduced in different ways in different textbooks. Approximately this same material is covered in your textbook in the following sections:
Electric Circuits 6th Edition by Nilsson and Riedel: Sections 9.3 through 9.5
Electric Circuits 10th Edition by Nilsson and Riedel: Sections 9.3 through 9.5

## Slide 5: Phasor Analysis
A phasor is a transformation of a sinusoidal voltage or current. Using phasors, and the techniques of phasor analysis, solving circuits with sinusoidal sources gets much easier.
Our goal is to show that phasors make analysis so much easier that it worth the trouble to understand the technique, and what it means.
We are going to define phasors, then show how the solution would work without phasors, and then with phasors.

## Slide 6: The Transform Solution Process
In a transform solution, we transform the problem into another form. Once transformed, the solution process is easier. The solution process uses complex numbers, but is otherwise straightforward. The solution obtained is a transformed solution, which must then be inverse transformed to get the answer. We will use a transform called the Phasor Transform.

## Slide 7: Definition of a Phasor – 1
A phasor is a complex number. In particular, a phasor is a complex number whose magnitude is the magnitude of a corresponding sinusoid, and whose phase is the phase of that corresponding sinusoid. There are a variety of notations for this process.

## Slide 8: Definition of a Phasor – 2
A phasor is a complex number whose magnitude is the magnitude of a corresponding sinusoid, and whose phase is the phase of that corresponding sinusoid.
In the notation below, the arrow is intended to indicate a transformation. Note that this is different from being equal. The time domain function is not equal to the phasor.
This is the time domain function. It is real. For us, this will be either a voltage or a current.
This arrow indicates transformation. It is not the same as an “=“ sign.
This is the phasor. It is a complex number, and so does not really exist. Here are two equivalent forms.

## Slide 9: Definition of a Phasor – 3
A phasor is a complex number. In particular, a phasor is a complex number whose magnitude is the magnitude of a corresponding sinusoid, and whose phase is the phase of that corresponding sinusoid. There are a variety of notations for this process.
This notation indicates that we are performing a phasor transformation on the time domain function x(t).
This is the phasor. It is a complex number, and so does not really exist. Here are two equivalent forms.

## Slide 10: Definition of a Phasor – 4
A phasor is a complex number. In particular, a phasor is a complex number whose magnitude is the magnitude of a corresponding sinusoid, and whose phase is the phase of that corresponding sinusoid. There are a variety of notations for this process.
This notation indicates, by using a boldface upper-case variable X, that we have the phasor transformation on the time domain function x(t). We will use an upper-case letter with a bar over it when we write it by hand. The phasor is a function of frequency, w.
This is the phasor. It is a complex number, and so does not really exist. Here are two equivalent forms.

## Slide 11: Definition of a Phasor – 5
A phasor is a complex number. In particular, a phasor is a complex number whose magnitude is the magnitude of a corresponding sinusoid, and whose phase is the phase of that corresponding sinusoid. There are a variety of notations for this process.
We will use an upper-case letter with a bar over it when we write it by hand. We will use an m as the subscript, or part of the subscript. We will drop this subscript when we introduce RMS phasors in the next chapter. The m indicates a magnitude-based phasor. This is required.

## Slide 12: Phasors – Things to Remember
All of these notations are intended, in part, to remind us of some key things to remember about phasors and the phasor transform.
A phasor is a complex number whose magnitude is the magnitude of a corresponding sinusoid, and whose phase is the phase of that corresponding sinusoid.
A phasor is complex, and does not exist. Voltages and currents are real, and do exist.
A voltage is not equal to its phasor. A current is not equal to its phasor.
A phasor is a function of frequency, w. A sinusoidal voltage or current is a function of time, t. The variable t does not appear in the phasor domain. The square root of –1, or j, does not appear in the time domain.
Phasor variables are given as upper-case boldface variables, with lowercase subscripts. For hand-drawn letters, a bar must be placed over the variable to indicate that it is a phasor. An m must be added to the subscript to show that we are using magnitude-based phasors.

## Slide 13: Circuit Elements in the Phasor Domain
We are going to transform entire circuits to the phasor domain, and then solve there. To do this, we must have transforms for all of the circuit elements.
The derivations of the transformations are not given here, but are explained in many textbooks.

## Slide 14: Phasor Transforms of Independent Sources
The phasor transform of an independent voltage source is an independent voltage source, with a value equal to the phasor of that voltage.
The phasor transform of an independent current source is an independent current source, with a value equal to the phasor of that current.

## Slide 15: Phasor Transforms of Dependent Voltage Sources
The phasor transform of a dependent voltage source is a dependent voltage source that depends on the phasor of that dependent source variable.

## Slide 16: Phasor Transforms of Dependent Current Sources
The phasor transform of a dependent current source is a dependent current source that depends on the phasor of that dependent source variable.

## Slide 17: Phasor Transforms of Passive Elements
The phasor transform of a passive element results in something we call an impedance. The impedance is the ratio of the phasor of the voltage to the phasor of the current for that passive element. The ratio of phasor voltage to phasor current will have units of resistance, since it is a ratio of voltage to current. We use the symbol Z for impedance. The impedance will behave like a resistance behaved in dc circuits. Thus, a impedance is defined by the equation

## Slide 18: Phasor Transforms of Passive Elements
The inverse of the impedance is called the admittance. The admittance is the ratio of the phasor of the current to the phasor of the voltage for that passive element. The ratio of phasor current to phasor voltage will have units of conductance, since it is a ratio of current to voltage. We use the symbol Y for admittance. The admittance will behave like a conductance behaved in dc circuits. We define admittance in the equation

## Slide 19: Terminology for Impedance and Admittance
The impedance and the admittance for a combination of elements will be complex. Thus, the impedance, or the admittance, can have a real part and an imaginary part. Alternatively, we can think of these values as having magnitude and phase. We have names for the real and imaginary parts. These names are shown below.
Admittance
Conductance
Susceptance
Impedance
Resistance
Reactance

## Slide 20: Phasor Transforms of Resistors
The phasor transform of a resistor is just a resistor. Remember that a resistor is a device with a constant ratio of voltage to current. If you take the ratio of the phasor of the voltage to the phasor of the current for a resistor, you get the resistance. The ratio of phasor voltage to phasor current is called impedance, with units of [Ohms], or [W], and using a symbol Z. The ratio of phasor current to phasor voltage is called admittance, with units of [Siemens], or [S], and using a symbol Y. For a resistor, the impedance and admittance are real, because the voltage and current are in phase.

## Slide 21: Phasor Transforms of Resistors
The ratio of phasor voltage to phasor current is called impedance, with units of [Ohms], or [W], and using a symbol Z. The ratio of phasor current to phasor voltage is called admittance, with units of [Siemens], or [S], and using a symbol Y. For a resistor, the impedance and admittance are real.
For this course, we will not use bars, or add m to the subscripts, for impedances or admittances. We will use only upper-case letters.

## Slide 22: Phasor Transforms of Inductors
The phasor transform of an inductor is an inductor with an impedance of jwL. In other words, the inductor has an impedance in the phasor domain which increases with frequency. This comes from taking the ratio of phasor voltage to phasor current for an inductor, and is a direct result of the inductor voltage being proportional to the derivative of the current. For an inductor, the impedance and admittance are purely imaginary. The impedance has a positive imaginary part, and the admittance has a negative imaginary part.

## Slide 23: Phasor Transforms of Capacitors
The phasor transform of a capacitor is a capacitor with an admittance of jwC. In other words, the capacitor has an admittance in the phasor domain which increases with frequency. This comes from taking the ratio of phasor current to phasor voltage for a capacitor, and is a direct result of the capacitive current being proportional to the derivative of the voltage. For a capacitor, the impedance and admittance are purely imaginary. The impedance has a negative imaginary part, and the admittance has a positive imaginary part.

## Slide 24: Table of Phasor Transforms
The phasor transforms can be summarized in the table given here. In general, voltages transform to phasors, currents to phasors, and passive elements to their impedances.
Component | Value | Transform
Voltages |  | 
Currents |  | 
Resistors |  | 
Inductors |  | 
Capacitors |  | 

## Slide 25: Phasor Transform Solution Process
So, to use the phasor transform method, we transform the problem, taking the phasors of all currents and voltages, and replacing passive elements with their impedances. We then solve for the phasor of the desired voltage or current, then inverse transform, using analysis as with dc circuits, but with complex arithmetic. When we inverse transform, the frequency, w, must be remembered, since it is not a part of the phasor solution.

## Slide 26: Sinusoidal Steady-State Solution
The steady-state solution is the part of the solution that does not die out with time.
Our goal with phasor transforms to is to get this steady-state part of the solution, and to do it as easily as we can. Note that the steady state solution, with sinusoidal sources, is sinusoidal with the same frequency as the source.
Thus, all we need to do is to find the amplitude and phase of the solution.

## Slide 27: Example Solution the Hard Way – 1
Let’s solve this circuit, but ignore the phasor analysis approach. We will only do this once, to show that we will never want to do it again.
If the source is sinusoidal, it must have the form,
This is a differential equation, first order, with constant coefficients, and a sinusoidal forcing function. We know from differential equations that the solution will have the form, a sinusoid with the same frequency as the forcing function.
Applying Kirchhoff’s Voltage Law around the loops we get the differential equation,
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?
Notes: If you do not remember enough of your differential equations course to derive this result, do not worry. The solution process is only given to show that we don’t want to do this again.

## Slide 28: Example Solution the Hard Way – 2
We know from differential equations that the solution will have the form of a sinusoid with the same frequency as the forcing function.
We can substitute this solution into the KVL equation,
and get,
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?
Notes: If you do not remember enough of your differential equations course to derive this result, do not worry. The solution process is only given to show that we don’t want to do this again.

## Slide 29: Example Solution the Hard Way – 3
Next, we take advantage of Euler’s relation, which is
This allows us to express our cosine functions as the real part of a complex exponential,
We do this, and get the first equation, in which we can expand the exponentials into two terms, and get the second equation,
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?

## Slide 30: Example Solution the Hard Way – 4
So, now we have,
So, now we can take the derivative and put it inside the Re statement. We can do the same thing with the constant coefficients. This gives us
Next, we note that if the real parts of a general expression are equal, the quantities themselves must be equal. So, we can write that
We can perform the derivative, and get

## Slide 31: Example Solution the Hard Way – 5
So, now we have,
So, now we recognize that
and divide by it on both sides of the equation to get
Next, we pull out the common terms on the right hand side of the equation,
Finally, we divide both sides by the expression in parentheses, which again cannot be zero, and we get

## Slide 32: Example Solution the Hard Way – 6
So, now we have,
This is the solution.
Now, this may seem hard to accept, so let us explain this carefully. We have assumed that we have the circuit given at right. Thus, it assumed that we know R and L. In addition, the vS(t) source is assumed to be known, so we know Vm, w and f. The natural logarithm base e is known, and therefore the only quantities that are unknown are Im and q.
Is this sufficient? Do we have everything we need to be able to solve?
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?
Notes: Think about your answer carefully before going to the next slide.

## Slide 33: Example Solution the Hard Way – 7
We have,
Is this sufficient? Do we have everything we need to be able to solve?
The answer is yes.
This is one complex equation in two real unknowns. Therefore, we can set the real parts equal, and the imaginary parts equal, and get two equations, with two unknowns, and solve. Alternatively, we can set the magnitudes equal, and the phases equal, and get two equations, with two unknowns, and solve.
So, this is the solution.
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?

## Slide 34: Example Solution the Easy Way – 1
Now, let’s try this same problem again, this time using the phasor analysis technique.
The first step is to transform the problem into the phasor domain.
Now, we replace the phasors with the complex numbers, and we get
where Im and q are the values we want.
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?

## Slide 35: Example Solution the Easy Way – 2
Now, we examine this circuit, combining the two impedances in series as we would resistances, we can write in one step,
where Im and q are the values we want. We can solve. This is the same solution that we got after about 20 steps, without using phasor analysis.
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?

## Slide 36: The Phasor Solution
Let’s compare the solution we got for this same circuit in the first part of this module. Using this solution,
let’s take the magnitude of each side. We get
and then take the phase of each side. We get
We get
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?

## Slide 37: The Sinusoidal Steady-State Solution
To get the answer, we take the inverse phasor transform, and get
This is the same solution that we had before.
Imagine the circuit here has a sinusoidal source. What is the steady state value for the current i(t)?

## Slide 38: Should I know how to solve these circuits without phasor analysis?
This is a good question. One could argue that knowing the fundamental differential equations techniques that phasor analysis depends on is a good thing.
We will not argue that here. We will assume for the purposes of these modules that knowing how to use the phasor analysis techniques for finding sinusoidal steady-state solutions is all we need.