## Slide 1: ECE 2202 Circuit Analysis II
Dr. Dave Shattuck
Associate Professor, ECE Dept.
Lecture Set #12
Complex Power
Version 18
Shattuck@uh.edu
(713) 743-4422

## Slide 2: Overview of Lecture Set Complex Power
In this lecture set, we will cover the following topics:
Definition of Complex Power
Usefulness of Complex Power
Notation and Units

## Slide 3: Textbook Coverage
This material is introduced in different ways in different textbooks. Approximately this same material is covered in the Nilsson and Riedel textbook in the following sections:
Electric Circuits 7th Edition by Nilsson and Riedel: Sections 10.4 through 10.5
Electric Circuits 10th Edition by Nilsson and Riedel: Sections 10.4 through 10.5

## Slide 4: Complex Power
We have defined real power and reactive power, and indicated why they might be important for efficient power distribution when we have sinusoidal voltages and currents.
Now we are going to show how they can be found more easily. We will find that:
A new concept called complex power can be defined in terms of complex numbers, as a function of the real power and reactive power.
Using phasor analysis makes it relatively simple to find this complex power.
This complex power tells us the real and reactive power, things that we want to know.
The power lines, which connect us from distant power generating systems, result in lost power. However, this lost power can be reduced by adjustments in the loads. This led to the use of the concept of reactive power.

## Slide 5: AC Circuit Analysis Using Transforms
Let’s remember first and foremost that the end goal is to find the solution to real problems. We will use the transform domain, and discuss quantities which are complex, but obtaining the real solution is the goal.

## Slide 6: Power with Sinusoidal Voltages and Currents
It is important to remember that nothing has really changed with respect to the power expressions that we are looking for. Power is still obtained by multiplying voltage and current.
The fact that the voltage and current are sine waves or cosine waves does not change this formula.

## Slide 7: Power as a Function of Time
We start with the equation for power as a function of time, when the voltage are current are sinusoids. We derived this in Lecture Set #9. We found that
The terms set off in red and blue above have meaning and are useful, and so we gave them names.

## Slide 8: Definition of Real Power
We define the term in red to be the Real Power. We use the capital letter P for this. Note that we have already shown that this is the average power as well.

## Slide 9: Definition of Reactive Power
We define the term in blue to be the Reactive Power. We use the capital letter Q for this.

## Slide 10: Definition of Complex Power
We define Complex Power to be the Real Power added to Reactive Power times j, which is the square root of minus one. Thus, complex power is a complex number. We use the capital letter S to refer to complex power. The real power is the real part of the complex power. The reactive power is the imaginary part of the complex power.

## Slide 11: Definition of Apparent Power
We define Apparent Power to be the magnitude of the Complex Power. Thus, apparent power is a real number. We use brackets around the capital letter, |S| to refer to apparent power. The apparent power is the magnitude of the complex power, and has the same units as complex power.

## Slide 12: Units for Complex Power
We use special units to keep all this straight. For Complex Power and Apparent Power we use the units [Volt-Amperes] or [VA]. For Real Power we use the units [Watts] or [W]. For Reactive Power we use the units [Volt-Amperes-Reactive] or [VAR]. It is important to use the correct units, so that we know what kind of power we are talking about.
Units are [W]
Units are [VAR]
Units are [VA]

## Slide 13: Meaning of Complex Power
The meaning of complex power is much less direct than the definitions of real power and reactive power. One way to look at it is that complex power is a way to obtain the real power and reactive power, quickly and efficiently, using phasors. We will explain how, next.

## Slide 14: The Usefulness of Complex Power – Part 1
We will show that it is relatively easy to obtain the complex power, if we use phasor analysis. Notice that we can substitute into our definition of complex power, using the formulas for real power and reactive power. We do this in the equations that follow. For this derivation, it is convenient to go back to our alternative notation, which we called the General Case, where the phase of the voltage is qv, and the phase of the current is qi.

## Slide 15: The Usefulness of Complex Power – Part 2
Using our result from the previous slide, we may recognize that this is in the form of Euler’s Relation. Euler’s Relation is given below to remind us of what it says. Thus, we can express complex power in terms of a complex exponential. We have the equations that follow.

## Slide 16: The Usefulness of Complex Power – Part 3
Now, we take this equation from the previous slide, and combine the terms for voltage together, and the terms for current together, and we recognize the result as the phasor transforms of the voltage and current (Vm(w) and Im(w)).

## Slide 17: The Usefulness of Complex Power – Part 4
Note that the phasor transform of the current I(w) would have a phase qi. Since the phase here is the negative of that, - qi, we don’t get the phasor transform, but rather the complex conjugate of the phasor transform, or I*(w).

## Slide 18: The Usefulness of Complex Power – Part 5
Thus, we reach the conclusion about complex power, which is shown below. We get the complex power by multiplying the phasor of the voltage times the complex conjugate of the phasor for the current. The real part of this is the Real Power, and the imaginary part of this is the reactive power.
If we use a different way of defining phasors, where the magnitude of the phasor is the RMS value of the sinusoid, instead of the zero-to-peak value, we then have

## Slide 19: The Usefulness of Complex Power – Part 6
This, then is the fundamental usefulness of complex power. We want to know P and Q. The real power, P, is the average power. The reactive power, Q, is a measure of the energy delivered to inductors or capacitors, and then returned. We can get these by taking the product of phasor voltage and the complex conjugate of the phasor current, using rms phasors. The real part of this product is P, and the imaginary part is Q.

## Slide 20: The Usefulness of Complex Power – Part 7
There is an approach, based on this, that can be used to find P and Q, which is even easier to use. Using the notation for impedance,
where R is called the resistance, and X is called the reactance, we can then say that

## Slide 21: The Usefulness of Complex Power – Part 8
Thus, to find P and Q, we can use
Note that we don’t need the phasor for the voltage, or even the phase of the phasor for the current. All we need is the magnitude of the phasor for the current, and the impedance, where

## Slide 22: Notation with RMS Phasors
The equations that follow,
use rms phasors. Here, we have added rms to the subscript. In our handwritten notation, we could also simply omit the m from the subscript. Thus, we can assume that if there is no m added to the subscript of a phasor, it is an rms phasor.

## Slide 23: Important Notes – 1
When we find P and Q, we need to be clear about what our answer means. In these derivations, we have assumed that we were using voltage and current in the passive sign relationship. However, this is not always true.
So, we need to return to our practice of having a two-part subscript for every power expression. This includes real power, reactive power, and complex power.

## Slide 24: Important Notes – 2
When we find P and Q, we need to be clear about what our answer means. So, our rules should be
Signs matter, as always. If we want to get power absorbed, as shown here, we will often use the passive sign relationship. If we use the active sign relationship, we need to include a minus sign.

## Slide 25: Important Notes – 3
When we find P and Q, we need to be clear about what our answer means.
Signs matter, as always. If we want to get power absorbed, as shown here, we will often use the passive sign relationship. If we use the active sign relationship, we need to include a minus sign.

## Slide 26: Important Notes – 4
There is a useful concept here. If you look at these equations, and compare them with the definitions for these quantities, we have
This means that the phase of the impedance of some load, is equal to the phase of the complex power for that load. The phase of the complex power for the load is called the power factor angle.

## Slide 27: Important Notes – 5
This is useful because for a load, we often want the reactive power to be zero. This corresponds to a zero power factor angle. Thus, the power factor angle is a useful quantity to measure and know, and it is equal to phase of the impedance of the load.
The phase of the impedance of a load is equal to the phase of the complex power for that load, and is called the power factor angle.

## Slide 28: Important Notes – 6
This is not as useful as the formulas for the current, so I suggest that you do not use this approach.
The complex power absorbed by a load can also be expressed in terms of the phasor voltage across that load.

## Slide 29: Sample Problem 1
Taken from Nilsson and Riedel, 8th Edition
Solutions:
Pabs.by.load = 975[W]
Qabs.by.load = 650[VAR]
Pabs.by.line = 25[W]
Qabs.by.line = 100[VAR]

## Slide 30: Sample Problem 2
Taken from Nilsson and Riedel, 8th Edition
Solutions:
Pabs.by.load = 1129[W]
Qabs.by.load = 753[VAR]
Pabs.by.line = 23.52[W]
Qabs.by.line = 94.09[VAR]

## Slide 31: Sample Problem 3
For the circuit shown below, assume that a capacitor with a reactance equal to XC is placed in parallel with the load. Find the value for that reactance that will give a combined load with a unity power factor. Using that reactance value, find the real and reactive power absorbed by the load, and the real and reactive power absorbed by the line.
Solutions:
XC = -84.5[W]
Pabs.by.load = 1066[W]
Qabs.by.load = 0
Pabs.by.line = 18.92[W]
Qabs.by.line = 75.68[VAR]

## Slide 32: Sample Problem 4
Taken from Nilsson and Riedel, 8th Edition, with some edits.
reactive power
reactive power
We do not show units for variables. So, we will remove these inappropriate units.

## Slide 33: Sample Problem 5
The circuit given below operates in steady-state.
We know that Load 1 absorbs 37[kW] and delivers 56[kVAR].
We know that Load 2 absorbs (43Ð-16°)[kVA].
We know that Load 3 absorbs 57[kW] at a lagging power factor of 0.47.
a) Find vA(t).
b) Find the impedance of Load 1.
Taken from Final Exam, Fall 2015, Problem 7
Solutions:
a)
b) (26.59 - 40.25j)[W]

## Slide 34: So what is the point of all this?
This is a good question. First, our premise is that since electric power is usually distributed as sinusoids, the issue of sinusoidal power is important.
Second, the quantities real and reactive power are important. Real power is the average power, and has direct meaning. Reactive power is a measure of the energy that is being stored temporarily. The sign tells us of the nature of the storage. Using these concepts, we can make changes which can improve the efficiency of the transmission of power.
Phasors make the calculation of real and reactive power straightforward. We use the new quantity “complex power” to tie it all together. The complex power gives us real and reactive power relatively easily.