## Slide 1: ECE 3355 Electronics
Lecture Notes
Set 7 – Version 25
BJT Amplifiers
Dr. Dave Shattuck
Dept. of ECE, Univ. of Houston

## Slide 2: Bipolar Junction Transistors
We will cover material from Chapter 7 from the 8th Edition of the Sedra and Smith text, starting from Section 7.2.2 on page 397.
We will take a somewhat different approach, mostly working from the transistor characteristic curves. While reading the book will be useful, you will only be responsible for the material covered in class.

## Slide 3: Overview of this Part Bipolar Junction Transistors (BJTs)
In this lecture set, we will cover the last topic from the list below:
The structure and terminology for BJTs
Transistor action
Transistor characteristic curves and notation standards
DC analysis of transistors, large signal models
AC analysis of transistors, small signal models

## Slide 4: Small Signal Equivalent Circuits for BJTs
When we say the transistor has been biased, it means that when we solve the dc problem (with signals set to zero) the transistor is in a desired region.
When the transistor is biased into the active, or linear, region, we can then solve the circuit again for the signal behavior. During this part, we set the dc sources to zero. We replace the transistor with an equivalent circuit, and then solve.

## Slide 5: Small Signal Equivalent Circuits for BJTs
When the transistor is biased into the active, or linear, region, we can then solve the circuit again for the signal behavior. We set the dc sources to zero. We replace the transistor with an equivalent circuit, and then solve. What equivalent circuit do we use? We will use a three-parameter equivalent circuit. We will try to see where this model comes from, by looking first at the output characteristic of the transistor.

## Slide 6: Small Signal Equivalent Circuits for BJTs
We will try to see where this model comes from, by looking first at the output characteristic of the transistor.
How would we model this kind of behavior?

## Slide 7: Small Signal Equivalent Circuits for BJTs
We will try to see where this model comes from, by looking first at the output characteristic of the transistor.
First, assume that the lines are horizontal, and equally spaced.

## Slide 8: Small Signal Equivalent Circuits for BJTs
If the lines are horizontal, and equally spaced, we would model with a current dependent current source.
We will try to see where this model comes from, by looking at the output characteristic of the transistor.

## Slide 9: Small Signal Equivalent Circuits for BJTs
However, these lines have a nonzero slope.
This slope reflects a linear increase in iC with increase in vCE. What would model a linear relationship between voltage and current?
We will try to see where this model comes from, by looking at the output characteristic of the transistor.

## Slide 10: Small Signal Equivalent Circuits for BJTs
What would model a linear relationship between voltage and current? A resistor. We add that resistor, to get the following model.
We will try to see where this model comes from, by looking at the output characteristic of the transistor.

## Slide 11: Small Signal Equivalent Circuits for BJTs
What would model a linear relationship between voltage and current? A resistor. We add that resistor, to get the following model.
The value of ro is the inverse of the slope of the lines in the characteristic curves.
We will try to see where this model comes from, by looking at the output characteristic of the transistor.

## Slide 12: Small Signal Equivalent Circuits for BJTs
We will try to see where this model comes from, by looking at the output characteristic of the transistor.
The value of ro is the inverse of the slope of the lines in the characteristic curves. The spacing of the lines comes from the current gain, b.

## Slide 13: Small Signal Equivalent Circuits for BJTs
This model works pretty well. But, we can make it more accurate still, by examining another characteristic curve. We plot iB as a function of vBE, which is called the input characteristic. We get something that looks like the following, essentially independent of other parameters:

## Slide 14: Small Signal Equivalent Circuits for BJTs
This model works pretty well. But, we can make it more accurate still, by examining another characteristic curve. We plot iB as a function of vBE, which is called the input characteristic. We get something that looks like the following, essentially independent of other parameters:
Here again, we can model the relationship in the active region with a straight line. What can we model this behavior with? Answer: With a resistor, of course.

## Slide 15: Small Signal Equivalent Circuits for BJTs
This model works pretty well. But, we can make it more accurate still, by examining another characteristic curve. We plot iB as a function of vBE, which is called the input characteristic. We get something that looks like the following, essentially independent of other parameters:
Here again, we can model the relationship in the active region with a straight line. It is a resistor connected between base and emitter, such that the base current will be proportional to the voltage base to emitter.

## Slide 16: Small Signal Equivalent Circuits for BJTs
Our standard transistor model for this course will be as follows:
The value of rπ is the inverse of the slope of the line in the input characteristic, evaluated at the dc bias point.

## Slide 17: Small Signal Equivalent Circuits for BJTs
Our standard transistor model for this course will be as follows:
The value of rπ is the inverse of the slope of the line in the input characteristic, evaluated at the dc bias point. We will use the relationship
rπ = VT / IB
where VT is the thermal voltage, which is about 25[mV] at room temperature.

## Slide 18: Small Signal Equivalent Circuits for BJTs
Our standard transistor model for this course will be as follows: The value of rπ is
rπ = VT / IB
where VT is the thermal voltage, which is about 25[mV] at room temperature. The value of ro is infinity, and b is given.

## Slide 19: Some Important Concepts
We will begin by solving the DC problem. This gives us IB, which we need to find rp.
Then, we solve by inserting the model below, if we are in the linear, or active, region.

## Slide 20: Some Important Concepts
We will begin by solving the DC problem. This gives us IB, which we need to find rp.
Then, we solve by inserting the model below, if we are in the linear, or active, region. The models for npn and pnp are shown below.
npn
pnp

## Slide 21: Some Important Concepts
We will begin by solving the DC problem.
Then, we solve by inserting the model below, if we are in the cutoff region.

## Slide 22: Some Important Concepts
We will begin by solving the DC problem.
Then, we solve by inserting the model below, if we are in the cutoff region. The models for npn and pnp are shown below.
npn
pnp

## Slide 23: Some Important Concepts
We will begin by solving the DC problem.
Then, we solve by inserting the model below, if we are in the saturation region.

## Slide 24: Some Important Concepts
We will begin by solving the DC problem.
Then, we solve by inserting the model below, if we are in the saturation region. The models for npn and pnp are shown below.
npn
pnp

## Slide 25: Some Important Concepts
When we say that we want to solve for a gain, or an input or output resistance, in the passband, we are talking about solving where the response |H(w)| is flat, versus w. That means that there are no capacitors or inductors. In turn, that means that all capacitors or inductors are either short circuits or open circuits.
The passband also means that the gain is maximum. So, the choice of whether the inductor or capacitor becomes a short circuit or open circuit, depends on which result maximizes the gain.

## Slide 26: Some Important Concepts
In the passband, we are talking about solving where the response |H(w)| is flat, versus w. The passband also means that the gain is maximum. The inductors or capacitors become a short circuit or open circuit, depends on which result maximizes the gain.
Magnitude Plot
Frequency (log scale)