## Slide 1
Prof. David R. Jackson
Dept. of ECE
Notes 2
ECE 5317-6351
Microwave Engineering
Fall 2019
Transmission Lines
Part 1: TL Theory
Adapted from notes by Prof. Jeffery T. Williams

## Slide 2
Transmission-Line Theory
We need transmission-line theory whenever the length of a line is significant compared to a wavelength.

## Slide 3
Transmission Line
2 conductors
4 per-unit-length parameters:
C = capacitance/length [F/m]
L = inductance/length [H/m]
R = resistance/length [/m]
G = conductance/length [ /m or S/m]

Dz

## Slide 4
Transmission Line (cont.)
+ + + + + + +
- - - - - - - - - -
x
x
x
B
Note: There are equal and opposite currents on the two conductors.
(We only need to work with the current on the top conductor, since we have chosen to put all of the series elements there.)
+
-
+
-

## Slide 5
Transmission Line (cont.)
+
-
+
-

## Slide 6
Hence
Now let Dz  0:
“Telegrapher’sEquations”
TEM Transmission Line (cont.)

## Slide 7
To combine these, take the derivative of the first one with respect to z:
Switch the order of the derivatives.
TEM Transmission Line (cont.)

## Slide 8
The same differential equation also holds for i.
Hence, we have:
TEM Transmission Line (cont.)
Note: There is no exact solution in the time domain, in the lossy case.

## Slide 9
TEM Transmission Line (cont.)
Time-Harmonic Waves:

## Slide 10
Note that
Then we can write:
TEM Transmission Line (cont.)

## Slide 11
Define
We have:
Solution:
Then
TEM Transmission Line (cont.)
 is called the “propagation constant”.
Question: Which sign of the square root is correct?

## Slide 12
Principal square root:
TEM Transmission Line (cont.)
We choose the principal square root.
Hence
(Note the square-root (“radical”) symbol here.)

## Slide 13
Denote:
TEM Transmission Line (cont.)

## Slide 14
TEM Transmission Line (cont.)
There are two possible locations for the complex square root:
Hence:
Re
Im
Re
Im
Re
Im
The principal square root must be in the first quadrant.

## Slide 15
TEM Transmission Line (cont.)
Wave traveling in +z direction:
Wave is attenuating as it propagates.
Wave traveling in -z direction:
Wave is attenuating as it propagates.

## Slide 16
TEM Transmission Line (cont.)
Attenuation in dB/m:

## Slide 17
Wavenumber Notation

## Slide 18
TEM Transmission Line (cont.)
Forward travelling wave (a wave traveling in the positive z direction):
The wave “repeats” when:
Hence:
“snapshot” of wave

## Slide 19
Phase Velocity
Let’s track the velocity of a fixed point on the wave (a point of constant phase), e.g., the crest of the wave.
(phase velocity)

## Slide 20
Phase Velocity (cont.)
Set
Hence
In expanded form:

## Slide 21
Characteristic Impedance Z0
so
Assumption: A wave is traveling in the positive z direction.
(Note: Z0 is a number, not a function of z.)

## Slide 22
Use first Telegrapher’s Equation:
so
Hence
Characteristic Impedance Z0 (cont.)
Recall:

## Slide 23
From this we have:
Use:
Characteristic Impedance Z0 (cont.)
Both are in the first quadrant
(principal square root)

## Slide 24
Hence, we have
Characteristic Impedance Z0 (cont.)

## Slide 25
In the time domain:
Wave in +z direction
Wave in -z direction
General Case (Waves in Both Directions)

## Slide 26
Backward-Traveling Wave
so
A wave is traveling in the negative z direction.
Note:
The reference directions for voltage and current are chosen the same as for the forward wave.
z

## Slide 27
General Case
A general superposition of forward and backward traveling waves:
Most general case:
z

## Slide 28
Guided wavelength:
Phase velocity:
Summary of Basic TL formulas

## Slide 29
Lossless Case
so
(independent of freq.)
(real and independent of freq.)

## Slide 30
Lossless Case (cont.)
If the medium between the two conductors is lossless and homogeneous (uniform) and is characterized by (, ), then (proof given later):
The speed of light in a dielectric medium is
Hence, we have that:
In the lossless case the phase velocity does not depend on the frequency, and it is always equal to the speed of light (in the material).
(proof given later)
and

## Slide 31
Where do we assign z = 0 ?
The usual choice is at the load.
Amplitude of voltage wave propagating in negative z direction at z = 0.
Amplitude of voltage wave propagating in positive z direction at z = 0.
Terminated Transmission Line
Terminating impedance (load)

## Slide 32
Terminated Transmission Line (cont.)
Hence
Can we use z = z0 as a reference plane?
Terminating impedance (load)

## Slide 33
Terminated Transmission Line (cont.)
Compare:
This is simply a change of reference plane, from z = 0 to z = z0.
Terminating impedance (load)

## Slide 34
What is V(-d) ?
Propagating forwards
Propagating backwards
Terminated Transmission Line (cont.)
d  distance away from load
The current at z = -d is then:
(This does not necessarily have to be the length of the entire line.)
Terminating impedance (load)

## Slide 35
Similarly,
L  load reflection coefficient
Terminated Transmission Line (cont.)
or
(-d) = reflection coefficient at z = -d

## Slide 36
Z(-d) = impedance seen “looking” towards load at z = -d.
Terminated Transmission Line (cont.)
Note:
If we are at the beginning of the line, we will call this the “input impedance”.

## Slide 37
At the load (d = 0):
Terminated Transmission Line (cont.)
At any point on the line(d > 0):

## Slide 38
Thus,
Terminated Transmission Line (cont.)
Recall

## Slide 39
Simplifying, we have:
Terminated Transmission Line (cont.)
Hence, we have

## Slide 40
Impedance is periodic with period g/2:
Terminated Lossless Transmission Line
Note:
The tan function repeats when
Lossless:

## Slide 41
Summary for Lossy Transmission Line

## Slide 42
Summary for Lossless Transmission Line

## Slide 43
No reflection from the load
Matched Load (ZL=Z0)

## Slide 44
Always imaginary!
Short-Circuit Load (ZL=0)
Lossless Case

## Slide 45
Note:
S.C. can become an O.C. with a g/4 transmission line.
Short-Circuit Load (ZL=0)
Inductive
Capacitive
Lossless Case

## Slide 46
Always imaginary!
Open-Circuit Load (ZL=)
or
Lossless Case

## Slide 47
O.C. can become a S.C. with a g/4 transmission line.
Open-Circuit Load (ZL=)
Note:
Inductive
Capacitive
Lossless Case

## Slide 48
Using Transmission Lines to Synthesize Loads
A microwave filter constructed from microstrip line.
This is very useful in microwave engineering.
We can obtain any reactance that we want from a short or open transmission line.

## Slide 49
Find the voltage at any point on the line.
At the input:
Voltage on a Transmission Line

## Slide 50
At z = -l :
Hence
Voltage on a Transmission Line (cont.)
Incident (forward) wave (not the same as the initial wave from the source!)

## Slide 51
Let’s derive an alternative form of the previous result.
Start with:
Voltage on a Transmission Line (cont.)

## Slide 52
where
Therefore, we have the following alternative form for the result:
Hence, we have
(source reflection coefficient)
Voltage on a Transmission Line (cont.)
Recall:
Substitute

## Slide 53
The “initial” voltage wave that would exist if there were no reflections from the load
(we have a semi-infinite transmission line or a matched load).
Voltage on a Transmission Line (cont.)
This term accounts for the multiple (infinite) bounces.

## Slide 54
Wave-bounce method (illustrated for z = -l ):
Voltage on a Transmission Line (cont.)
We add up all of the bouncing waves.

## Slide 55
Geometric series:
Group together alternating terms:
Voltage on a Transmission Line (cont.)

## Slide 56
or
This agrees with the previous result (setting z = -l ).
The wave-bounce method is a very tedious method – not recommended.
Hence
Voltage on a Transmission Line (cont.)

## Slide 57
At a distance d from the load:
If Z0  real (low-loss transmission line):
Time-Average Power Flow
Note:
P(z) = power flowing in + z direction
(please see the note)

## Slide 58
Low-loss line
Lossless line ( = 0)
Time-Average Power Flow (cont.)
Note:
For a very lossy line, the total power is not the difference of the two individual powers.

## Slide 59
Quarter-Wave Transformer
so
Hence
(This requires ZL to be real.)
Matching condition
Lossless line

## Slide 60
Match a 100  load to a 50  transmission line at a given frequency.
Lossless line
Quarter-Wave Transformer (cont.)
Example

## Slide 61
Voltage Standing Wave
Lossless Case
Note: The voltage repeats every g. The magnitude repeats every g /2.
Note: The voltage changes by a minus sign after g /2.

## Slide 62
Voltage Standing Wave Ratio

## Slide 63
At high frequency, discontinuity effects can become important.
Limitations of Transmission-Line Theory
Bend
Incident
Reflected
Transmitted
The simple TL model does not account for the bend.

## Slide 64
At high frequency, radiation effects can also become important.
When will radiation occur?
We want energy to travel from the generator to the load, without radiating.
Limitations of Transmission-Line Theory (cont.)
This is explored next.

## Slide 65
The coaxial cable is a perfectly shielded system – there is never any radiation at any frequency, as long as the metal thickness is large compared with a skin depth.
The fields are confined to the region between the two conductors.
Limitations of Transmission-Line Theory (cont.)
Coaxial Cable

## Slide 66
The twin lead is an open type of transmission line – the fields extend out to infinity.
The extended fields may cause interference with nearby objects.
(This may be improved by using “twisted pair”.)
Limitations of Transmission-Line Theory (cont.)
Having fields that extend to infinity is not the same thing as having radiation, however!

## Slide 67
The infinite twin lead will not radiate by itself, regardless of how far apart the lines are (this is true for any transmission line).
The incident and reflected waves represent an exact solution to Maxwell’s equations on the infinite line, at any frequency.
S
Limitations of Transmission-Line Theory (cont.)
Incident
Reflected
No attenuation on an infinite lossless line

## Slide 68
A discontinuity on the twin lead will cause radiation to occur.
Note:
Radiation effects usually increase as the frequency increases.
Limitations of Transmission-Line Theory (cont.)
Incident wave
Pipe
Obstacle
Reflected wave
Bend
Incident wave
Bend
Reflected wave

## Slide 69
To reduce radiation effects of the twin lead at discontinuities:
Reduce the separation distance h (keep h << ).
Twist the lines (twisted pair).
Limitations of Transmission-Line Theory (cont.)
CAT 5 cable
(twisted pair)