## Slide 1
Prof. David R. Jackson
Dept. of ECE
Notes 4
ECE 5317-6351
Microwave Engineering
Fall 2019
Transmission Lines
Part 3: Baluns
Adapted from notes by Prof. Jeffery T. Williams

## Slide 2
Baluns
Baluns are used to connect coaxial cables to twin leads.
4:1 impedance-transforming baluns, connecting 75  TV coax to 300  TV twin lead
Coaxial cable: an “unbalanced” transmission line
Twin lead: a “balanced” transmission line
Balun: “Balanced to “unbalanced”
https://en.wikipedia.org/wiki/Balun
They suppress the common mode currents on the transmission lines.

## Slide 3
Baluns (cont.)
https://en.wikipedia.org/wiki/Balun
“Baluns are present in radars, transmitters, satellites, in every telephone network, and probably in most wireless network modem/routers used in homes.”
Baluns are also used to connect coax (unbalanced line) to dipole antennas (balanced).

## Slide 4
Ground (zero volts)
+
-
Ground (zero volts)
+
0
The voltages are usually unbalanced with respect to ground.
The voltages are usually balanced with respect to ground.
Coax
Twin Lead
Baluns (cont.)
What does “balanced” and “unbalanced” mean?
Note:
If the coax outer conductor was not at zero volts, there would be a field between the coax and the ground. There would be charge and current on the outside of the coax.
This would correspond to a “common mode”.

## Slide 5
Baluns (cont.)
Baluns are necessary because, in practice, the two transmission lines are always both running over a ground plane.
If there were no ground plane, and you only had the two lines connected to each other, then a balun would not be necessary.
(But you would still want to have a matching network between the two lines if they have different characteristic impedances.)
Coax
Twin Lead
No ground plane

## Slide 6
Baluns (cont.)
When a ground plane is present, we really have three conductors, forming a multiconductor transmission line, and this system supports two different modes.
The differential and common modes are shown for a twin lead over ground.
For the common mode, both conductors of the transmission line act as one net conductor, while the ground plane acts as the other conductor (return path for the current).
Differential mode
(desired)
+
-
+
+
Common mode
(undesired)

## Slide 7
Baluns (cont.)
Ground
Differential mode: currents are equal and opposite
Ground
Common mode: a net current flows on the two conductors

## Slide 8
Baluns (cont.)
Differential mode
(desired)
Common mode
(undesired)
The differential and common modes are shown for a coax over ground.
+
-
+
-
(The red flux lines show the electric field.)

## Slide 9
Baluns for Coax to Twin Lead
Because of the asymmetry, a common mode current will get excited at the junction between the two lines, and propagate away from the junction.
Ground
Note:
If the height above the ground plane goes to infinity, the characteristic impedance of the common mode goes to infinity, and there is no common mode current – we would not need a balun.
Coax
Twin Lead
Common mode
Common mode
No Balun
Differential mode
Differential mode

## Slide 10
A balun prevents common modes from being excited at the junction between a coax and a twin lead.
Ground
Baluns for Coax to Twin Lead (cont.)
With Balun
Coax
Twin Lead
Differential mode
Differential mode
Balun

## Slide 11
From another point of view, a balun prevents currents from flowing on the outside of the coax.
Baluns for Coax to Twin Lead (cont.)
No Balun
Coax
Twin Lead
Ground
I1
I1
I2
I1
I2- I1
(current on outside of the coax)
Assume we have some amount of common mode.

## Slide 12
A simple model for the mode excitation at the junction
The coax is replaced by a solid tube with a voltage source at the end.
Solid tube
Twin Lead
Ground
+
-
Baluns for Coax to Twin Lead (cont.)

## Slide 13
Next, we use superposition.
+
Solid tube
Twin Lead
Ground
+
-
+
-
Differential mode
Solid tube
Twin Lead
Ground
+
-
+
-
Common mode
Baluns for Coax to Twin Lead (cont.)

## Slide 14
Baluns are also useful whenever one transmission line is grounded and the other one isn’t.
Baluns and Grounding
No Balun
Twin Lead
Ground
The twin lead is now forced to also be grounded.

## Slide 15
Baluns are also useful whenever one transmission line is grounded and the other one isn’t.
Baluns and Grounding (cont.)
The twin lead is now ungrounded (this is the usual case for twin lead).
With Balun
Coax
Twin Lead
Ground
Balun

## Slide 16
Baluns using Transformers
One type of balun uses an isolation transformer.
https://en.wikipedia.org/wiki/Balun
The input and output are isolated from each other, so the input can be grounded if desired (e.g., when using a coax feed for the primary) while the output is not (e.g., when using a twin lead feed for the secondary).
The common mode must be zero at the transformer, since a net current cannot flow off of the windings into the transformer core.
This balun uses a 4:1 autotransformer, having three taps on a single winding, on a ferrite rod.
The center tap on the input can be grounded if desired, while the balanced output is not. The common mode is choked off due to the high impedance of the coil.

## Slide 17
Here is a more exotic type of 4:1 impedance transforming balun.
This balun uses two 1:1 transformers to achieve symmetric
(and ungrounded) output voltages.
“Guanella balun”
Baluns using Transformers (cont.)
Balanced and ungrounded twin lead output
Unbalanced and grounded coax input

## Slide 18
Inside of 4:1 impedance transforming VHF/UHF balun for TV
Ferrite core
Baluns using Transformers (cont.)

## Slide 19
A 4:1 impedance transforming balun built using only coax
Balun using Coax
The two outputs are 180o out of phase.
(See slide 24 for a microstrip version.)
Unbalanced
Balanced

## Slide 20
Choke Baluns
Another type of balun uses a choke to “choke off” the common mode.
https://en.wikipedia.org/wiki/Balun
A coax is wound around a ferrite core. This creates a large inductance for the common mode, while it does not affect the differential mode (whose fields are confined inside the coax).

## Slide 21
Microstrip Line
Coax can be used to feed a microstrip line on a PCB without needing a balun.
Both the microstrip line (with ground plane) and the coax are two-conductor transmission line systems, so there is no common mode.

## Slide 22
Baluns and CPS Line
Baluns are very useful for feeding differential circuits with coax on PCBs.
No balun
Without a balun, there would be a common mode current on the coplanar strips (CPS) line.
CPS line

## Slide 23
=
+
Excites desired differential mode
Excites undesired common mode
Superposition allows us to see what the problem is.
+
-
+
-
+
-
+
-
-
+
Baluns and CPS Line (cont.)

## Slide 24
Baluns for CPS can be implemented in microstrip form.
Balun feeding a microstrip Yagi-Uda antenna
Tapered balun
Coax feed port
Paired-strip output
Baluns and CPS Line (cont.)
Coax feed port

## Slide 25
Baluns for CPS can be implemented in other microstrip forms.
Marchand balun
180o hybrid rat-race coupler used as a balun
Output (unbalanced)
Input #2 (balanced)
Input #1 (balanced)
Null output
Baluns and CPS Line (cont.)

## Slide 26
If you try to feed a dipole antenna directly with coax, there will be a common mode current on the coax.
No balun
Baluns for Antennas

## Slide 27
The equivalent circuit explains why there is a common mode on the coax.
No balun
Note:
The voltage source sees an asymmetric structure. The current flowing to the right has two possible paths.
+
-
Baluns for Antennas (cont.)

## Slide 28
Baluns are commonly used to feed dipole antennas from coax.
A balun first converts the coax to a twin lead, and then the twin lead feeds the dipole.
Baluns for Antennas (cont.)

## Slide 29
This acts like voltage source for the dipole, which forces the differential mode.
The dipole is loaded by a short-circuited section of “twin lead” (composed of the two hollow pipes). This is an open circuit at the source location because of the /4 height.
Baluns are commonly used to feed dipole antennas from coax.
Baluns for Antennas (cont.)
“Twin Arm Balun”

## Slide 30
Equivalent Circuit
Baluns for Antennas (cont.)
The equivalent circuit shows us that the current on the dipole arms are perfectly balanced.
+
-
Short
The voltage source sees the dipole in parallel with a short-circuited length of “twin lead” (made from the vertical pipes) of length 0 / 4.

## Slide 31
Another balun for feeding a dipole antenna from coax.
“Split Coax Balun”
Baluns for Antennas (cont.)
The operation here is very similar to the previous balun.
Both sides of the coax are split.

## Slide 32
A “sleeve balun” directly connects a coax to a dipole.
“Bazooka Balun”
Baluns for Antennas (cont.)
Another balun for feeding a dipole antenna from coax.
Coaxial “sleeve” region
The current on the inside and outside of the sleeve is forced to be zero at the top of the sleeve (open circuit). This makes it small everywhere on the outside.

## Slide 33
A balun is not always necessary when feeding an antenna.
Dipole antenna
Twin lead
Monopole antenna
Coax
Infinite ground plane
The system stays balanced – no common mode.
Current cannot flow on the outside of the coax.
Baluns for Antennas (cont.)

## Slide 34
Baluns and Measuring Probes
Baluns can be important when connecting to
unbalanced devices like oscilloscopes.
OSC
Coax input
Measuring probe
Wires
No Balun
There may be a strong common mode current on the two coax wires. The coax wires will act as an antenna! You may not really be measuring the field from the probe.

## Slide 35
Baluns can be important when connecting to
unbalanced devices like oscilloscopes.
No Balun
Now there is a common mode on the coax. The coax will act as an antenna! You may not really be measuring the field from the probe.
Baluns and Measuring Probes (cont.)
OSC
Coax input
Measuring probe
Coax

## Slide 36
Baluns can be important when connecting to
unbalanced devices like oscilloscopes.
With Balun
Now there is only a differential mode on the coax, and the coax acts as a transmission line. We measure what is coming from the probe.
Baluns and Measuring Probes (cont.)
OSC
Coax input
Measuring probe
Coax
Balun