ECE 6340

Fall 1998

# Class Project

INSTRUCTIONS: This project is due at 12:00 noon on Tuesday, Dec. 15. Please show all of your work and write neatly (you will be graded on the thoroughness and neatness of your write-up, and your results).

A unit-strength electric dipole is located at z = 0  inside a rectangular waveguide, of dimensions (a ( b). The dipole current is represented as

.

- Derive carefully a complete expression for the fields inside the waveguide, in the region  z > 0.

Assume a vertical (y-directed) dipole located at the center of the waveguide. Make a plot of the field  (along the centerline of the waveguide) versus , for a waveguide having dimensions a = 2.29 cm, b = 1.02 cm, at a frequency of  f = 10 GHz. Plot for .

# Text boxes

x

y

a

b