ECE 6340

# Fall 2001

### Project

## Instructions

This project is due in the instructor’s office by 5:00 p.m. on Thursday, Dec. 6. Please work individually on the project. You will be graded on the accuracy of your derivation and results, and on the neatness and quality of your write up and results. Please use “good” scales when you plot your results so that the plots are easy to read and look nice.

A microstrip line is shown below. The line extends to infinity in the ( z directions. A signal generator is attached at z = 0. The signal generator applies a voltage source that is

,

where  [s]. (Note that Vs (t) is not the same thing as the transmission line voltage V(t) at z = 0, but the transmission line voltage at  z = 0 can be easily found from the source voltage.)

Calculate the transmission line voltage V(t) at  z = 20 [cm], and make the following plots.

- Plot the characteristic impedance and the effective relative permittivity versus frequency from 0 to 100 GHz.

- Plot the conductor attenuation and the dielectric attenuation  versus frequency from 0 to 100 GHz.

- Plot the transmission line voltage V (t) at z = 20 [cm] versus time, and compare (on the same plot) with the transmission line output voltage when z = 0+ (an infinitesimal positive number).

- Plot the normalized transmission line output voltage (normalized so that the maximum 1.0). Compare (on the same plot) the source voltage .

- Repeat parts (3) and (4) assuming no dielectric or conductor losses.

## ILLUSTRATION OF MICROSTRIP GEOMETRY

DIMENSIONS:

(loss tangent of substrate)

h = 1.0 [mm]

W = 3.0 [mm]

t = 0.01 [mm]

( = 3.0 ( 107 [S/m]  (for metal)

APPROXIMATE DESIGN FORMULAS (valid for W/h > 1):

Note: these formulas assume that frequency is a positive number

where

#### For the conductor loss we have approximately

.

#### For the dielectric loss we have

where the “filling factor” q is

.

REFERENCES

B. C. Wadell, Transmission Line Design Handbook, Artech House, 1991 (pp. 93-98).

D. M. Pozar, Microwave Engineering, John Wiley, 1998 (pp. 162-163).

EXTENSION TO NEGATIVE FREQUENCY

In the inverse Fourier transform, . The integration  variable  goes from minus infinity to plus infinity. When  is negative, take the absolute value before calculating the attenuation constants  and . That is,

when .

When calculating the phase constant , use

when .

# Text boxes

TOP VIEW

END VIEW

x

z

W

h

W

-

+

t

t

SIDE VIEW

h

-

+

z

y