## Slide 1
Spring 2024
Notes 23
ECE 6345
Prof. David R. Jackson
ECE Dept.

## Slide 2: Overview
In this set of notes we apply the SDI method to investigate the fields produced by a patch current.
We calculate the field due to a rectangular patch on top of a substrate.
We examine the pole and branch point singularities in the complex plane.
We examine the path of integration in the complex plane.

## Slide 3: Patch Fields
Find Ex (x,y,0)
Note: The origin is at the center of the patch.

## Slide 4: Patch Fields (cont.)
From Notes 22 we have:
where
For the patch current, we have:

## Slide 5: Patch Fields (cont.)
From the TEN we have:
T denotes TM or TE
(TMz or TEz)
+
-
Note: For kz0 we choose a positive real number or a negative imaginary number:
(The branch choice for kz1 is arbitrary.)
(works for any kt)

## Slide 6: Patch Fields (cont.)
Define the denominator term as:
so that

## Slide 7
Patch Fields (cont.)
We then have:
The final form of the electric field at the interface is then:

## Slide 8
Polar Coordinates
Use the following change of variables:
Advantage of polar coordinates: The poles and branch points are located at a fixed position in the complex kt plane.
(kt is also often called k)

## Slide 9
Polar Coordinates (cont.)
Hence, we have:
This is in the following general form:

## Slide 10
Poles
Poles occur when either of the following conditions are satisfied:
TMz:

## Slide 11
Poles (cont.)
Hence, we have:
This equation coincides with the well-known Transverse Resonance Equation (TRE) in microwave engineering for determining the characteristic equation of a guided mode (e.g, TM0 SW mode).
(Kirchhoff’s laws)
This gives us:
+
-
TM0 SW:

## Slide 12
Poles (cont.)
Comparison:
TRE (surface-wave mode)
Poles in kt plane
(A similar comparison holds for the TE case.)

## Slide 13
Poles (cont.)
Hence, we have the conclusion that
That is, the poles are located at the wavenumbers of the guided modes (the surface-wave modes).
Note: In most practical substrate cases, there is only a single TM0 surface-wave mode.

## Slide 14
Poles (cont.)
The complex plane thus has poles on the real axis at the wavenumbers of the surface waves.

## Slide 15
Path of Integration
The path avoids the poles by going above them.
This rectangular path can be used for numerical computation.

Lossy case
Lossy case


## Slide 16
Lossless case

(typical choices)
Practical note:
If hR is too small, we are too close to the pole. If hR is too large, there is too much round-off error due to exponential growth in the sin and cos functions.
Path of Integration (cont.)
The path avoids the poles by going above them.

## Slide 17
changes
Branch Points
To explain why we have branch points, consider the TM function:
with
If
Note:
There are no branch cuts for kz1
(the function DTM is an even function of kz1).
(We need branch cuts for kz0.)

## Slide 18
Branch Points (cont.)
Note:
The representation of the square root of –1 as –j is arbitrary here.

## Slide 19
Branch Points (cont.)
Note:
The shape of the branch cuts is arbitrary, but vertical cuts are shown here.
Branch cuts are necessary to prevent the angles from changing by 2 :
Note:
The branch cuts should not cross the real axis when there is loss in the air and the branch points move off of the real axis (the integrand must be continuous).

## Slide 20
Branch Points (cont.)
We obtain the correct signs for kz0 if we choose the following branches:
The wave is then either decaying or outgoing in the air region when we are on the real axis.

## Slide 21
Branch Points (cont.)
The wavenumber kz0 is then uniquely defined everywhere in the complex plane:
Example

## Slide 22
Riemann Surface
The Riemann surface is a pair of complex planes, connected by “ramps” (where the branch cuts used to be).
The angles (and hence the function) change continuously over the surface.
All possible values of the function are found on the surface.

## Slide 23
Riemann Surface (cont.)
Riemann surface for z1/2
Top sheet
Bottom sheet
Top view
Note: A horizontal branch cut has been arbitrarily chosen.
A “ramp” or “escalator” now exists where the branch cut used to be.

## Slide 24
Riemann Surface (cont.)
Side view
Top view
Bottom
Top
3D view
Riemann surface for z1/2

## Slide 25
The Riemann surface can be constructed for the wavenumber function:
Top sheet
Bottom sheet
Example:
We go counter-clockwise around the branch point at k0 . We start on the top sheet on the real axis and end up back where we started but on the bottom sheet.
We track the point shown below (red dot).
Riemann Surface (cont.)

## Slide 26
Sommerfeld Branch Cuts
Sommerfeld branch cuts are a convenient choice for theoretical purposes (discussed more in ECE 6341 and ECE 6382):
on branch cut
(everywhere in complex plane)
This defines kz0 everywhere on the Riemann surface.

## Slide 27
Sommerfeld Branch Cuts (cont.)
Practical note:
If we give the air a small amount of loss, we can simply check to make sure that Im(kz0) < 0.
Note: The branch points move off of the axes for a lossy air.
(everywhere in complex plane)
kz0 is real here on the real axis, for a lossless air.
(The Sommerfeld branch cuts are the mapping of the negative real axis in the mapping below.)

## Slide 28
Sommerfeld Branch Cuts (cont.)
The Riemann surface with Sommerfeld branch cuts.
(top sheet)
(bottom sheet)
Note: Surface wave poles must lie on the top sheet, and leaky-wave poles must lie on the bottom sheet.

## Slide 29
Path of Integration
where
Top sheet
(bottom sheet)